## Slide 1: Beam Instrumentation On Fixed Target Experiments at CERN
S.Burger / T. Lefevre – CERN
NBI2022 12th International Workshop Neutrino Beams Instrumentation

## Slide 2: Outline
Fixed Target Facilities at CERN
Performance and Limitation of Beam Instrumentation
Examples of R&D activities
Conclusions

## Slide 3: Fixed-Targets at CERN
Fixed Target Facilities
CNGS – 500kW 2006-2012
Beam energy | Target Facility | Power / Energy

## Slide 4: Fixed-Targets (Beam Dumps) at CERN
Beam Dumps
2 main constraints for Beam Instrumentation design
Material issue  Power to handle with intercepting devices
Radiation level
SPS-300kW
LHC-560MJ

## Slide 5: Performance and Limitations of Beam Instrumentation
LHC and SPS dumps – beam dilution observation systems
LHC beam footprint
Beam sizes
6mm@450GeV
1.2mm@7TeV
Using a set of H-V kickers to dilute the beam power on the dump surface
SPS beam footprint

## Slide 6: Performance and Limitations of Beam Instrumentation
SPS Dump: Observation Screen
Screen underneath circulating beam
17m long optical line
Set of high-quality mirrors
F600mm focal length camera lens
Standard digital Camera inside Shielding
Al2O3:CrO2
1mm thick
S. Burger et al, ‘New CERN SPS Beam Dump Imaging System’, IBIC 2021
Circulating beam
Dumped beam
DUMP

## Slide 7: Performance and Limitations of Beam Instrumentation
SPS Dump: Camera Settings
The acquisition system is based on the decay time of the Chromox screen which can be quite long i.e. > few 100ms; saturation level depending on beam intensity, size and dilution strength
Multiple images (@35Hz) are stored as soon as a trigger event - from the extraction kicker system - is received.
The on-line SW performs the selection of the first non-saturated image.
S. Burger et al, ‘New CERN SPS Beam Dump Imaging System’, IBIC 2021

## Slide 8: Performance and Limitations of Beam Instrumentation
4x Beam position monitors, 1x Beam current transformer and 4x Screens

## Slide 9: Performance and Limitations of Beam Instrumentation
Noise / Perturbation on Electro-magnetic monitors
Beam position monitor - No target – BPM524 in front of the experimental stations
T. Lefevre, unpublished

## Slide 10: Performance and Limitations of Beam Instrumentation
Noise / Perturbation on Electro-magnetic monitors
Beam position monitors - With target
T. Lefevre, unpublished
First Observed in fall 2015 when testing high-Z targets affecting all BPMs
    Backscattered particles affecting the electronic
    Relocation of the electronic in a radiation safe zone in 2016
But still some perturbations observed on the beam position signal resulting in large fluctuations in the BPM readings (±mm)

## Slide 11: Performance and Limitations of Beam Instrumentation
Request for Target instrumentation
  Measuring beam position as close as possible from the target/experiment
   BPM using a screen for offset calibration
  Finally, screen based instrument design capable to withstand all beam intensities (288 x 1.2 1011 p+) and sizes (< 0.25x0.25 mm)

## Slide 12: Performance and Limitations of Beam Instrumentation
Originally in air  parasitical lights (Cherenkov, luminescence, etc…) that distorts the measurement  Blocking foil + put the screen in vacuum
Target IN
Backscattered particles disturbing the measurement (instantaneous process)
   Move camera outside of the area
Screen material for high intenstity / small beam size
  Glassy C HTW Germany (sigradur.com)
Sigradur G Glassy C
0.5mm
Al2O3:CrO2 0.5mm
Ti
0.1mm
SiC
0.5mm
Main points to solve for relying on screen instrument for HiRadMat

## Slide 13: Performance and Limitations of Beam Instrumentation
Relying on Screen for Target instrumentation
Thermal resistant OTR screen in primary vacuum
Photons
BEAM
Photons
>5m optical line to install the camera in a radiation-friendly location
288 bunches at 1.2e11ppb
σH = 0.26mm
σV = 0.28mm
Upgrade of the optical line may improve the accuracy
of the measurement by reducing the spherical aberrations

## Slide 14: Performance and Limitations of beam instrumentation
AD target instrumentation renovated in 2020
20m long optical line
Digital camera installed in safe area
F800mm
Al2O3:CrO2 screen degrading in air (oxydation?)
Chromox

## Slide 15: Performance and Limitations of beam instrumentation
Screen upgrade
OTR Glassy C screen
OTR Glassy C screen + blocking foil
We got signal thanks to:
Good initial alignment
& large OTR emission angle
But lot of background light + unexpected tail
Image seems totally cleaned-up !!
Need to verify the impact of the Forward OTR from the blocking foil
Beam

## Slide 16: R&D on Rad-tolerant Camera
Collaboration with MicroCameras & Space Exploration
Design initiated to develop a rad-tolerant camera
Full prototype ready in 2021
Using of the shelf qualified electronics components
www.microcameras.ch

## Slide 17: MC BeamCam Irradiation Test Preliminary Results
REF
36krad
3 campains of irradiation test done the last years
1x mixed field CERN CHARM facility in 2018
2x Co60 sources (Spain & CERN) in 2020 and 2021
  Reached TID of 36 Krad
CERN CHARM facility in 2022 (next week)
  Latest version of the electronics
  Aim of validating the SE immunity

## Slide 18: R&D on Optical lines using Machine Learning
Applying ML algorithms to beam imaging technology
Courtesy of G. Trad
An image will not be preserved at the exit of one fiber
Can it be recovered ?
Beam
Fibre output
ARTIFICIAL INTELLIGENCE-ASSISTED BEAM DISTRIBUTION IMAGING USING A SINGLE MULTIMODE FIBER AT CERN. G.TRAD (CERN) IPAC2022, Bangkok, Thailand

## Slide 19: R&D on Optical lines using Machine Learning
Simulations showed ML can work with few % accuracy
Lab. studies carried out using large core multimode optical fibre
Beam tests carried out at CLEAR@CERN
Courtesy of G. Trad
Fiber OUTPUT
Beam Image
Predicted Image
Typical beam image reconstruction for a model trained on real data
Encouraging first results with some improvements foreseen on training algorithms and experimental set-up

## Slide 20: Conclusions
Beam instrumentation for High Power Targets is very challenging
  need to cope with high radiation level
  need robust material for intercepting devices
At CERN, it is mainly based on optical methods (OTR imaging systems / Optical lines)
New projects under studies at CERN in the framework of the Physics Beyond Collider program (e.g. ShiP, Hiradmat 2) will require improved performances
R&D on radiation-tolerant camera and optical systems using ML on-going
R&D on screen using low density materials (Carbon Nano Tubes, Graphene, BNNT, etc…)

## Slide 21: Thanks for your attention A big thanks to all colleagues at CERN and elsewhere

## Slide 23: Performance and Limitations of beam instrumentation (1)
Experience from CNGS target beam instrumentation
  Stripline BPM
  Beam imaging systems using
    OTR screen (Optical Transition Radiation) : Carbon and Titanium material
    Rad-tolerant CMOS sensor : SYRA Camera (10Mrad)
BTV images
1012 protons 1013 protons
In-air BPM and BTV worked well during beam commissioning
Finally not used much during normal operation due to background leading to some unreliable readings
Some radiation effects on Camera at high intensities on the monitor installed close the target
Courtesy of R. Jones, T. Bogey, S. Burger and E. Bravin
Picture of stripline BPM in air in CNGS
Picture of the BTV in CNGS during mechanical calibration

## Slide 24: Performance and Limitations of beam instrumentation (3)
60cm ∅ screen installed at the end of a 900m long line ~ 30m upstream of the dump
Electronics located another 20m upstream the cameras in the tunnel behind an dedicated shielding made of iron
LHC Dump Observation Screen
Work very reliably since 2009 !
T. Lefevre et al, ‘A large scintillating screen for LHC dump line’, DIPAC 2007
Beam Splitter
Cam1
Cam2
Electronics behind iron shielding
30m
Shielding
900m
 DAQ
Al2O3:CrO2
3mm thick
4 quadrants

## Slide 25: Performance and Limitations of Beam Instrumentation
No target 1.72g/cm3 5.39g/cm3
Noise / Perturbation on Electro-magnetic monitors
BCT
Perturbations increasing with higher density targets
 BCT were moved upstream in the line
T. Levens, unpublished

## Slide 26: Performance and Limitations of beam instrumentation
Relying on Screen for Target instrumentation
OTR screens without Target downstream
Sigradur G Glassy C
0.5mm
Al2O3:CrO2 0.5mm
Ti
0.1mm
SiC
0.5mm
OTR screen alone
Filter OD 3.7
Strange and unexpected beam shape
OTR screen + Al foil in front
Filter OD 3
5x less light, but ‘normal’ shape

## Slide 27: Performance and Limitations of beam instrumentation
Relying on Screen for Target instrumentation
Sigradur G Glassy C
0.5mm
Al2O3:CrO2 0.5mm
Ti
0.1mm
SiC
0.5mm
Cherenkov emission
Energy threshold in air: 37.4GeV
Vacuum
Air
OTR screen
OTR Light
S. Burger et al, ‘Scintillation and OTR Screen Characterization with a 440 GeV/c Proton Beam in Air at the CERN HiRadMat Facility’, IBIC 2016
Beam

## Slide 28: Performance and Limitations of beam instrumentation
Relying on Screen for Target instrumentation
Sigradur G Glassy C
0.5mm
Al2O3:CrO2 0.5mm
Ti
0.1mm
SiC
0.5mm
R. Keiffer et al, ‘Experimental Observation of “Shadowing” in Optical Transition Radiation’’, PRL 120, 094802, 2018
Cherenkov emission
Energy threshold in air: 37.4GeV
Vacuum
Air
Beam
2nd screen
BW OTR
FW OTR
1st screen
BW OTR
Mitigation using a block foil

## Slide 29: Performance and Limitations of beam instrumentation
AD target instrumentation renovated in 2020
Target
Screen
Horn
Before
After
Courtesy of S. Burger

## Slide 30: R&D on Optical lines using Fibre Bundle
IPAC 19-24 May 2019 – Melbourne, Australia
https://doi.org/10.18429/JACoW-IPAC2019-WEPGW078
Joint ARIES-ADA Workshop on 'Scintillation Screens and Optical Technology for Transverse Profile Measurements
31 March – 3 April 2019 Krakow, Poland
https://indico.cern.ch/event/765975/contributions/3250516/
R2E annual meeting – 2018 11 December
https://indico.cern.ch/event/760345/timetable/
Motivation :
“Transport an image far away from the target to a location with low radiation level”
Courtesy of D.Celeste & Co

## Slide 31: R&D on Optical lines using Fibre Bundle
Tested rad-hard ‘FIGR-10 from Fujikura (10k fibres)
  Light transmission down by a factor 35
  Contrast down by a factor 3
  50% light reduction after 694kGy irradiation using 60Co source at CEA
Beam tests on PS extraction showed some crosstalk between fibres
Courtesy of D.Celeste & Co
Standard optics/camera system
Fiber bundle system
 Project currently stopped

## Slide 32
New fast wire scanners in PSB, PS and SPS rings
From graphene to Carbon Nano-Tubes
Test of CNT wires at Hiradmat@CERN in 2021
Wire
Strips
CNT
100 µm
~ 0,5 µm
~ 20 nm
CNTW multi-scale
‘Lower density material’ for more robust wire – Study on Carbon NanoTubes wires

## Slide 33: Fixed-target / Beam dumps beam parameters at CERN
Particle type | Protons / ions
Beam energy | 440 GeV/c
Beam intensity | 5 109 to 3.5 1013
Pulse length | 7.95us
Pulse period | 20s
Energy per pulse on Target | 2.4MJ
Beam size on Target (RMS) | 0.5 to 2mm
72 bunches
72 bunches
72 bunches
72 bunches
TT61
TNC
Potential to double the beam intensity using LIU beams in the future