## Slide 1: LBNF Radiation Safety Issues
S.D. Reitzner, N. Mokhov, I. Rakhno, I. Tropin, and K. Vaziri
NBI 2022
September 21, 2022

## Slide 2: Introduction
Beamline Overview
Radiation transport modeling parameters
Prompt radiation
Residual radiation
Ground water protection
Activated air release
Conclusion

## Slide 3: LBNF Beamline Components
Absorber Complex
(LBNF-30)
Target
Complex
(LBNF-20)
Primary Beam Service Building
(LBNF-5)
Decay Region
Primary
Beamline
Enclosure
Fermilab
Main Injector
Tunnel
Neutrino Beam
to SURF, SD

## Slide 4: Radiation Transport Modeling Parameters
Radiological safeguards designs based on 2.4 MW operation
120 GeV protons @ 1.5×1014 p / 1.2 s
56% duty factor
Model radiation transport using MARS
  2.2 m target for target hall calculations
  1.5 m target for decay pipe and absorber

## Slide 5: LBNF MARS Model
Target Station
Absorber Hall
Decay
Pipe
Target
Hall

## Slide 6: Prompt Dose
10 mrem/year from entire lab at site boundary.
  0.25 mrem/hr for rad worker
  50 μrem/hr for non rad workers
mrem/hr
166 mrem/hr
7 ft thick ceiling
5 ft thick walls
No access during operation.
Energy (GeV)
Neutrons/GeV/cm2/s

## Slide 7: Prompt Dose at Nitrogen Handling Room Level
mrem/hr
Nitrogen handling
room (NHR)
Pretarget
2.5 mrem/hr
No access in pretarget
or NHR during beam on
53 mrem/hr
Morgue
86 mrem/hr
Y = 0 m

## Slide 8: Prompt Dose at Battlement Level
y = 4.9 m
Work Cell
Power
Supply
Radioactivate
Water (RAW)
54 μrem/hr
Battlement
Borated
poly cover
mrem/hr
Access
Corridor
Rad worker access to
support rooms except RAW
N2 fill
Y = 4.9 m

## Slide 9: Residual Dose
mrem/hr
200 rem/hr max
t-blocks
<200 mrem/hr top
of shield pile
800 rem/hr max
cooling panels
230 mrem/hr
max top of steel
150 mrem/hr max
on concrete blocks
100-d irr/4-hr cooling

## Slide 10: Remote Handling and Storage
Work cell is designed for 4000 rad/hr on contact object.
2000 R/hr activity estimated for Horn B or Horn A and target
Work cell and morgue located in target hall.
Target hall will be shielded enough to handle unshielded moves.

## Slide 11: Ground Water Protection for Target Hall
Federal surface water limits:
  3H < 2600 pCi/mL
  22Na < 16 pCi/mL
Potential transmission to ground water via support piles.
  Shield to meet groundwater limit.
Groundwater limit below limit of detection
  3H <1 pCi/mL
  22Na <0.04 pCi/mL
Underdrain system to reduce buildup.
stars cm-3s-1

## Slide 12: Ground Water Protection Absorber Hall
Shield to meet groundwater limit.
Steel kern downstream to protect from muons
  170’ length
  10’ diameter
Barrier to prevent tritium diffusing from shielding into environment.
Monitoring wells to be used to detect any contamination.

## Slide 13: Air Activation
Air emission permit of 0.1 mrem/year annual sitewide release (EPA)
  LBNF annual release goal to be < 30 μrem/year to the public.
Nitrogen cooling for the target hall and decay pipe will maintain LBNF air releases within budget.
Maintain negative pressure in areas of activated air.

## Slide 14: Air Release Path

## Slide 15: Total Air Releases
Exit (Ci/yr) | 3H | 11C | 13N | 15O | 41Ar
Absorber Hall | 7.08×10-2 | 2.37×10-4 | 1.59×10-12 | 2.23×10-70 | 2.54
NHR | 1.03 | 1.41 | 1.32×10-4 | 5.09×10-31 | 1.36
Target Hall | 1.16 | 2.42×102 | 1.4×101 | 8.60×10-5 | 1.98
Morgue | 1.16 | 2.78×101 | 1.68×10-1 | 4.21×10-12 | 1.29
Primary Encl | 1.16 | 5.53 | 7.78×10-3 | 8.77×10-9 | 9.59×10-1
3H Source | Activity (Ci/yr)
Target Pile | 540
Decay Pipe | 152
Absorber Pile | 156
Tgt He Cooling | 0.015
Tritium from other sources
28.25% of
FNAL Site
Limit
Total release:
30.66% of
FNAL Site Limit
41Ar from RAW | 0.96 Ci/yr
0.49% FNAL Site Limit

## Slide 16: Wait Time Access Due to Activated Air
No access to area until air activity below 0.1 DAC after beam off.
DAC: Derived Air Concentration
DAC =
  Ci = concentration of ith isotope
  CRi = concentration of ith isotope which gives 5000 mrem effective dose from a 2000 hr exposure.
Location | Wait Time
Absorber Hall | 6 hrs
NHR | 45 min
Target Hall | 1.5 hrs
Primary Encl | 1.5 hrs

## Slide 17: Conclusion
Appropriate selection of shielding to maintain prompt dose below limits set by FNAL policy.
  Model for 120 GeV, 2.4 MW operation.
Shielding and underdrains will be used to maintain concentration of radioactive isotopes below regulatory limits for surface and ground water.
Morgue and work cell in target hall to allow for unshielded moves.
Use of nitrogen for cooling and long transit times in ventilation to maintain activated air releases below regulatory limit.