## Slide 1
NUMI Absorber Operation Experience and LBNF Absorber Mechanical Design
Abhishek Deshpande and Vladimir Sidorov
NBI 2022
September 19-22, 2022

## Slide 2: Overview
1. NUMI absorber operation experience
2. LBNF Absorber mechanical design
3. Absorber core
4. Absorber Core blocks
5. Absorber core modules assembly
8. Absorber Steel shielding
9. Hadron Alignment Detector System
10. HADES Retractive system
11. HADES and Core blocks Remote Handling
12. Energy deposition, temperatures, and stresses in the core
10. Absorber core cooling system
11. Steel shielding air cooling
12. Beam interlock hardware system
13. Absorber core thermocouple layout
14. Radiological protection
15. Core block prototyping and weld samples
16. LBNF Absorber Status.

## Slide 3
Water-cooled Aluminum core
Steel core
“Blue Block” steel shielding
Access door to Hadron Monitor
Concrete shielding
Absorbs the leftover hadronic and E.M. radiation at the end of the NuMI decay vessel. Protects surroundings from prompt and residual radiation. During normal operation, about 1/6 of beam power is deposited in the absorber
Aluminum core is assembled from 8 12” x 51” x51” blocks
Each block has two independent gun-drilled internal water loops, welded to aluminum piping extending out the back
NuMI Absorber operation experience
Steel core is assembled from 10 9.1” x 51” x51” blocks.Steel blocks have holes to let aluminum core cooling pipes through
18 year plot of temperature at shower max.
NuMI has 2 thermocouples
centered at shower max (block 3)
and 2 thermocouples centered on block 8.
(blocks 4,5,6 etc. not shown)
During 18 years of operation, NuMI has accumulated 3 MW-yr of integrated beam power. No known problems with absorber over that period.
In particular : No water leaks
All four thermocouples still working
Jim Hylen

## Slide 4: LBNF Absorber mechanical design
Absorber
Hall
Absorber
Service
Building
Hadron
Absorber
Decay Region
Helium Vessel
Surface
Hatch
Neutrino Beam
From Target Complex
Muon
Monitors
with
Shielding
Muon
Steel
Shielding
Neutrino Beam
to SURF, SD
Decay Region
Nitrogen
Cooling
Located directly downstream of the decay pipe –made up of actively cooled Aluminum and Steel blocks surrounded by concrete.
Provides radiation protection to people and keeps soil/groundwater activation levels to below allowable limits.
Designed for the worst case condition at 2.4 MW operation:
    Decay distance is 221m from MCZero9Target) to end of decay vessel.
    Helium filled decay pipe
    For a 1.5-m RAL style target, longer target options are less severe for the absorber
    Designed to sustain 2 successive beam accident pulses - interlock system limits the accent pulses to 1"

## Slide 5
The configuration of the Absorber is determined through an iterative process between the engineering design, radiological safety, MARS modeling, and the beamline groups.
Designed for the optimized beam condition (Dune-doc-294):
Energy deposition in the Absorber and radiological parameters are determined by MARS. They are a function of the type of Target used in the Target Hall.
Proton beam energy (Gev) | Protons per cycle | Cycle time (Sec) | Beam power (MW)
120 | 1.5E+14 | 1.2 | 2.4
MARS calculated distribution prompt
dose (mSv/hr) in the HA complex
LBNF Absorber mechanical design

## Slide 6
The mechanical design uses experience from NuMI and MiniBooNE design and operations.
The materials specified for different components of the Absorber have been used successfully at the lab previously.
Its two major components are the water-cooled core and the surrounding steel which is air-cooled. Following is the distribution of heat load for 2.4 MW and 1.5-m RAL target case:
Component | Heat load, kW | Reference
Aluminum spoiler and core | 228.7 | Dune-doc-17064
Absorber steel | 244.0 | Dune-doc-17064
Concrete shielding | 3.0 | Dune-doc-17064
Hadron Absorber hall | 41.00 | Dune-doc-17064
Muon Kern | 1.14 | Dune-doc-17064
Miscellaneous | 4.16 | Dune-doc-17064
Absorber Complex Total | 522 | 
LBNF Absorber mechanical design

## Slide 7
The absorber core includes: The Aluminum Spoiler, four Aluminum Masks and thirteen Aluminum blocks.
Five millimeters gap between two neighbor core blocks is made during installation.
Removable
Concrete
Shielding
Non- Removable Concrete Shielding
Steel
Shielding
Aluminum
Cores Blocks
HADES
Monitor
Decay Region
Helium Vessel
Decay Region
Nitrogen ‘Turn Around’ Box
Aluminum
Spoiler
Aluminum
Masks
Morgue
Removable
Concrete
Shielding
Absorber Core
Cores Blocks
Module
Neutrino Beam
Air box
Decay Vessel
Concrete shielding

## Slide 8: Absorber core blocks
Material: 6061-T6 Aluminum
Quantity: 1
Dimensions: 79”W X 77”H X 12”
Cooling lines: 4
Weight: 7150 lb
Material: 6061-T6 Aluminum
Quantity: 4
Dimensions: 77”-79”W X 77”H X 12”
Cooling lines: 2
Weight: 2800 lb
Material: 6061-T6 Aluminum
Quantity: 1
Dimensions: 77”W X 77”H X 12”
Material: 6061-T6 Aluminum
Quantity: 13
Dimensions: 67”-69”W X 67”H X 12”
Cooling lines: 4
Weight: 5180 lb
67”
Spoiler
Mask
Core Block
Air box
Absorber core is water cooled. All Aluminum blocks have gun-drilled cooling lines.
Air box is welded from aluminum channels covered with thin aluminum sheets

## Slide 9
The four water lines are drilled in the absorber aluminum core block and plugged by Al rods creating water loops. Three hole are drilled through the inlet and outlet ports for loops connection. Two elbows are welded to the block ports and connected to the manifold with pipes.
Loop
32”x32”
Elbow
Loop24”x24”
Plug
Aluminum Core Block
Supply Port
holes
Return Port
holes

## Slide 10
Water loops
1/16” disk
Elbow
Plug
Plug
The mask blocks are made from aluminum, dimensions 77”-79”Wx77”Hx12”.
The 67” diameter hole is covered with two thin 1/16”disks to keep the radioactive air inside the mask.
Two water loops holes are drilled in the mask block.
Mask Core Block

## Slide 11
Absorber core modules assembly
Four types of modules are installed in the absorber Air box, Spoiler, Mask, and Aluminum core block.
Mask module
Aluminum Core block module
Spoiler module
77”
77”-79”
67”-69”
67”
77”
79”
160.5-163”
160.4-175.25”
158.5”
77”
77”
159.25”
Air box module

## Slide 12
About 6 million pound of steel are used in the absorber shielding. The most of shielding is made from cheap 9.11 steel and blue blocks . The center module supporting structure is welded from 12” thick low carbon steel plates. Four removable T- blocks are installed in the downstream end of the absorber pile. They can be replaced with water cooled core blocks in the future if it will be required. There is 5mm gap between blue blocks and support structure weldment for the air travel.
Absorber steel shielding
Water
collecting pan
9.11”
Blue blocks
Module support
structure
Air
channels
T-block

## Slide 13
NUMI original 7x7 hadron monitor
Built by UT Austin
Modified HM 5x5 pixel array Installed in 2021
35.5”
901.7mm
LBNF proposed HM 13x13 array
2.75”
Hadron Alignment Detector System
The HADES design is based on technology used in NuMI. Hades is a segmented gas ionization chamber using helium, The HADES must be capable of measuring the angle of the primary proton beam to within 70mrad, the position of cross-hairs on horns B and C , the vertical and horizontal edges of bafflette and target, the vertical and horizontal edges of baffle and target with 0.5 mm accuracy.

## Slide 14
HADES Retractive system
Absorber
core
HADES Module
Steel
shielding
Concrete G-blocks
HADES Cable
penetration
HADES
Inside support block
The HADES is installed in the front of the absorber core blocks. The HADES Retractive system delivers the HADES to
the beam center line with tolerance +/- 0.5 mm for the beam parameters measurement.
The HADES is located inside of the Retractive system support block during the operation time .
HADES in measurement
position
HADES
Steel block
Concrete
bunker

## Slide 15
The HADES life has limit and in case of a failure it is replaced. The HADES Remote handling procedure is required.
Core blocks don’t have life limit and take beam during the project operation period . If the core leak occur during the operation, any core block module can be removed and stored in the morgue . The morgue is located in the concrete bunker beside the absorber steel shielding . Two section of the morgue can be occupied by four absorber core blocks with modules and middle section is storage of any broken hadron monitors.
HADES and Core blocks Remote Handling
Morgue
Morgue
Core block
module
HADES
module
HADES
G-blocks
Absorber
bunker

## Slide 16: Energy deposition, temperatures, and stresses in the core
The energy deposition in the Absorber strongly depends on the target design.
Several target designs have been considered, The current target is the 1.5-m RAL target.
Sergi Striganov

## Slide 17: Energy deposition, temperatures, and stresses in the core
The power deposited in individual Absorber components (kW):

## Slide 18: Summary of Result _ Rectangular Cooling Circuit (for the 1.5-m RAL Target _ 2.4 MW)
Material is Al 6061-T6. with the yield stress of 40 ksi.
The 13.6 ksi (mostly from the thermal loading) << 40 ksi.
 | Rectangular Cooling Circuit _ The Latest Design Dec 2020 |  |  |  |  | 
 | Maximum temperature ( C ) | FEA heat reaction (KW) | MARS data | Ratio | Stress (psi) | Total deflection (mm)
Spoiler | 57.58 | 27.05 | 27.32 | 99.01% | 11.3 | 1.3
Aluminum_1 | 59.21 | 28.547 | 29.27 | 97.53% | 13.6 | 0.969
Aluminum_2 | 70.651 | 31.688 | 32.18 | 98.47% | 12.01 | 0.946
Aluminum_3 | 69.121 | 28.092 | 28.67 | 97.98% | 9.97 | 0.953
1 cm bin in the center
Al Spoiler
Al block
Only Aluminum spoiler and Aluminum block are considered for the rectangular cooling circuit. No change for the steel block
Ang Lee

## Slide 19: 2nd aluminum block temperature, stress and deflection
Stress ~12 ksi <<40 ksi
Vertical deflection ~0.89 mm
Total deflection ~0.94 mm
Cooling circuit
Ang Lee

## Slide 20: Absorber core cooling: System layout
All piping parts and materials have been used without any failures on NuMI RAW systems since 2007.
304L SS flanged connections to 6061-T6 flanged connections exist in the NuMI Absorber hall. Worked well since 2007.
Piping layout in LBNF Absorber Hall
Valves removed after PDR recommendation to make design simpler
10” SS IPS RAW
Supply/return
RAW Manifold
2” Cooling
lines
Core block
module

## Slide 21: Absorber core cooling
Requirement of the system is to provide temperature regulated DI water to the core.
Maintain an average velocity of 5-7 ft/s ( 1.5-2.13m/c) in all the gun-drilled cooling channels in core components.
Parameter | Value | Units | Remarks
System volume | 1325 | Gal. | 5016L
System design temperature | 130 | F | 54.4C
System operation temperature | 80 | F | 26.7C
Maximum available working pressure | 75 | Psig | 517.1kPa
System operating pressure | 44 | Psig | 303.4kPa
System pump design horse power | 50 | Hp | 1 pump running, 1 stand by
System design flow | 1310 | Gpm | 4959 Lpm

## Slide 22
Air delivery
holes9”x48”
Air travels downwards at ~ 15 m/s through the 5 mm gaps
Enters air passageways at the bottom. Air channels connected to an exhaust duct. Air exhaust temperature ~ 44 0C
Exhaust duct
Steel shielding air cooling
An air cooling system, designed by CF, delivers 25,000 CFM of air which blows in on top of the absorber blocks and passes through the 5-mm gaps between the blocks. Collects in the air channels at the bottom and enters the return duct at the back of the Absorber.

## Slide 23: Steel shielding air cooling
Thermal/CFD analysis for the region with max EDEP was performed:
Total air flow for the air-cooling system: 25,000 CFM.
Steel temperature predictions for NuMI were ~158 0C. And the limit for the anti-rust paint is 260 0C.
Dune-doc-20831

## Slide 24: Beam interlock hardware system
Three independent systems provide redundancy to pull beam permit quickly in non-normal condition .
Jim Hylen

## Slide 25
Two thermocouple array installed in Al core block 2.
Permit is pulled on absolute temperature limits and also on comparison of temperatures before and after each pulse.
System designed to pull the beam permit after 1 accident pulse.
Ungrounded, 1/16”, J-type thermocouples used in NuMI will be specified. They have a 0.3 sec response to dT in surrounding material.
Beam interlock hardware system
Core block 2
Thermocouples array

## Slide 26
Absorber core thermocouple layout
Total of 224 thermocouples in bars slotted in front and back of block 2
TC tips
3.25”
3.25”
4”
Front array
8.255 cm
square grid
Both arrays
(back array
is offset
from font)
Within R<49 cm of center,
nowhere is further than
4 cm from a thermocouple
Thermocouple bar is 5/8” thick
Expect thermocouples to last lifetime of facility, but
each thermocouple bar is individually replaceable
without removing block from absorber

## Slide 27: Radiological protection
One of the requirements of the Absorber is to provide radiation protection to people in compliance with FRCM.
Residual dose rates in Beam OFF areas need to be less than 20 mrem/hr. Max is 10 mrem/hr as shown below.
Beam ON prompt dose rates in the Absorber service building do not exceed 5 x 10-5 mrem/hr.
Max: 10 mrem/hr
Igor Rakhno and Nikilai Mokhov

## Slide 28: Qualifying weld procedure for all types of welds
Sample coupons
Radiographs
2”pipe
Elbow
Core block
Weld
6 out of 6 pipe to block weld coupons passed ASME B31.3 Normal Fluid Service criteria.
Welds were done as per WPS: ED0017753-LBNF Absorber Aluminum Core Block Pipe to Block WPS.
6 out of 6 plug weld coupons passed ASME B31.3 Normal Fluid Service criteria. Welds were done as per WPS: ED0017773-LBNF Absorber Aluminum Core Block Plug Welds WPS.
Samples welding box

## Slide 29
LBNF Absorber Status
The preliminary design of the LBNF Absorber is completed.
The Final Design Review is scheduled in April 2023.

## Slide 30
Back up Slides

## Slide 31: LBNF-30 Absorber Complex
Absorber Complex
(LBNF-30)
Target
Complex
(LBNF-20)
Primary Beam Service Building
(LBNF-5)
Decay Region
Primary
Beamline
Enclosure
Fermilab
Main Injector
Tunnel
Proton Beam
From MI-10
Neutrino Beam
to SURF, SD
Extraction
Enclosure
Major
Vehicle
Access
Located directly downstream of the decay pipe –made up of actively cooled Aluminum and Steel blocks surrounded by concrete.
Provides radiation protection to people and keeps soil/groundwater activation levels to below allowable limits.
Designed for the worst case condition at 2.4 MW operation:
    Decay distance is 221m from MCZero9Target) to end of decay vessel.
    Helium filled decay pipe
    For a 1.5-m RAL style target, longer target options are less severe for the absorber
    Designed to sustain 2 successive beam accident pulses - interlock system limits the accent pulses to 1"
Introduction

## Slide 32: Absorber Complex – Support Rooms
Elevator Shaft
Absorber
Service
Building
Pump Room
Utility Shaft
RAW Room
Instrumentation
Room
Hadron
Absorber
Air Handling
Room
Mechanical
Room

## Slide 33
Spoiler
Loop24”x24”
Loop
41.5”x41.5”
The spoiler design is identical with the core block design, overall dimensions are larger 79”Wx77”H.

## Slide 34
The air box is designed to keep the radioactive air inside the absorber . The air box is located in the front of the absorber core blocks. Air box dimensions: 77”Wx77”Hx12”
Thickness-0.05”
Al channel

## Slide 35
Energy flux at absorber entrance
200 cm NuMItarget
21 GeV/POT
100 cm NuMI target
43 GeV/POT
150 cm RAL target
26 GeV/POT
220 cm RAL target
17 GeV/POT

## Slide 36: Spoiler temperature C stress and deflection
Stress 11.3 ksi <<40 ksi
Vertical deflection ~1.16 mm
Total deflection ~1.3 mm

## Slide 37: 1st aluminum block temperature, stress and deflection
Stress 13.6 ksi <<40 ksi
Vertical deflection ~0.89 mm
Total deflection ~0.968mm
Cooling circuit

## Slide 38: 3rd aluminum block temperature, stress and deflection
Stress ~9.7 ksi <<40 ksi
Vertical deflection ~0.85 mm
Total deflection ~0.95 mm
Beam direction
Beam direction +Z
Cooling circuit

## Slide 39: Scenario 4, variation, on-beam-axis accident including CFD
CFD was used to simulate temperatures in the aluminum block for the on-axis accident condition described in Dune-doc-7317.
120 GeV beam, 10 us spill, cycle time: 1.2 Sec, and total spills: 2.
Steady state energy deposition for block 1 and accident energy deposition for block 2 was used. Water temp: 25 0C. HTC~7000 W/m2-K.
End of first pulse. Max temp~116 0C
End of second pulse. Max temp~172 0C
Source: Abhishek Deshpande, DUNE DocDB: 9670
On-axis accident was also simulated.
dT for accident pulse (without target) matches off-axis case just shown.
However, the steady state
used here as a starting
point was from a different
target configuration, and
final temperatures would be
somewhat higher for current
target design.
None-the-less, do not expect
any significant damage from
2 on-axis accident pulses.

## Slide 40: Surrounding steel cooling
CFD simulations show the velocity profiles in the 5-mm gaps between Absorber components are uniform.
Sensitivity analysis to show that air velocity is adequate if the air gap sizes become non-uniform was also done.
The below analysis is for an older version of the steel shielding which used 9-11 steel components.
Dune-doc-431

## Slide 41
Side plates are welded to the penetrated into the concrete steel strips.
Weld
Steel
strip
The pan is welded from the 48”x120”x ¼” stainless steel base plates and side plates 24 “ height and 1/8” thickness. The final weld of the pan is made in the absorber hall.
Radioactive water collecting pan
286”
258”
234”

## Slide 42
NUMI Hadron Monitor
NUMI HM replacing fixture

## Slide 43: NUMI Hadron Monitor Installation

## Slide 44: Absorber core cooling system
AFT Fathom Therma/Fluid Model
3D Model of RAW Skid

## Slide 45: Absorber core cooling
Requirement of the system is to provide temperature regulated DI water to the core.
Maintain an average velocity of 5-7 ft/s in all the gun-drilled cooling channels in core components.
Minimum flow requirement for Absorber core components:
RAW pump Operating here: 1310 Gpm @ 83 Ft.

## Slide 46: Lower part of concrete blocks – temporal dependence of contact residual dose at hot spots
Temporal dependence of contact residual dose in a hot spot A 100-day irradiation and various cooling times Statistical uncertainty of the calculated dose is 15-20% |  | 
Cooling time | Fraction of the 100-d/4-hr dose (%) | Absolute value (mrem/hr)
4 hours | 100 | 150
3 days | 25 | 40
7 days | 15 | 23
Configuration with 8 BMCN blocks

## Slide 47
Jonathan Paley

## Slide 48
HADES Retractive system
Drive mechanism
Hadron
monitor
The HADES Retractive system delivers the HADES to the beam center line with tolerance +/- 0.5 mm for the beam parameters measurement. During the operation the HADES is located inside of the Retractive system support block.
Screw jack
HADES Module
Support
block
Moving
block
HADES

## Slide 49: Qualifying weld procedure for all types of welds
Welding procedure was qualified for both pipe and plug weld designs.
6 out of 6 pipe to block weld coupons passed ASME B31.3 Normal Fluid Service criteria. Welds were done as per WPS: ED0017753-LBNF Absorber Aluminum Core Block Pipe to Block WPS.
6 out of 6 plug weld coupons passed ASME B31.3 Normal Fluid Service criteria. Welds were done as per WPS: ED0017773-LBNF Absorber Aluminum Core Block Plug Welds WPS.