## Slide 1: CIEMAT and the IFMIF-DONES Irradiation Facility: Design Status and Near Future
J. Maestre (A. Ibarra) on behalf of CIEMAT and WPENS

## Slide 2: Outline
Introduction to the IFMIF-DONES Facility
The IFMIF-DONES Project Organization
Current design status of the Facility
CIEMAT contribution and other synergies
Planning and near future
1
2
3
4
5

## Slide 3: Outline
Introduction to the IFMIF-DONES Facility
1

## Slide 4: What is?
IFMIF-DONES
International
Fusion
IFMIF-DONES
Materials
Irradiation
Facility
Oriented
Neutron
Source
DEMO
IFMIF-DONES

## Slide 5: Why and Roadmap
ITER (800 m3)
ITER under construction in Cadarache (France). To demonstrate the scientific feasibility of fusion energy (500 MW of power from fusion energy with Q>10) no connected to the grid.
DEMO (~1000-3500 m3):
Being designed to operate continuously providing electricity to the grid (~2-4 GW), showing commercial nuclear fusion is technically feasible. Q>10, 2050
JET (80 m3)
JET started its operations in 1983. It was designed to study plasma behaviour in conditions close to those required for a fusion reactor. (16MW and Q<1 still)
MAGENETIC CONFINEMENT FUSION
1-3 dpa/lifetime
~20 dpa/year
Main challenge:
Materials capable of withstanding the thermal loads and irradiation effects that may occur on the chamber walls.
See https://www.euro-fusion.org/eurofusion/roadmap/
Engineering Standards

## Slide 6: IFMIF-DONES Facility
Accelerator-based fusion-like neutron source for
the qualification of the materials oriented to DEMO
Neutron spectrum up to 55 MeV energy
High Flux Test Module:
20 dpa/fpy in 100 cm3 of material

## Slide 7: Site
Granada (Escúzar)
Thanks to CIEMAT: Leadership of the Spanish proposal to host the facility in Granada including all the related preparatory work

## Slide 8: Outline
The IFMIF-DONES Project Organization
2

## Slide 9: Framework
In the last 15 years, key projects are:
IFMIF/EVEDA (included in the BA – 2007 on going ),
WPENS –including specific Industry contract- (EUROfusion WP – 2015 on going)
DONES-PreP (EURATOM CSA – 2019 up to 2021)
DONES-PRIME and DONES-UGR (Spanish funded projects – 2020 up to 2023 on going).
Completed Dec 2021
DONES-PRIME
DONES-UGR
Notes: DONES-PreP:
- Propose a legal, governance and management framework for the Project
- Propose a financial framework for the Project
- Prepare the required specific Licensing and Permitting
Prepare for the use of Structural Funds
Evaluate possible technical alternatives of strategic interest (For all the possible users)
DONES PRIME-UGR: Local support to the project and first administrative and lab buildings.

## Slide 10: System Organization
Project is organized based on a PBS (Plant Breakdown Structure)
“In Kind” contribution
Research Units: 17
Project Management manager + Tech Advisor
Project Leader
System responsible
Coordinators
Research Units

## Slide 11: Outline
Current design status of the Facility
3

## Slide 12: Overview of the Facility

## Slide 13: Main Building
Accelerator System
Test System
Lithium System

## Slide 14: Accelerator System
A very challenging design due to the high 125 mA beam current (5 MW beam power)
Validation results from LIPAc (Rokkasho) as part of IFMIF/EVEDA activities
LIPAC
(in 2019 a world-record has been obtained by accelerating a 125 mA deuteron beam up to 5 MeV, in pulsed mode, with high efficiency)
Notes: To add information of the Accelerator:
To add comments from LIPAC: LIPAc installation and commissioning has been done in several phases. Presently the full accelerator except the SRF Linac has been installed and it is operating. It has been commissioned with pulsed deuteron beams up to 125 mA current accelerated up to 5 MeV.
RFQ conditioning needs to be completed reaching full power and it has been tested with pulsed beams with 0.1% duty cycle. Same happen with MEBT.

## Slide 15: Lithium System
Target System
Impurity Control System
Heat Removal System
Function:
Provide a continuous Li jet whose interaction with D+ beam generates the Neutron flux
Main parameters:
Li inventory ~12 m3
Li flow rate ~100 l/s
Li jet at 15 m/s (25 mm thickness)
Li working temperature (cold side) ~300 °C

## Slide 16: Lithium System
Challenges:
Hydro-dynamic stability of the of Li
Management of radioactive impurities in the Li flow
High corrosivity and reactivity of the Li system
Fire-protection system and Lithium recovery system
Target System exposed to extreme conditions: ~20 dpa/fpy; Thermo-mechanical loads
Function:
Provide a continuous Li jet whose interaction with D+ beam generates the Neutron flux
Main parameters:
Li inventory ~12 m3
Li flow rate ~100 l/s
Li jet at 15 m/s
Li working temperature (cold side) ~300 °C
Back Plate
Inlet Nozzle
Beam

## Slide 17: Lithium System
ELTL validation results from IFMIF/EVEDA phase implemented in the design
Lithium loop at scale 1:3
Fluid-Dynamic stability of the Li jet.
Stable and continuos operation of the Li
Pictures of a lithium flow in ELTL taken with 2 s and 10 µs exposure time [Kondo et al. (2015), Wakai et al. (2016)]
ELTL Facility (Japan)

## Slide 18: Lythium System
Heat Removal System
Update of Li loop design considering the new operating temperature (300°C),
RH requirements and building modifications.
Update of EMP and Dump Tank
Purification system
Consolidated design of impurities Traps
Getter qualification
Corrosion tests on Eurofer and 316L (Lifus-6 facility)
Development of monitoring impurity equipment
Target System
Coupled fluid-structure thermal- mechanical analysis (and accidental scenarios)
Final design, procurement and testing of the quick disconnecting systems (QDS) on beam ducts
Li jet diagnostics
Ancillaries system
Update design of the ancillary systems (gas, heating, power and vacuum) due to the new operating condition
Courtesy of G. Bongiovi
Courtesy of D. herranz
Chromatic
confocal
Courtesy of B. Brenneis
Courtesy of L. Buldings
Courtesy of P. Fabuzza

## Slide 19: Test System
Main Objetive:
Allocating the stripping reaction Li-D and the module of irradiations (HFTM)
To irradiate large volum of SSTT samples (>800 samples)
Characterization of Neutron and gamma field (STUMM)
1st Confinement barrier
Challenges:
Harsh environment (several MGy/h)
Strict Safety Requirements (Fire prevention and massive Li spillage)
Strict thermo-mechanical stability of all the assembly
Radiation map
uSv/h
Courtesy of Y. Qiu

## Slide 20: Irradiation modules
HFTM
Specimen capsule (Eurofer)
F. Arbeiter (KIT)
SSTT
Controlled temperature by low pressure helium gas
Lifetime: 1year / 2.5 years (53 dpa). Body made from 316LN (acc. RCC-MRx)
Masses: Total 680 kg, 40 kg irradiation capsules with specimens
MATERIALS
Steel irradiation (conditions matched to DEMO FW)
  12–25 dpa/fpy in 306 cm³ (~ 850 specimens)
  13 appm He / dpa, 53 appm H / dpa.
  250 – 550 °C, sodium immersed specimens
Copper irradiation (divertor heat sink)
  5–30 dpa/fpy (same capsules as for steel)
Tungsten irradiation (armor)
Courtesy of Y. Qiu
Dpa/fpy on Stainless Steel capsules
The up-to-date design activities of IFMIF-DONES have so far developed the so called High Flux Test Module (HFTM), as the first-to-be-installed irradiation experiment (critical path for Breeding Blanket of DEMO).

## Slide 21: Irradiation modules
Capsule: specimen stack
Tensile: 30 (min 12)
Fracture toughness: 14 (min 12)
Fracture crack growth: 6 (min 4)
Impact: 10 (min 8)
Fatigue: 9 (min 8)
Specimens
Total: 69 SSTT
Sesors:
Thermocouples
SPNDs
Courtesy of M. Serrano and R. Hernández
MATERIALS
Steel irradiation (conditions matched to DEMO FW)
  12–25 dpa/fpy in 306 cm³ (~ 850 specimens)
  13 appm He / dpa, 53 appm H / dpa.
  250 – 550 °C, sodium immersed specimens
Copper irradiation (divertor heat sink)
  5–30 dpa/fpy (same capsules as for steel)
Tungsten irradiation (armor)
The up-to-date design activities of IFMIF-DONES have so far developed the so called High Flux Test Module (HFTM), as the first-to-be-installed irradiation experiment (critical path for Breeding Blanket of DEMO).
SSTT Samples (sub-size specimens)
Tensile test
Impact test
Fracture toughness
Fatigue & Fatigue crack growth
Towards Standarization
Beyond the limits
Courtesy of M. Serrano and R. Hernández

## Slide 22: Outline
CIEMAT contribution
4

## Slide 23: CIEMAT Contribution
RF coupler Test Bench
CIEMAT HPRF lab.
Scraper
Beam Dump
Leadership
Project leader (WPENS)
DONES Integration manager
DONES-PreP - European ESFRI Roadmap
Safety & Licencing coordination
Accelerator System
Engineering design of IFMIF-DONES: - Beam dynamics & diagnostics - Beam intercepting devices
- MEBT
- RF System - Etc.
LIPAC from design to commissioning: RF System; MEBT; HEBT; Beam Dump; Diagnostics, superconducting solenoids, etc.

## Slide 24: CIEMAT Contribution
CIEMAT Liquid Metal Lab
Hydrogen Sensor
H-Trap Test Bench
Leadership
Project leader (WPENS)
DONES Integration manager
DONES-PreP - European ESFRI Roadmap
Safety & Licencing coordination
Accelerator System
Engineering design of IFMIF-DONES: - Beam dynamics & diagnostics - Beam intercepting devices
- MEBT
- RF System - Etc.
LIPAC from design to commissioning: RF System; MEBT; HEBT; Beam Dump; Diagnostics, superconducting solenoids, etc.
Lithium System
Liquid Lithium purification tech. (LITEC)
Others: jet diagnostics, Impurity monitoring systems, etc.

## Slide 25: CIEMAT Contribution
Valeria Lab: DONES virtual simulation
SSTT sample design
Leadership
Project leader (WPENS)
DONES Integration manager
DONES-PreP - European ESFRI Roadmap
Safety & Licencing coordination
Accelerator System
Engineering design of IFMIF-DONES: - Beam dynamics & diagnostics - Beam intercepting devices
- MEBT
- RF System - Etc.
LIPAC from design to commissioning: RF System; MEBT; HEBT; Beam Dump; Diagnostics, superconducting solenoids, etc.
Lithium System
Liquid Lithium purification tech. (LITEC)
Others: jet diagnostics, Impurity monitoring systems, etc.
Test System
DONES Coordinator
Material Qualification: SSTT samples
Transversal activities
RH, Maintenance and Logistics
Safety & neutronics analysis
Control System

## Slide 26: Outline
Planning and near future
5

## Slide 27: NEAR FUTURE
IFMIF-EVEDA
IFMIF-DONES
Reference Design
2007
2014-16
2021
Consorcio IFMIF-DONES
2022
FIRST LABORATORIES AND ADMINISTRAVE BUILDINGS
+10 AÑOS
COMMISIONING
+20-30 AÑOS
FACILITY OPERATION
EU site agreement: Granada
2017

## Slide 28: First building DONES-PRIME
Under construction

## Slide 29: IFIMIF-DONES
Thanks for your attention

## Slide 30: Material Qualification
1. Fission irradiations
Intensive and broad use of Material Test Reactors (MTR) fission irradiation: EU plans for 50 M€ in the next decade.
Issue:
Number of MTR with reasonable n-fluence and volume is becoming limited!
Limited reproducibility of He-effects on degradation of properties
2. Fusion-like irradiations
Mandatory: a dedicated facility for material qualification that best reproduces a 14 MeV neutrons spectrum with reasonable irradiation volume, fluence, and homogeneity with the objective to validate in-vessel materials
3. Also needed: develop “quasi-standards” of Small Specimen Test Technique (SSTT) towards accepted standards and norms
DESIGN CODES
Neutron-induced damage

## Slide 31: Current desing status
Start-Up Monitoring Module (STUMM) prototype to validate the final design and diagnostics,
Quick Disconnecting System (QDS). To validate RH connection system
Multipurpose VaCuum accidental scenarios (MuVaCas). To analyse different possible accidental scenarios related with Vacuum
SRF LINAC High Beta cavity prototyping to validate the final design
Electromagnetic Pump prototype
Li purification prototype loop (LITEC) to test impurities control technology
LIFIRE facility to study Lithium fire risks
ANGEL facility to evaluate Nitrogen trap performance
Valeria lab for virtual reality maintenance and RH modelling
Be in Lithium loop for evaluation of Be behaviour in Lithium
….
PLANT DESCRIPTION DOCUMENT
Engineering desing report
Safety Analysis Report 2021

## Slide 32: Test System
Test Cell
Optimization and consolidation of the design of Test Cell Removable Shielding Blocks (Maintainability and minimizing neutron streaming)
Experimental activities focused on the thermal behaviour of the TC shielding
HFTM
Irradiation campaign of critical components as the capsule heaters at Maria reactor
Integration design
STUMM
Full-scaled prototype of the STUMM (to be finished by end 2023)
Prototype of the Rabbit System with the purpose of testing its mechanical reliability
TS Ancillaries
Specific Contract (industrial) aiming at reaching a definition design status
Courtesy of A. Talarowska
Courtesy of T. Dezsi
Courtesy of F. Albeiter

## Slide 33: Irradiation parameter