## Slide 1: Electron Sources and Injectors. Lecture V
Dr. Boris Militsyn
STFC Accelerator Science and Technology Centre (ASTeC)
Notes: To add overall slide about electron source applicability

## Slide 2: Beam Dynamics in the Electron sources
Beam dynamics in DC guns
  Acceleration
  Beam focusing
  Emission in the magnetic field
  Space charge effects
  Emittance compensation
Beam dynamics in the RF guns
  Transverse beam dynamics

## Slide 3: Typical thermionic DC gun based electron injector
Cathode
Anode
Focusing solenoid
Booster accelerator
0
Buncher
Chopper-
collimator

## Slide 4: Photocthode DC gun based electron injector
Cathode
Anode
Focusing solenoid
Booster accelerator
0
Buncher

## Slide 5: Photocathode RF gun based electron injector
Cathode
Focusing solenoid
Booster accelerator
RF cavity

## Slide 6: Space charge effects. Longitudinal effects I
Longitudinal space charge effects:
Short beam . In the beam rest frame
That gives for and
  The beam field is not small and should be taken into account at beam dynamics analysis
  Beam field leads to repulsion of the particles and to lengthening of the bunch
  It leads to acceleration of the bunch head and deceleration of the bunch tail
  In order to accelerate such a beam a gun with a field of higher than is required

## Slide 7: “Cigar” emission
Photocathode
For a DC gun
          * - D. Filippetto et al., Phys. Rev. ST Accel. Beams 17, 024201 (2014)
Notes: This formula does not take into account beam lengthening during propagation from cathode to the exit of the gun

## Slide 8: Acceleration in uniform DC electric field I
Right after emission from the cathode the beam has an energy equal to it’s intrinsic energy which is about 1 eV so relativistic factor:
At the exit of the gun beam energy varies from 10’s keV to 100’s keV so for example for 100 kV gun
We can not ignore relativistic effects

## Slide 9: Acceleration in uniform DC electric field II. Longitudinal motion
Typical field in DC gun varies from 1 MV/m to 10 MV/m
In single particle approximation:
Let’s ignore for a moment influence of the magnetic field:

## Slide 10: Acceleration in uniform DC electric field III. Transverse motion
For radial motion

## Slide 11: Acceleration in a 350 kV DC gun as calculated with GPT
Longitudinal electric field
Total beam energy
Longitudinal electron velocity
Transverse electron velocity

## Slide 12: Acceleration in a DC gun. Beam defocusing.
At the exit of the gun there electric field ends the beam is defocused by the electrostatic anode lens:
At a beam with kinetic energy and a gun field and in the open space the focusing distance
At the presence of space charge beam energy is not uniform along the bunch so focusing of the beam is slightly different for the head and the tail of the bunch that immediately leads to increase of transverse emittance

## Slide 13: Acceleration in a DC gun. Beam focusing I
To compensate this defocusing a solenoidal magnetic lens is used. The focusing distance of the solenoidal lens is defined as
The magnetic solenoid lens is always focusing independently of sign of the particle charge and magnetic field
The solenoidal lens is frequently characterised by its effective length:
where is peak field in the lens

## Slide 14: Acceleration in a DC gun. Beam focusing II
To create a lens with focusing distance to compensate defocusing effect of anode lens in the 100 kV gun we need a lens with integral
That gives for a peak field of or
Practically a stronger focusing solenoid is required to provide beam transport through the buncher or for injection into the booster
Focusing distance of the electrostatic lens at anode diaphragm scales as, magnet solenoid as
It may be difficult to compensate chromaticity, induced by the anode lens, especially at higher energy.

## Slide 15: Acceleration in the DC gun. Space charge effects
Transverse space charge effects
Long bunch
We should include into the right part of the equation for the force provided by the beam field:
for
for
As can be seen:
  The force is directed out of axis so it leads to additional beam defocusing
  The force is linear with
Finally

## Slide 16: Space charge effects. Longitudinal effects II
Longitudinal phase space at the exit of the 350 kV DC photocathode gun as calculated with ASTRA code. Bunch charge 500 pC

## Slide 17: Acceleration in RF guns. Longitudinal dynamics
Field in the RF gun is not constant and depends on time and longitudinal coordinate:
That leads to:
Different parts of the beam are emitted at different field and obtain different energy during acceleration in the gun and obtain different defocusing at the exit of the gun
CLARA 1.5 cell RF gun

## Slide 18: Acceleration in the RF guns. Transverse dynamics I
Strong dependence of the electric field on time and longitudinal coordinate leads to additional forces in the transverse motion.
This provide radial force:
Transverse momentum obtained by electron is defined by:
That gives for :

## Slide 19: Acceleration in the RF guns. Transverse dynamics II
For we have then:
This less depends on at its minimum close to
The remaining quadratic dependence gives rise to the beam projected emittance:

## Slide 20: Space charge effects. Emittance compensation I
Due to the space charge effects after leaving the gun electrons in the bunch have different energy and differently focused and defocused in the beam line.
Different parts of the beam (slices) will occupy different position in the phase space. This results that at attempt to measure emittance with a not time resolved method, and after integration over the bunch we obtain “projected” emittance which will be higher than emittance of each individual slice.
Head
Tail
z
’
Projected emittance

## Slide 21: Space charge effects. Emittance compensation II
For a beam with significant space charge
  Where
  - is the channel focusing strength and
  - generalized perveance.
For a beam with high space charge the third term may be omitted and optimal beam radius and channel focusing are linked as:

## Slide 22: Emission in the magnetic field.
Practically the length of the magnetic field is longer than effective length and propagates to the cathode. It means that the cathode emits the beam in the magnetic field.
Presence of the longitudinal magnetic field on the cathode introduces an angular momentum or beam rotation which appears right after emission and preserves along the beam propagation in the beam line:
  where
This relations is known as Busch’s theorem.
In practice at the exit of the gun where magnetic field is zero angular beam velocity, which is induced by the cathode magnetic field is

## Slide 23: Compensation of the cathode field I
The presence of the angular velocity also known as “beam shear” has negative impact on the beam quality. There are two ways to mitigate cathode magnetic field:
  To move solenoid lens as far as possible from the cathode – the method used in DC and SRF guns
  To compensate residual field with an additional solenoid frequently referred as “bucking coil” – used in NCRF guns

## Slide 24: Compensation of the cathode field II
Compensation of the cathode field with bucking coil

## Slide 25: Velocity bunching
After passing the cavity energy gain is At energy gain is almost linear with and head of the bunch gets negative energy gain and tail – positive Relative speed modulation is After the buncher the length of the bunch reduces and reaches it’s minimum at distance:
Optimal kinetic energy for velocity bunching 60-100 keV
Before buncher
After buncher
Optimal compression
Excessive compression

## Slide 26: Literature
M. Raiser, Theory and Design of Charged Particle beams, WILEY-VCH Verlag GmbH & Co, 2008, ISBN 987-3-527-40714-5
Kwang-Je Kim, RF and Space-Charge Effects in Laser-Driven RF Electron Guns, NIM A275 (1989)201-218
Luca Serafini & James B. Rosenzweig, Envelope analysis of intense relativistic quasilaminar beams in rf photoinjectors: A theory of emittance compensation, Phys. Rev. E 55, 7565(1997)
S.G. Anderson et al., Velocity bunching of high brightness electron beams, PRST AB, 8, 014401 (2005)