## Slide 1
  FFAs for Health
  Roger Barlow, David Bruton, Rob Edgecock, Carol Johnstone and Jordan Taylor
  FNAL & University of Huddersfield
From two theses:
David Bruton, “Investigation of a Compact Accelerator for Radioisotope Production”, 2018
Jordan Taylor, “The Design of Helium Ion Accelerators for External Ion Beam Cancer Therapy”, 2018
Both available from the Huddersfield repository

## Slide 2: Motivations - Radioisotopes
Two isotopes of interest: 99mTc and 211At
99mTc:
  Single photon emitter for SPECT
  Most commonly used radioisotope
  Production route: reactor produced 99Mo as a generator
Cooling problems in main two reactors caused shortage in 2008/2009
Motivated investigations of other production routes
Various studies of accelerator use undertaken

## Slide 3: Motivations - Radioisotopes
Particle accelerators
Electron accelerators
Deuteron accelerators
Proton accelerators
100Mo target
Heavy nucleus target
Bremsstrahlung target
Carbon target
n
γ
n
98Mo target
235U target
238U target
100Mo target
100Mo target
Reaction: 100Mo(p,2n)99mTc
Reaction: 98Mo(n,γ)99Mo
Reaction: 235U(n,f)99Mo
Reaction: 238U(γ,f)99Mo
Reaction: 100Mo(γ,n)99Mo
Reaction: 100Mo(n,2n)99Mo
Primary particle
Secondary particle
Short term: <2017
Med term: 2017-2025
Long term: >2025
Nuclear Energy Agency: direct production 100Mo(p,2n)99mTc

## Slide 4: Motivations - Radioisotopes
Basic parameters
  Energy: 20-25 MeV range
  Beam current: > 200µA, as large as losses, target, etc, allow

## Slide 5: Motivations - Radioisotopes
Therapeutic isotopes – not being fully exploited
211At: single α emitter
28 MeV He ions, high current
209Bi(α,2n)211At
209Bi(α,3n)210At

## Slide 6: Motivations - Radioisotopes
Recent interest in 225Ac
218 keV
440 keV

## Slide 7: Motivations – Cancer Therapy with Helium

## Slide 8: Motivations – Cancer Therapy with Helium

## Slide 9: FFA Design Technique
Employs the Carol method
Non-linear, non-scaling FFAGs
Wedge-shaped magnets, so gradient, edge and weak focussing
Magnetic field profile:
Machine design involves selecting
  Magnet number, shape and size
  Field profile parameters, n and bi
Much flexibility to get flat(ish) tunes and pseudo-isochronicity

## Slide 10: Method
Starting parameters calculated by Carol via her script
Optimisation in Cosy Infinity
Implemented in FACT( Carol and Pavel Snopok):
  Calculates field map, including edge fields
  Finds stable equilibrium orbits as a function of energy
  Calculates tunes, path lengths, etc
  Allows tof to be calculated
(Many!) iterations required to achieve optimal design
Tracking, acceleration and space charge studies done with Opal
Also PyZoubi for radioisotope machine

## Slide 11: Baseline Radioisotope Proton FFAG
75 keV (89mm) to 28 MeV (1687mm)

## Slide 12: Baseline Radioisotope FFAG
CW operation

## Slide 13: Baseline Radioisotope FFAG RF
2 x 7.5 MHz, λ/2 cavities, each 100 kV
Use on 5th harmonic to reduce size, but also phase slip

## Slide 14: Helium Ion Acceleration
For non-relativistic energies, beam rigidity of helium ≈ protons
0.9% different at 28 MeV

## Slide 15: Helium Ion Acceleration
Tunes and DA very similar
TOF is 2 times bigger and spread about 1.5%
Works with the same parameters as protons
Can be improved with small tweaks to the field profile

## Slide 16: Space Charge for Protons
Studied with ± 2cm aperture
Above 20 mA, very large losses
Emittances at 20 mA:

## Slide 17: Space Charge for Protons
Studied with ± 2cm aperture
Above 20 mA, very large losses
Emittances at 20 mA:

## Slide 18: Space Charge Losses

## Slide 19: Proton Injection and Extraction
Radial injection seems to work, with additional small magnet
For extraction, orbit separation at 28 MeV
Not large enough for clean extraction

## Slide 20: Internal Target Studies for 100Mo(p,2n)99mTc
Moly target placed at radius of maximum cross-section, 14 MeV
Aperture of ± 2cm used
Yield is essentially independent of target thickness

## Slide 21: Internal Target Studies for 100Mo(p,2n)99mTc

## Slide 22: Internal Target Studies for 100Mo(p,2n)99mTc
Calculated yield exceeds that measured with ASIC 24 MeV
Can be improved (in principle):
  Wedge-shaped target
  Re-acceleration

## Slide 23: Helium Ion Therapy - Heather
Final design
  Injector: to 1 MeV
  Stage 1: to 400 MeV
  Transfer line
  Stage 2: to 900 MeV

## Slide 24: Heather Stage 1

## Slide 25: Heather Stage 1

## Slide 26: Heather Stage 2

## Slide 27: Heather Stage 2

## Slide 28: Heather Stage 2

## Slide 29: Heather RF Studies
Stage 1:
  Uses 2 delta-type λ/2 double gap resonators
  Gap voltage 300 kV
  Kilpatrick says works with a 4cm gap
  Already used at Riken
  5th harmonic to keep cavity size down
Stage 2:
  Single gap resonators
  Gap voltage 500 kV
  Larger values achieved in operating cyclotrons

## Slide 30: Heather RF Studies

## Slide 31: Heather Extraction Studies
Aim was to see if the PSI technique would work
Optimisation of injection to increase final orbit separation

## Slide 32: Heather Extraction Studies – Stage 1

## Slide 33: Heather Extraction Studies – Stage 2
With parameter optimisation to maximise separation of last orbit

## Slide 34: Conclusions
Designs of two non-linear, non-scaling FFAGs performed
One for high current p and He acceleration for radioisotope production
One for He ion cancer therapy
Both look promising so far, but much more work required
The method used (Carol’s!) is very flexible
The non-linearity and non-scaling nature of the accelerators give many opportunities