## Slide 1
TURBO
Technology for Ultra Rapid Beam Optimisation
Dr. Suzie Sheehy
Senior Lecturer, University of Melbourne
Baker/ANSTO Fellow in Medical Accelerator Physics
suzie.sheehy@unimelb.edu.au
@suziesheehy
Jacinta Yap, Adam Steinberg, Hannah Norman, Rob Appleby

## Slide 2: Questions questions…
What are the (future) challenges in particle therapy?
Where are the technology bottlenecks?
How can FFA optics help?
What needs to be solved/demonstrated?
Is there clinical need/demand?

## Slide 3: Challenges of particle therapy systems
Total treatment time =
  Patient related activities (immobilisation, imaging, unload etc.)
  +
  Equipment related checks (couch positioning, beam checks etc.)
  +
  BDS: Beam delivery time (BDT)
    Beam-on: Irradiation
    Beam-off: Requested, waiting
TIME: efficiency & efficacy…
  Technological limitations restrict availability & utilisation

## Slide 4: From J. Yap, PTCOG 2022:

## Slide 5: How can we improve the delivery of CPT?
Faster treatment means better:
1. Availability: Cost, throughput
Delivery efficiency
2. Utilisation: Effectiveness, quality
  Treatment efficacy
Consider modern active delivery techniques (Pencil beam scanning – spot, line etc.)
  Inherently slow
  Interplay effects
  CPT uncertainties: range & physiologic motion
  Limits treatment for certain (mobile) sites: hypofractionation, rescanning & many other mitigation strategies
<- Multiple x to order of magnitude slower

## Slide 6: Limiting factor: Energy modulation
The constraint which determines the BDT is the energy layer switching time (ELST)
The most dominant contributor to BDT at 71%
BDS efficiency directly related to utility & availability, 70-90% of BDT for majority of tumours <1 L
  1 min reduction in BDT could result in 10x (prostate) patients/day
(J. Shen et al., 2017, Med. Phys., vol. 44, doi:10.1002/mp.12504)
(K. Suzuki et al., 2011, Med. Phys., vol. 38, doi:10.1118/1.3604153)
(K. Suzuki et al., 2016, Med. Phys., vol. 43, doi:10.1118/1.4952731)

## Slide 7: Toward faster treatments…

## Slide 8: What does faster depth scanning mean?
Possibilities for…
Rapid 3D scanning
Bi-directional scanning
  New optimisation methods/delivery sequences
Volumetric rescanning
Delivery in single breath hold/cycle
Beam tracking/gating
Hypofractionation schedules
Notes: Disruptive

## Slide 9: Upright treatments?
TURBO-UP ?
= Fixed beamline delivery
+ upright treatment
+ fast switching
Gantry ‘complimentary’
Advanced imaging: Vert CT/MR
Several clinical indications: Lung/pulmonary, liver/GI etc.
  Ease with breathing, pain, comfort
Faster, robust patient setup?
Greater value of benefit with mobile sites… what about upright treatments?
Future advanced methodologies require an improved BDS…
Image: Leo Cancer Care

## Slide 10: Large energy acceptance (LEA) transport
De-risk & explore feasibility as a fixed-beamline solution for CPT delivery
Lab opportunity for a demonstrator
  Pelletron accelerator
  Low energy (0.5-3.5 MeV) protons & He

## Slide 11: Project TURBO: Technology for Ultra Rapid Beam Operation
CPT is dosimetrically superior and physical possibilities have not been reached: Cost & technological limitations
Goals: improved costs, availability, delivery
  Smaller, cheaper, better
TURBO BDS demonstrator for scaled-down conditions being developed, driven by clinical requirements:
Beam characterisation & simulation studies
Complete beamline development: Diagnostics, magnets, degrader, control system, output platform(s)
FFA arc optics: 3D printed permanent magnet Halbach arrays
Electromagnets: Matching system, scanning magnets
Many emerging modalities... Improvements to BDS are necessary for the future needs of CPT
Jacinta presenting at PTCOG

## Slide 12: Objectives
Development of a novel beam delivery system (BDS) for charged particle therapy (CPT) with an increased energy/momentum acceptance range enabling ‘TURBO 3D’ delivery.
1) World-first demonstration of hadron beams transported through linear non-scaling fixed-field alternating gradient (FFA) optics with a large energy acceptance (LEA)
2) Proof-of-concept measurements demonstrating key TURBO 3D delivery functionalities: rapid energy change and fast multi-dimensional scanning
3) Demonstrate potential clinical advantage of TURBO 3D - treatment planning studies
4) Outline the research and partnership strategy to full-scale clinical prototype
We are open to collaboration on any or all of these elements

## Slide 13: TURBO Progress
Layout Schematic
Magnet Prototyping
Beam Measurements
Profile
Pelletron Current
SEE ADAM STEINBERG’S TALK WEDS 11AM
Notes: Figures:
Layout Schematic: For our beamline, all energies will need to enter at a point, before dispersing out to a maximum at the centre, and returning to their initial positions by the end: this layout will allow for the large energy acceptance required.
Magnet Prototyping: Rapid, low cost magnet creation will allow our beamline to be modified to suit many experiments on a short timescale. We aim to be the first beamline using only commercially available magnet material – held in place by a custom 3D printed support structure - to control our beam. So far, we have successfully demonstrated that this will work, by building a simple example magnet and demonstrating that our predicted fields are achieved.
Beam Measurements: As part of the design process, we need a good idea of the beam distribution that we will need to transport. To measure the profile, we are using the D-PACE fibre scanner, which scrolls a thin wire across the beam to find the distribution. We can directly measure the current using the internal Pelletron diagnostics, which we have used to find and solve potential issues with how the beam intensity varies over time.

## Slide 14: TURBO @ UniMelb
Beam characterisation studies: Pelletron beam input
Simulation studies: beam dynamics & particle tracking
  End-to-end modelling
Conceptual plans:
Complete beamline: Diagnostics, magnets, degrader, control system, output platform(s)
  FFA arc optics: 3D printed permanent magnet Halbach arrays
  Electromagnets: Matching system, scanning magnets
Flexible output end station:
Additional applications?
Radiobiological, detector/diagnostics testing, rock-art scanning

## Slide 15: Slid-Grid Measurement of Pelletron Beam
Notes: As part of the design process, we need a good idea of the beam distribution that we will need to transport. To measure the profile, we are using the D-PACE fibre scanner, which scrolls a thin scintillating fibre across the beam to find the distribution. We built and implemented a new slit-grid measurement system, and can also compare that to directly measuring the current using the internal Pelletron diagnostics, which we have used to find and solve potential issues with how the beam intensity varies over time.

## Slide 16: Lots of avenues to be explored…

## Slide 17
Slides courtesy: H Norman
CCT Magnet Diagrams with windings and mandrel
`Canted-Cosine-Theta (CCT) magnet’

## Slide 18: Scaling Up
Full-scale clinical beamline requires:
  Higher strength magnets (maximum field ~3.5 T)
  Good field quality
  Compactness
Curved Canted-cosine-theta (CCT) arrangement may be suitable:
  Strong focusing
  Large field to accommodate heavier ions to full kinetic energies
  Compact and lightweight
Collaboration with CERN (NIMMS) on EM model to study and adapt for TURBO
Alternating-Gradient (AG) Quadrupole layers 1,2
Dipole layers 3,4
Alternating-Gradient CCT dipole magnet, adapted from W. Wan et al, DOI: 10.1103/PhysRevSTAB.18.103501
SEE HANNAH NORMAN’S TALK WEDS 16:45

## Slide 19: Some other UniMelb updates…

## Slide 20: Lattice optimization for compact synchrotrons
X. Zhang, S. Sheehy, DOI: 10.1063/5.0047815
Frank Zhang, Completion Seminar

## Slide 21: X-LAB (X-band Lab for Accelerators & Beams)

## Slide 22: X-LAB: X-band Laboratory for Accelerators and Beams PROGRAM 2021 - 2026
Conditioning of TD24 & algorithm
Design for applications
Reconfigure to accelerating mode
Rf pulses with beam
2022
2023
2024
Phase 2: 40 MeV tunable, pulsed electrons & applications
Heavy work, water & electricity completed
Design & simulation
Procurement of beamline
Beamline commissioning
Phase 1: X-band Research & Establishment
FUNDED ARC LIEF
w. ANSTO, Wollongong & Sydney
First X-band rf pulses
Enable application-based research: space dosimetry, biophysics, radiotherapy, etc…
Electron gun added
2025/6
Compton light source experiments?
2 OPEN PhD POSITIONS
Notes: Main Goal

## Slide 23: The Matter of Everything: Twelve Experiments that Changed our World
UK/Aus launch April’22: Amazon top #100 all books, bestseller in popular science & physics
US/Canada launch in Jan 2023 + 11 translations
If you want a copy, I recommend Mostly Books (a few mins walk away from Coseners House) or Blackwells in Oxford.

## Slide 24: Job Opportunity
https://careers.ansto.gov.au/job/Melbourne-Accelerator-Physicist-VIC/931733410/