## Slide 1
FFA’22
Canted-Cosine-Theta Magnets for FFAs
Hannah Norman
  Universities of Manchester and Melbourne, Cockcroft Institute
  28/09/22
hannah.norman@manchester.ac.uk

## Slide 2: Outline
Review of Canted-Cosine-Theta (CCT) Technology
CCT Magnets in FFAs: How would that work?
  TURBO
NIMMS (Next Ion Medical Machine Study) Collaboration
  Superconducting Magnet Studies
Questions

## Slide 3: Problems in FFAs
Disadvantages:
Strong focusing  Large energy acceptance
High rep. rate, fast acceleration, higher currents + intensities
Reliable due to fixed magnets (no ramping)
FFAs (in general) can be a very advantageous accelerator solution:
Large complex magnets  Large footprints
Difficulty adjusting magnets
Higher energies require stronger fields
Heavy dependence on field quality due to DA shrinkage

## Slide 4: More generally…
One quadrant of cosine-theta coil
Hadron colliders require strong (> 4 T) magnetic fields
  Superconducting magnets needed
  Common type is ‘Cosine-Theta’
  Wire carrying current on annulus of width bw
  Pure dipole (n=1) field produced for current density

## Slide 5
From Maxwell’s magnetic field equations, we arrive at the Laplace equation
Magnet Theory
From 2D magnetic field solution:
Bn , An = Normal and Skew multipoles
FFT on Bmain returns multipole coefficients
Scale for different Rref to know field everywhere

## Slide 6: Canted-Cosine-Theta Magnets
Dipole component adds
Solenoid component cancels
How do they work?
(AKA double helix, tilted solenoid, etc…)
Coil-dominated
‘Perfect’ dipole field due to
Basic idea of CCT

## Slide 7: Examples of CCT
A very attractive solution for…
CCT Winding Geometry
ϑ = azimuth, h = winding pitch, α = tilt, n = order, ϕ = phase (0 = normal, ½ = skew)
Requires little to no pre-stress
Requires no additional supports
Can achieve very strong fields (16 T)
Concept to combat limitations in cos-theta magnets:

## Slide 8: High Energy Colliders
*(now will be racetrack)
Name | Conductor | Bore [mm] | I [kA] | B-bore [T] | B-bore tested [T]
CCT1 | NbTi | 50 | 4.0 | 2.5 | 2.4
CCT2 | NbTi | 90 | 10.3 | 5.1 | 4.6
CCT3 | Nb3Sn | 90 | 17.7 | 10.0 | 7.4
FCC-hh Main Dipole*
Fast turnaround of CCT development
Poor control of cable positioning
Costly materials (Nb3Sn conductor → $1.7M USD per magnet)
Study Outcomes:
Design goals: 16T, 15m long, 50mm aperture
  R&D short samples parameters (2-layer, operating at 4.2 k)

## Slide 9: High Energy Colliders
Correctors
(HL-LHC, Super β)
Project | Length [m] | Conductor | Bore [mm] | I [A] | B-bore | Integrated Field
HL-LHC | 2.19 | NbTi | 50 | 435 | 2.59 T | 5 Tm
Super β | ~0.5 | NbTi | 50 | 2626 | 95.6 T/m | 0.231 T
Straight 2m corrector for Hi-Lumi LHC
Interaction point of Super β
e+e- collider with CCT quad correctors

## Slide 10
Corrector (HIE-ISOLDE)
Extraction septum magnet (SuShi)
High Energy Applications
Superconducting Shield (SuShi) Septum Magnet
High Intensity and Energy (HIE) Isotope Mass Separator (ISOLDE) Main Ring layout
Project | Magnet | Field [T] | Gradient [T/m] | Current [A]
HIE-ISOLDE | F | 2.27 | 13.8 | 437
 | D | 2.27 | -13.8 | 437
 | Trim Quads | - | 2.2 | ± 300
SuShi | Dipole | 3.0 | - | 428

## Slide 11: Medical Accelerators
PAMELA FFA
Magnet | Field [T] | Current [A] | Length [m] | Rinner [mm] | Router [mm]
F | 3.9 | 755 | 0.6644 | 170 | 216.2
D | 5.06 | 650 | 0.66 | 170 | 244
Variation of multipole strength along magnet
length
Solenoidal components did not cancel locally
  Lead to beam losses after a few turns
  2 additional layers to cancel unwanted components
Multipole errors adjusted via winding
  Tune shift (0.3, 0.23) (h,v) v.s. (0.5, 0.5) previously
Study Outcomes:
PAMELA FFA and particle tracing through cell

## Slide 12: Medical Technology
Gantries (LBNL, HUST) (in progress)
LBNL (top), HUST (bottom) SC gantry layouts
Parameter | LBNL | HUST
B[T] | 2.4 | 2.46
Gradient [T/m] | 17.43 | 12.0
Current [A] | 922 | 584.38 (dip), 370.84 (quad)
Physical Bend [°] | 67.5 | 90

## Slide 13
Why CCTs?

## Slide 14: Advantages
Due to the unique geometry of the CCT,
Dipole
Quadrupole
Sextupole
Octupole
Decapole
Dodecapole…
Can be combined function (depending on coil winding)
Good field quality
Small stresses on conductor
Can independently tune harmonics
Compact design
Simple to wind
Can be strongly curved (for e.g space saving purposes)

## Slide 15: Why not CCTs?
Though proposed in 1969, CCTs are still a relatively new concept and widely untested
Need more conductor for higher fields (£££)
No one has used them in medical accelerators in practice yet
Can be complicated to design and resolve fields (especially for curved case)
Can’t ramp quickly (leads to quench)

## Slide 16: Possible Applications
Though CCTs look good on paper, we should be careful about how we are using them and what we are using them for
Application | Field | Length | # of magnets | Benefit v.s. cost, effort
Large Colliders | Large (> 16 T) | Long (15 m) | Lots | Arguable
Compact Machines | Small (3-4 T) | Short (~2 m) | Few | Huge
What about in an FFA?

## Slide 17
TURBO
(Technology for Ultra Rapid Beam Operation)

## Slide 18: TURBO
TURBO FFA Beamline (lab demonstrator version)
Courtesy of J. Yap
18
Scaled-down (0.5-3 MeV) test beamline for treatment
Closed-dispersion FFA arc for Large P Acceptance
Accommodates clinical system requirements
Controllable beam dynamics for transported energies
Non-linear magnets with required multipoles for stability
Unique magnets at each point in arc → CCT demonstrator
Concept:
To show:
Requires:

## Slide 19: Scaling Up
  Higher strength magnets (maximum field ~3.5 T) to treat in modes
  Adjustable multipoles
  Good field quality (1E-4)
  Compactness
1st mode
2nd mode
3rd mode
Species | E [MeV/u] | Tm] |  | Tm]
p+ | 70 - 250 | 1.23 – 2.43 | 33% | 0.6 – 1.22
4He2+ | 70 - 250 | 2.43 – 3.32 | 33% | 1.22 – 1.66
12C6+ | 70 - 430 | 2.50 – 6.63 | 45% | 1.25 – 3.32
16O8+ | 70 - 500 | 2.50 – 7.26 | 49% | 1.25 – 3.63
Species | E [MeV/u] |  |  | 
p+ | 70 - 250 | 1.23 – 2.43 | 33% | 0.6 – 1.22
4He2+ | 70 - 250 | 2.43 – 3.32 | 33% | 1.22 – 1.66
12C6+ | 70 - 430 | 2.50 – 6.63 | 45% | 1.25 – 3.32
16O8+ | 70 - 500 | 2.50 – 7.26 | 49% | 1.25 – 3.63
Full-scale Clinical Beamline Requires:

## Slide 20: Scaling Up
Alternating-Gradient CCT dipole magnet
  Strong focusing
  Large field to accommodate heavier ions to full kinetic energies
  Compactness, light weight
  Tuneable multipoles
Collaboration with CERN (NIMMS) on electromagnetic model to study and adapt for TURBO
But first, a model…
Curved Alternating-Gradient CCT demonstrator could provide:
Notes: Mention momentum ranges achievable (also what was achieved with the previous gantries)

## Slide 21: Review so far
CCTs are an exciting technology, but still ‘new’
Could benefit future designs of FFAs, compact medical machines, more possibilities
Straight and curved magnet models for analysis
Particle tracking through 3D multipole fields on and off-axis
Establish tolerances for multi- v.s. single pass systems
In order to confirm that we can apply (curved) CCTs to FFAs, we need:
Beam dynamics studies required…

## Slide 22
NIMMS
(Next Ion Medical Machine Study)
A collaborative study from CERN to develop portfolio of technology for future facilities

## Slide 23: Medical Superconducting Synchrotron
Goal: Design a smaller heavy ion therapy synchrotron for next gen. facilities
NIMMS Superconducting Compact Synchrotron, courtesy of E. Benedetto
What makes this design special?
23
Based on 90° CCT magnets at 3.5 T
27 m circumference, 1.89 m bending radius
Combined-function quadrupole layers inside dipole
Adapt magnets from synchrotron to gantry
Perform beam dynamics simulations:
Study unique magnet effects

## Slide 24: Curved, Combine-Function Magnets
24
How does curvature affect the field distribution?
How does this affect particles in the accelerator?
What issues arise from additional CF layers?
Alternating gradient CCT layers
Problem: We can’t use multipole expansion
Curvature (seemingly) introduces additional harmonics
→ Can be corrected

## Slide 25: Validity of Multipole Expansion
We’ve already seen we can express the magnetic field in a 2D straight system as:
Vector potential in curved coordinates:
Not a solution to Maxwell’s equations
Multipoles have no physical meaning
Can’t use scaling law
25

## Slide 26: Validity of Multipole Expansion
Three cases where we can’t use multipole expansion to describe the field:
When might we have all three to worry about? In FFAs!
In curved coordinate systems
Longitudinally dependent fields (at the ends)
Where the field has longitudinal components (off-axis)
Workaround Solution:
Taylor expansion of potential satisfies Maxwell’s equations
3D version:
Z cross-terms
Analytical solutions
26

## Slide 27: Straight and Curved Magnets
30° bend
B = 3T, g= 3.5 T/m
27
Courtesy of M. Karpinnen
NIMMS CCT model a WIP
CF Cosine-Theta dipole to analyse in meantime
Modelling in OPERA 3D:
Straight cosine-theta demonstrator EM model
Curved cosine-theta demonstrator EM model (30 °)

## Slide 28: Straight and Curved Magnet Comparison
Component | Straight |  | Curved | 
 | FFT | Fit | FFT | Fit
B1 (Dip.) [Tm] | -3.46 | -3.46 | -3.46 | -3.43
b2*(Quad.)[10-4 ] | -318.2 | -287.4 | 236.1 | 275.6
b3 (Sext.)[10-4 ] | 3.1 | 3.0 | 1.9 | 1.52
b4 (Oct.)[10-4 ] | -1.7 | 2.0 | 2.5 | 5.15
x
y
z
(*On-axis analysis for now)
Developed two analytical techniques*
28
Measuring field as a function of angle
  Calculate multipoles using Fourier analysis
Measuring field map over slice
  Fit straight line to main field along midplane (y=0)
Field sampling in OPERA 3D

## Slide 29: Particle Tracking Study
Parameter | Value
Ekmax [MeV/u] | 430
Nparticles [-] | 2 x 1010
σx, σy [mm] | 0.85, 1.78
Qx , Qy [-] | 1.68, 1.13
NIMMS Synchrotron in MAD-X with magnets shown
Tracking parameters for the NIMMS Synchrotron
29
Tracked particles in synchrotron lattice
With and without curved magnet errors
Feed errors into lattice dipoles for tracking
→ How ‘bad’ are they?)

## Slide 30: Particle Tracking Study
Map of starting tracking locations (x,y) corresponding to
each particle’s time in the ring
30
Start particles at initial offset (x,y) in accelerator
Gather e.g. x-data from each particle per turn
Perform an FFT on data to return Qx
→ This lets us see how long those particles last
Map (x,y) to identify stable regions (DA)
DA mostly preserved within ½ aperture
Tracking to full magnet aperture, DA≈ 40%
→ Errors would need adjusting if we really use this
FFT on x -positions

## Slide 31
Next Steps

## Slide 32: Next Steps
Need full 3D magnetic field representation for each magnet
Track particles through these fields (using e.g. Zgoubi, Zgoubidoo) to investigate
  Beam distortion
  Fringe field extent in each layer
  DA shrinkage (needs parameterisation)
Establish design criteria for our scaled-up beamline

## Slide 33: Questions?
If you know, let us know!
How does curvature affect multipoles in a CCT?
  How much does it distort the beam/cause tune shifts?
Do fringe fields form between layers?
  How close can we layer the FDFD quads?
How can we accurately calculate 3D fields?
What are our design criteria?
What might TURBO look like based on CCTs?
Power the magnets individually?

## Slide 34: Summary
Heavy ion therapy necessary but limited by size, cost
Need innovative accelerators based on superconducting magnets
Tools developed for studying effect of magnet errors on particles in accelerators
Continue study for comparing errors from straight v.s. curved magnets
Establish design criteria for a CCT for other applications (TURBO)
Canted-Cosine Theta Magnets are an enabling technology
Huge potential, if used correctly
Applications:

## Slide 35: Thanks to:
UniMelb team:
A. Steinberg
J. Yap
F. Zhang
S. Williams
Supervisors: Prof. R Appleby (UoM), Dr S. Sheehy (UniMelb)
Collaborators: Dr E. Benedetto, Dr M. Karppinen (external, NIMMS)
35

## Slide 36: References
[1] D.I. Meyer and R. Flasck “A new configuration for a dipole magnet for use in high energy physics application”, Nucl. Instr. and Methods 80, pp. 339-341, 1970.
[2] S. Caspi S, “A 16T Canted-Cosine-Theta (CCT): An option for the FCC”, presentation, 2015, accessed 01/09/2022
CCT winding diagram, from [2]
[3] FCC-hh main dipole CCT from S. Caspi, “Status and Development of a Nb3Sn CCT magnet”, presentation, 2016, accessed 01/09/2022
[4] HL-LHC main corrector magnets and design parameters (straight and curved), G. Kirby, https://www.researchgate.net/project/LHC-hi-Lumi-orbit-corrector-5Tm-CCT, accessed 26/09/22 (gets updated daily)
[5] Super-beta layout and CCT quadrupole diagram, F Bosi et al (2013). Compact Superconducting High Gradient Quadrupole Magnets for the Interaction Regions of High Luminosity Colliders. 10.1109/TASC.2012.2231716.
[6] Recoil separator ring, Resta Lopez, Javier et al (2021). DESIGN AND BEAM DYNAMICS STUDIES OF A NOVEL COMPACT RECOIL SEPARATOR RING FOR NUCLEAR RESEARCH WITH RADIOACTIVE BEAMS. 10.18429/JACoW-IPAC2021-WEPAB180.
[7] SuShi septum magnet, from http://sushi-septum-project.web.cern.ch/, accessed 27/09/22
[8] PAMELA layout, cell and CCT design details, Witte, Holger et al (2012). The Advantages and Challenges of Helical Coils for Small Accelerators—A Case Study- IEEE TRANS APPL SUPERCONDUCT. 22. 4100110-4100110. 10.1109/TASC.2012.2186135.
[9] Superconducting gantry, CCT and design parameters, L. Brouwer et al, Design and test of a curved superconducting dipole magnet for proton therapy (2020) https://doi.org/10.1016/j.nima.2020.163414.
[10] Superconducting gantry and CCT design parameters, C. Li, "Coil Error Analysis of a Curved Canted-Cosine-Theta Magnet Applied to a Superconducting Gantry (2022) Art no. 4006105, doi: 10.1109/TASC.2022.3170857.
[11] CCT Windings, from G. Kirby “State of the art in CCTs”, 2022, [accessed 27/09/22]
[12] J.S.L. Yap, et al “TURBO: A Novel Beam Delivery System Enabling Rapid Depth Scanning for Charged Particle Therapy (2022) doi:10.18429/JACoW-IPAC2022-THPOMS001
13[] Radiotherapy clinic, https://www.whittington.nhs.uk/default.asp?c=27306 , accessed 28/09/22
[14] HIT Carbon gantry, adapted from https://www.worldscientific.com/doi/abs/10.1142/S0217751X14410024?journalCode=ijmpa , accessed 08/09/22
[15] NIMMS Superconducting Compact Synchrotron, adapted from E. Benedetto
CCT Diagram, E. Benedetto, et al., “A Carbon-Ion Superconducting Gantry and a Synchrotron Based on Canted Cosine Theta Magnets (2021) ,”doi:10.48550/arXiv.2105.04205
[16] Goodzeit, C, et al (2007). Combined function magnets using double-helix coils. 560 - 562. 10.1109/PAC.2007.4440278.
[17] D. Veres, et al, “A New Algorithm for Optimizing the Field Quality of Curved CCT Magnets (2022) doi:10.1109/TASC.2022. 3162389
[18] Curved and straight cosine-theta models, courtesy of M. Karpinnen
[19] H.X.Q. Norman, et al “Performance Study of the NIMMS Superconducting Compact Synchrotron for Ion Therapy with Strongly Curved Magnets (2022) ”,doi:10.18429/JACoW-IPAC2022-THPOMS028