## Slide 1: 22 GeV CEBAF FFA Energy Upgrade
Alex Bogacz
Feasibility study for additional FFA racetrack in the existing CEBAF tunnel to reach the top energy of about 22 GeV
FFA’22 Workshop, Abingdon, UK

## Slide 2
The FFA@CEBAF Collaboration
†

## Slide 3: Overview
Current baseline: 650 MeV inj + 4-pass CEBAF + 6-pass FFA
Adiabatic FFA Arc – -proven architecture
  Non-scaling FFA based on high-gradient permanent magnets
  Adiabatic control of betas and dispersion (gradual variation of cells)
Multi-pass linac optics
  650 MeV injector upgrade
  Periodic triplet lattice for all passes
Modified CEBAF ‘switchyard’ and TOF correction ‘splitters’
Synchrotron radiation impact on beam quality, mitigations
Summary, Outlook

## Slide 4: CEBAF FFA Upgrade – Baseline under Study
  Starting with 12 GeV CEBAF
  NO new SRF (1.1 GeV per linac)
  New 650 MeV recirculating injector
  Remove the highest recirculation pass (Arc 9 & A) and replace them with two FFA arcs including time-of-flight chicanes
  Recirculate 4.5 + 6 times to get to 22 GeV
Novel permanent magnet technology used for power and cost savings
Pass Arithmetic: 5.5 -1 + 6 = 10.5
TOF
TOF
650 MeV

## Slide 5
FFA CEBAF with -like Arcs

## Slide 6: FFA Arc - Compact FODO Cell
Large momentum acceptance FFA cell, configured with combined function magnets capable of transporting six beams with energies spanning a factor of two
Arc composed of 98 cells, Lcell = 2.44 m
Closely spaced orbits for all six beams (~ 3 cm)
Low betas (~ 10 m)
Extremally low dispersion (a few cm)
E=22.65 GeV
E=18.25 GeV
E= 13.85 GeV
E=20.45 GeV
E=11.65 GeV
E=16.05 GeV

## Slide 7: Permanent Magnet Design
8.3 cm
8.1 cm
Focusing Magnet QF
GF= -71.60551 T/m
LQF= 1.4 m
qF= -0.024771371 rad
BF= -1.209916 T
BFMAX=-1.6403 T
Defocusing Magnet BD
GD= 89.643365 T/m
LBD= 0.8802552 m
qD= -0.005504749 rad
BD= -0.427624 T
BDMAX=-1.631 T
8 cm
6.95 cm
magnets: from 38cm2 to 78cm2

## Slide 8: Adiabatic FFA Arc Architecture
Optical functions for the entire 10-22 GeV (6-pass) FFA racetrack
Gradual variation of individual cell length and bend angle allows for beta functions to expanded adiabatically and the dispersion to vanish at arc ends. The larger beta functions are compatible with higher-beta optics in the linacs (30 - 90 meter betas). This simplifies switchyard and reduces its functionality to pathlength and momentum compaction adjustment.

## Slide 9: Adiabatic FFA Arc Architecture

## Slide 10
Injector Upgrade - 650 MeV Recirculating Injector
With the present 123 MeV injector, the difference in the first and final pass energies in the North Linac is too large (1:175) to effectively control the beam.
650 MeV recirculating injector (3-pass) based on LERF will allow a manageable difference in energies (1:33)

## Slide 11
Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
436 MeV
10 MeV + 3 × 3 × 71 MeV = 650 MeV
10 MeV

## Slide 12
Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
436 MeV
10 MeV + 3 × 3 × 71 MeV = 650 MeV
10 MeV
C-75
C-75
C-75
10 MeV + 3 × 3 × 71 MeV = 650 MeV
New arc
New arc
650 MeV

## Slide 13
Present FODO linac offers periodic optics only for the lowest energy pass with large beta beating for higher passes (beta ~1000 m), which is not compatible with small betas (~10 m) in the FFA arcs.
‘Twin Cell’ Triplet
Strongly Focusing Multi-pass Linac Optics (11 passes)
19.2
0
120
0
BETA_X
BETA_Y
19.2
0
30
0
BETA [m]
BETA_X
BETA_Y
650 MeV
21.6 GeV
BETA [m]
G[kG/cm] = 2.35
G[kG/cm] = -2.40
Q = 0.39
Q = 0.39
pass-1
pass-11

## Slide 14: Multi-pass Linac Optics (1:33 Energy Ratio)
241
0
30
0
BETA_X&Y[m]
BETA_X
BETA_Y
650 MeV
pass-1
2.83 GeV
241
0
30
0
BETA_X&Y[m]
BETA_X
BETA_Y
pass-2
21.6 GeV
pass-10
241
0
90
0
BETA_X&Y[m]
BETA_X
BETA_Y
pass-11
Phase advance: 1400 per cell

## Slide 15: ‘Weakly Focusing’ Linac Optics
241.768
0
100
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
241.768
0
50
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 2
pass 1
2.8 GeV
0.65 GeV
Phase advance: 290 per cell

## Slide 16
241.768
0
300
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
241.768
0
300
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 11
pass 5
9.4 GeV
21.6 GeV
‘Drift’ Linac Optics – FFA Passes

## Slide 17: Energy Loss, Emittance Dilution (4-pass CEBAF)
  Doubling the energy, while staying within current CEBAF footprint, makes the synchrotron radiation effects of paramount importance.
  Quantum nature of a ‘recoil’ effect on electrons due to photon emission makes significant impact on both the transverse and longitudinal beam dynamics, leading to cumulative emittance growth (transverse and longitudinal).
Energy loss
Emittance dilution
Natural energy spread

## Slide 18: Energy loss, Emittance Dilution (6-pass FFA)
6 passes
Synchrotron radiation mitigation in FFAs
  High fill factor (88% space filled with bends) increases significantly the bend radius, r.
  By virtue of extremally small dispersion and betas, the horizontal emittance dispersion, <H>, is highly suppressed (factor of 50 lower then in a conventional CEBAF arc lattice).

## Slide 19: Vertical Switchyard Layout
pass 1
pass 2
pass 3
pass 4
FFA passes 5-10
FFA passes 5-10

## Slide 20: Vertical Switchyard Optics
Spreader pass 1
Spreader pass 5

## Slide 21: Horizontal Splitters
Functionality
Ensure RF synchronization for all FFA passes
Control longitudinal phase space distribution on FFA passes
Ensure transverse matching of linac to the FFA
Requirements
Each splitter line shall have its length adjusted so that the time of flight between the linacs differs from the time of flight between linacs for a non-FFA pass by an integer number of wavelengths
Each splitter line shall match the transverse lattice functions at the end of the corresponding linac to the lattice functions of the repeating FFA cell, the latter being treated as a single period
Each splitter line shall ensure that the derivative of time with respect to energy is zero from the linac preceding it the linac following it

## Slide 22: Error-free Orbit and Dispersion in FFA Arc

## Slide 23: FFA Arc with Uncorrected Random Errors
Every offset and drift in the whole lattice has a uniform error of up to .25 mm
Each magnetic field and gradient attribute has an error chosen from a normal distribution
Dispersion in uncorrected arc with errors
Beam position: error bars represent deviation from average

## Slide 24: Panofsky Quad Window Correctors

## Slide 25: Summary
Present Baseline (1.1 GeV per linac):
  650 MeV Recirculating Injector (additional three C-75 cryomodules)
  Recirculate 4 passes with the current CEBAF
  Plus Additional 6 passes via a single FFA: 10 – 22 GeV
Adiabatic FFA arcs configured with compact FODO cells
  Beta and dispersion matching to the linacs through cell-by-cell variation (length, bend)
  Open mid-plane permanent magnet design: B-field ≤ 1.7 T, Gradient ≤ 90 T/m
Synchrotron Radiation impact on beam quality:
  Net transverse emittance dilution (normalized): 60 mm mrad
  Net natural energy spread: 2×10-3
  Net synchrotron radiated energy: 0.96 GeV
Engineering analysis and cost estimates – are in progress
  Ready for Long Range Planning submission
at 22 GeV, b = 20 m → s = 150 microns

## Slide 26: Outlook
‘White Paper’ on Future of CEBAF

## Slide 27
Thanks for your attention!

## Slide 28
Backup Slides

## Slide 29: CEBAF Energy Upgrade 10.55 → 23.75 GeV
Injector at 650 MeV
1.1 GeV
1.1 GeV
#1-10.55 GeV
#2-12.75 GeV
#3-14.95 GeV
#4-17.15 GeV
#5-19.35 GeV
#6-21.55 GeV
#1-11.65 GeV
#2-13.85 GeV
#3-16.05 GeV
#4-18.25 GeV
#5-20.45 GeV
#6-22.65 GeV
9.45
9.45 GeV
8.35
7.25 GeV
7.25
6.15 GeV
5.05 GeV
1.75 GeV
2.85 GeV
6.15
3.95 GeV
3.95
1.75
8.35 GeV
2.85 GeV
12 GeV
5.05 GeV
WEST FFA
EAST FFA
23.75 GeV
0.650
80.6 m
80.6 m
4 existing lines + 6 FFA turns
1.75 GeV
22.65 GeV
23.75 GeV
0.65 GeV
Energy range
Energy range

## Slide 30
Multi-Bunch Dynamics in FFA Arc

## Slide 31: General Analysis and Outlook
Orbit average positions are stable, but fluctuations can be large; correction scheme will need to predict large deviations.
Work on a Markov chain Monte Carlo simulation to representatively sample the high dimensional space of possible errors is under way
  Hope to gain insight into an appropriate correction algorithm with reasonable statistics
Next steps in simulations include optimizing BPM placement and calculating preliminary response matrix