## Slide 1: Bayesian Data Analysis for Interpreting QENS Experiments
Sanghamitra Mukhopadhyay
ISIS Facility, Rutherford Appleton Laboratory, Chilton, Didcot, Oxfordshire OX11 0QX

## Slide 2: Motivation
Using Bayesian data analysis for neutron spectroscopy
  Analysis of Quasi elastic neutron spectroscopy (QENS) involves fitting of number of peaks where their characteristic parameters predict physical processes underlining of any dynamical event.
  Bayesian Data Analysis used to analyse complicated data consists of complicated spectrum
Development of the tool for the purpose of analysis of QENS data on neutron instruments
  Convolution with instrument resolutions
  Quantitative understanding of the quality of peak fitting
  Sequential fitting and multidimensional data fitting
Implementation of robust and efficient algorithm for high throughput QENS data analysis

## Slide 3: Outline
What is QENS spectra?
What is Bayesian data analysis ?
Fitting Algorithm for Bayesian Analysis of Data (FABADA)
Implementation of FABADA in Mantid
Examples of QENS data fitting
Summary
Outlook

## Slide 4
What is Quasi Elastic Neutron Scattering (QENS) ?
QENS is used to study the rotational and diffusive motions of atoms and molecules in materials.
The four dimensional data is often analysed by fitting with number of Lorentzians
The width of Lorentzian (Γ) depends on Q and temperatures

## Slide 5: Molecular Dynamics for INS and QENS
Molecular dynamics space
t
r
Q
ω
Neutron scattering space
van Hove correlation function
Intermediate scattering function
Dynamic structure factor
Frequency dependent radial distribution function

## Slide 6
F. Demmel and S. Mukhopadhyay, J. Chem. Phys. 144 14503 (2016).
Each Lorentzian is associated with particular type of molecular motion so it is important to know how many Lorentzian are there in a single peak
The Γ(Q) determines the mechanism of diffusion
QENS Experiment on molten NaF ionic liquid

## Slide 7
The model determines different types of mechanisms of diffusions
Diffusion Models for QENS

## Slide 8
QENS Experiment to design solid acid catalyst
Diffusion modes of cyclohexanone oxime passing through a pore with active sites (red), Top: Smooth Fickian diffusion means the oxime diffuses straight down the pore. Bottom: Jump diffusion sees the oxime move between active sites with a specific residence time.
The Q dependence of the HWHM of the Lorentzian for Zeolite-Y (left) and SAPO-37 (right) obtained from QENS experiment on OSIRIS
M. E. Potter et al., ACS Catal., 7 2926 (2017).

## Slide 9: Bayesian Data Analysis
Bayes Theorem
Model selection (How Many Lines are there?)
H : Hypothesis
D: Experimental data
I: Implicit information
Where M is the number of peaks, χ is the cost function
PDF P(χ2) is calculated by the FABADA code
Statistical methods are used to analyse complicated data consists of several overlapping peaks, backgrounds and spurions.

## Slide 10
Classical fitting schemes: two main problems
... a simple function

## Slide 11
WHY IS IT NOT FITTING?????
... a simple function
Classical fitting schemes: two main problems

## Slide 12
With four parameters I can fit an elephant,
and with five I can make him wiggle his trunk.
Von Neumann
... model selection is often dangerous:
Classical fitting schemes: two main problems

## Slide 13
Goodness of fit quantified by a single number
... model selection is often dangerous:
... having into account the number of parameters m
Classical fitting schemes: two main problems
With four parameters I can fit an elephant,
and with five I can make him wiggle his trunk.
Von Neumann

## Slide 14: Bayesian Data Analysis

## Slide 15
Fitting get’s stuck
Model selection
χ2 landscape minimum
χ2 landscape exploration

## Slide 16
Fitting get’s stuck
Model selection
χ2 landscape minimum
χ2 landscape exploration
How it is supposed to be
How it is supposed to be
Single global minimum
Squared well

## Slide 17
Fitting get’s stuck
Model selection
χ2 landscape minimum
χ2 landscape exploration
How it is supposed to be
How it is supposed to be
Single global minimum
Squared well
How it really is
How it really is
Multiple minima (unable to jump)
It is not squared

## Slide 18: FABADA
Fitting Algorithm for Bayesian Analysis of Data
FABADA algorithm uses Markov Chain Monte Carlo method and Gibbs sampling to find out the local minimum of χ2 and calculates probability distribution function.
It is a general purpose algorithm can be used anywhere where Bayesian analysis is required
We have adapted this algorithm to analyse QENS
To perform the best fit, a model selection algorithm also runs within FABADA which selects the preferred number of peaks and their parameters by minimising the cost function.
https://gcm.upc.edu/en/members/luis-carlos/bayesiano

## Slide 19
Bayesian tool to explore χ2 landscape
χ2old
Step | 2 | P1 | P2 | P3
1 | 1.368·104 | 1.341 | 0.0023 | 10.223
2 | 1.360·104 | 1.342 | 0.0023 | 10.223
3 | 1.362·104 | 1.342 | 0.0023 | 10.223
4 | 1.348·104 | 1.342 | 0.0022 | 10.170
... | ... | ... | ... | ...

## Slide 20
Bayesian tool to explore χ2 landscape
Acceptance rules:
If better always
If not, with probability
χ2new
χ2old
χ2old
Step | 2 | P1 | P2 | P3
1 | 1.368·104 | 1.341 | 0.0023 | 10.223
2 | 1.360·104 | 1.342 | 0.0023 | 10.223
3 | 1.362·104 | 1.342 | 0.0023 | 10.223
4 | 1.348·104 | 1.342 | 0.0022 | 10.170
... | ... | ... | ... | ...

## Slide 21
Bayesian tool to explore χ2 landscape
Step | 2 | P1 | P2 | P3
1 | 1.368·104 | 1.341 | 0.0023 | 10.223
2 | 1.360·104 | 1.342 | 0.0023 | 10.223
3 | 1.362·104 | 1.342 | 0.0023 | 10.223
4 | 1.348·104 | 1.342 | 0.0022 | 10.170
... | ... | ... | ... | ...
Acceptance rules:
If better always
If not, with probability
χ2new
χ2old
χ2old
χ2new
(Adaptive Gibbs Sampling Algorithm)

## Slide 22
Bayesian tool to explore χ2 landscape
fit
analyze

## Slide 23
Bayesian tool to explore χ2 landscape
fit
analyze
It does not get stuck

## Slide 24
Bayesian tool to explore χ2 landscape
fit
analyze
... and if it does
we increase the errors
A 2D χ2 landscape
Warming up the fitting
Simulated annealing
It does not get stuck

## Slide 25
Bayesian tool to explore χ2 landscape
fit
analyze
Parameter estimation:
Parameters are obtained as PDF's not as P±δP
δP=σ
Robust parameter
estimation
It does not get stuck

## Slide 26
Bayesian tool to explore χ2 landscape
fit
analyze
Robust parameter
estimation
Parameter estimation:
Parameters are obtained as PDF's not as P±δP
It does not get stuck

## Slide 27
Bayesian tool to explore χ2 landscape
fit
analyze
Model selection:
all possible combinations of parameters are investigated
and their χ2 calculated
Robust model selection
It does not get stuck
Robust parameter
estimation

## Slide 28: FABADA in Mantid (FIM)
FABADA has been implemented as a general purpose minimiser in fit wizard in Mantid
Choose FABADA as minimiser
Use high value for maximum number of iterations
Use of simulated annealing is optional
Define temperature if simulated annealing is chosen
https://www.mantidproject.org/MantidPlot:_Simple_Peak_Fitting_with_the_Fit_Wizard

## Slide 29: FIM as an Interface
D Monserrat, A Vispa, LC Pardo, R Tolchenov, S Mukhopadhyay, F Fernandez-Alonso, J Phys Conf. Ser 663 (2015).

## Slide 30: Recent Updates : Simulated Annealing
Simulated annealing can be used to find out global minimum
BL Vidal, E Oram, RA Banos, LC Pardo, S Mukhopadhyay, and F Fernandez-Alonso, J. Phys. Conf. Ser 1021, 12012 (2018).

## Slide 31: Multi dimensional Data Fitting
In multi dimensional data fitting option one can get option to fit several parameters simultaneously, such as amplitude and energy transfer
or
fix FWHM of certain peaks

## Slide 32: Fitting QENS Data
A typical plot and results after fitting a QENS spectrum using FIM

## Slide 33: Fitting QENS Data
FABADA is used to fit QENS data obtained from IRIS instrument at ISIS.
There is no gain by using L=3 over L=2 for this QENS fitting
A. Vispa, D. Monserrat, G. J. Cuello, F. Fernandez-Alonso,S. Mukhopadhyay, F. Demmel, J.Ll. Tamarit, and L. C. Pardo, Phys Chem Chem Phys 19 20259 (2017)

## Slide 34: Fitting Neutron Compton Profile
Gaussian peaks are fitted using FIM for analysing data obtained from VESUVIO instrument at ISIS
N=3 is the better fitting for Al but not for Cu

## Slide 35: How Machine Learning can Help for High Throughput QENS
20 Q points
X 3 Lorentzian
X 10 temperatures
X 3 samples
= 1800 peak fitting
With sample changer our capacity has improved by three times
Required high throughput data analysis
Supervised learning ?

## Slide 36: Summary
Bayesian analysis is useful to analyse complicated data consists of several overlapping peaks, backgrounds and spurions.
FABADA algorithm has been implemented in Mantid to facilitate Bayesian analysis
The next step is to introduce machine learning using Bayesian methodology for high throughput QENS

## Slide 37: Outlook
Dealing with sparse, low-count-rate data in a statistically rigorous fashion
The definition of quantitative criteria for a systematic analysis of the information content (and associated correlation) of the underlying PDFs
The development of a library of models starting with those typically used for the analysis of QENS and Compton data
The use of genetic algorithms and machine learning to increase overall efficiency for high throughput data analysis

## Slide 38: Acknowledgements
Universitat Polit`ecnica de Catalunya and the UK Science & Technology Facilities Council for their continued support of this collaborative work
Mantid team at ISIS for helping the implementation
Friendly Users group of Molecular Spectroscopy for testing the implementation patiently
Thank you for your attention !