## Slide 1
Towards Pulsed Radiolysis Capabilities for the UK Science Community
Alex Baidak, Research Fellow
CLARA User Meeting, 05 July 2022

## Slide 2
Dalton Cumbrian Facility (DCF)

## Slide 3: Dalton Cumbrian Facility (DCF)
Delivers >10,000 hours radiation access per year
  inc. national programs for UK academics
  multiple access routes, many free at point of delivery
4 distinct sources of ionising radiation
  gammas, X-rays, ion sources
In-situ preparation, characterisation and analytical equipment
Highly competent professional support team

## Slide 4: X-ray cabinet source Precision MultiRad350
30 – 350 kVp
up to 140 Gy/min
turntable,
hypoxic chamber,
collimators,…
like sources in many labs
Henry Royce Institute funded

## Slide 5: DCF Facilities
2 NEC Pelletrons
  5MV Tandem (15SDH-4)
  2.5MV Single (7.5SH-2)
3 Ion sources
  TORVIS – high current proton & alpha
  SNICS – heavy ion source
  RF – gas plasma source (p, He, Ar, Kr, Xe)
6 Beamlines

## Slide 6: ‘6’ Beamlines
Line 1 – Hotcell for high proton dose radiation damage
Line 2 – Radiation chemistry with autoclaves
Line 3 – Flexible Radiation chemistry
Line 5 – Radiation Damage
Line 6 – Radiation Damage
Line 7 – IBA (PIXE, RBS, ERD, NRA)

## Slide 7: Need for Time-Resolved Technique
Problem: Characterisation of all irradiated systems at DCF is done “post-mortem” => early stage events remain obscure => a lot of mechanistic information is lost.
Solution: to do pulse radiolysis!

## Slide 8
Existing Challenges in Radiation Chemistry
Well studied.
???

## Slide 9
Pulse Radiolysis and Radiation Science
Primary species: identification and reactivity
(e-)aq: strong absorption band with lmax ~ 720 nm
Figure 1: Short-lived species in pulse radiolysis of water.
Notes: XPS X-ray photoelectron spectroscopy

## Slide 10
Pulse Radiolysis and Radiation Science
Kinetics and mechanisms of reactions
Diffusion-controlled reactions (or slower) – ns time resolution is sufficient.
Notes: XPS X-ray photoelectron spectroscopy

## Slide 11
Pulse Radiolysis and Radiation Science
Secondary intermediates & reaction mechanisms
Scavenging to produce secondary radicals:
eaq- + N2O → N2 + O·- (a1)
O·- + H2O → ·OH + OH- (a2)
eaq- + S2O82- → SO4·- + SO42- (b)
·H/·OH + HCO2- → H2/ H2O + CO2·- (c)
H2O → (e-)aq + (H+)aq + .OH + H. + H2 + H2O2
Notes: XPS X-ray photoelectron spectroscopy

## Slide 12
Pulse Radiolysis and Radiation Science:
Secondary intermediates & reaction mechanisms
Notes: XPS X-ray photoelectron spectroscopy

## Slide 13
CREDIT: J. Wishart’s ICARST 2017 talk

## Slide 14
CREDIT: J. Wishart’s ICARST 2017 talk

## Slide 15
CREDIT: J. Wishart’s ICARST 2017 talk

## Slide 16
CREDIT: J. Wishart’s ICARST 2017 talk

## Slide 17
CREDIT: J. Wishart’s ICARST 2017 talk

## Slide 19
Conclusion: Direct oxidation by H2O•+
might of importance to:
Radiotherapy and radiobiology
PUREX process
Interfaces in waste forms
Radiation-induced corrosion

## Slide 20: Ultra-fast electron-driven radiation chemistry in aqueous environments

## Slide 21: Ultra-fast electron-driven radiation chemistry in aqueous environments
A pump-probe experiment aiming at observing the time-dependence of creation of electrons (ionisation) and their subsequent solvation in a range of water-based samples. Calculations suggested the signal should be clearly visible with the available beam parameters. However, despite trying a wide range of samples, alignments and technique variations, no such signal was observed.

## Slide 22: Beamline upgrades
70 ns pulses – light ions + neutrons
Transient absorbance spectrometer
Donation, beam kicker Daresbury
Henry Royce Institute funded

## Slide 23
Radiation scientists in the UK need domestic ultra-fast (and even ns!) pulse radiolysis capability;
Scientific quality of existing research projects in radiation chemistry would benefit from direct studies of non-homogenous and ultra-fast chemistry:
Radiation synthesis of metal nanoparticles (NP) in solutions;
Metal NP in radiotherapy;
Radiation chemistry of nuclear fuel recycle (high concentrations of solvents);
Radiation chemistry of nuclear waste (extensive interfaces);
Biological systems (damage to DNA).
Pulsed proton source at DCF: to be developed.
Ultra-fast experiments with electron beams at CLARA.
Conclusion

## Slide 24: Acknowledgements
Staff at CLARA:
David Dunning and other members of the team.
Team DCF:
  Fred Currell, Andrew Smith, Ruth Edge, Mel O’Leary

## Slide 25
Thank You!
Aliaksandr.baidak@manchester.ac.uk
www.dalton.manchester.ac.uk