## Slide 1
Status of CLARA Phase 2 and Near Future Plans
Deepa Angal-Kalinin
On behalf of CLARA Team
Making a brighter future through advanced accelerators

## Slide 2
Overview
CLARA Phase 2
  Schematic
  Accelerator Hall
  FEBE Overview
  Installation and Infrastructure progress
CLARA and UK XFEL timeline
Summary

## Slide 3
CLARA Phase 2 - Schematic
Three 4 m long S-band Linacs, Variable Bunch Compressor, X-band lineariser, diagnostics sections.
FEBE design is conceived and developed in collaboration with stakeholders and is building upon the existing community interest and demonstrations on CLARA FE.
The design incorporates the means to combine electron bunches with high energy laser light and facilitate user research in novel acceleration.
Dedicated diagnostics pre- and post interaction point to fully characterise beams.
FEBE Arc
FEBE Hutch
250 MeV, 250 pC FEL ready bunches at 100 Hz

## Slide 4
Status 2022
CLARA 250 MeV - Accelerator Hall
Tested & installed 2021-22
Tested & ready for install 2023
BA1

## Slide 5
CLARA 250 MeV - Accelerator Hall Roof

## Slide 6
FEBE Design Overview
~250 MeV
Up to
600 MeV
Hutch footprint: 10×5.4×3 m3, Shielding: total beam power 6 W Flexibility with bunch charge (maximum 250 pC), bunch repetition rate (maximum 100 Hz), beam energy (250 MeV – 2 GeV)
Flexible compression arc + mask
Matching section
Laser insertion
Two interaction points
Post-interaction spectrometer line
Radiation shutters

## Slide 7
Two identical chambers: more flexible, provides diagnostic support, and a route towards ambitious interaction/transport/application
FEBE Hutch Overview

## Slide 8
Services in FEBE hutch are being finalised.
North Shield Wall Blocks Removed
FEBE Hutch – Services Planning

## Slide 9
View from South
FEBE Hutch – Services Planning

## Slide 10
Accelerator module construction & installation
Completion of 100TW Laser room complex
Electrical/mechanical services installation
Painting floors and bunker surfaces to allow clean installation
FEBE Laser Room on Roof
FEBE Laser Room and Rack Room 4 on Roof
Phase 2 Installation
Rack Room 4 on Roof
Phase 2 Preparation Progress (1)

## Slide 11
Phase 2 Preparation Progress (2)
Gun Modulator replacement progressing well. HRRG commissioning to begin in August 2022.
Linac 2 & 3 modulators tested to low RF power, testing to continue once Linac 4 is complete.
Deflecting cavity modulator currently undergoing RF test.
FEBE hutch ready for equipment and service installation
RF Room 1
Gun modulator replaced
RF Room 2
Linac 2 & 3 modulators
RF Room 3
TDC and Linac 4 modulator
FEBE Hutch

## Slide 12
Status 2023
CLARA 250 MeV - Accelerator Hall
Deepa Angal-Kalinin, Third CLARA User Meeting, 5th July 2022

## Slide 13
2022
2023
2024
2025
2026
2027
2028
2029
2030
2031
CLARA
UK XFEL
CDR: Options analysis
TDR
Construction
Machine Development and CLARA Exploitation
HRRG
SD1
SD2
Technical Beam FEBE
Commissioning
FEBE Laser contract begins
FEBE Exploitation kick off meeting
FEBE Laser ready for exploitation
Shutdown - Gun Modulator/klystron change
SD1
SD2
Shutdown - Phase 2 installation
CLARA & UK XFEL Planning

## Slide 14
Summary
CLARA is providing unique platform for developing skills & expertise in addressing several technical and scientific challenges for future UK XFEL & for novel user experiments.
Straight-on space is retained for accelerator technology R&D in support of UK XFEL.
Phase 2 will provide 250 MeV FEL ready beam – To reach design parameters sufficient time needs to be allocated for commissioning and machine development in first few years.
Provisions for spare components are being made to ensure increased beam availability. Plans are also underway to recruit dedicated operators.
FEBE user kick-off meeting will be arranged in 2024 before exploitation call will be issued but early engagement with CLARA team is encouraged.
FEBE experimental capabilities will be covered in Tom Pacey’s talk and FEBE laser plans will be covered in Ed Snedden’s talk.