## Slide 1
FEBE Experimental Capabilities
Thomas Pacey,
On behalf of CLARA & FEBE teams
ASTeC,
Daresbury Laboratory
3rd CLARA User Meeting, 5th July 2022
Notes: Welcome

## Slide 2: Outline
Overview CLARA Front-End & BA1
Overview FEBE beam delivery
FEBE infrastructure
FEBE Beam Parameters
Conclusions

## Slide 3
CLARA Front End Overview
RF Gun:
10 Hz
100 pC
PI Laser:
Fixed longitudinal pulse shape
Linac 1
TW Class Laser
BA1
Chamber
Front -End
C2V:
Fixed R56
Large T566
Nominal beam at BA1 IP:
35 MeV
100 pC (space charge limitation)
300 fs RMS length
100 um RMS radius
Plus other charge and bunch length setups!
CLARA
VELA
Notes: Where we are now

## Slide 4
BA1 Infrastructure
BA1 comprises of components from CLARA,ALICE,EMMA & SRS facilities
Equipment not designed to support user exploitation
Program of continuous improvement involving staff effort and capital investment
BA1 laser is > 15 years old. Intrinsic difficulties controlling some of the hardware. Challenge to sustain high performance during user run
Reflect on the sum being greater than the parts
Notes: Sum greater than the parts

## Slide 5: FEBE Overview
Shielded hutch specifically designed for user exploitation
Designed to support experiments from themes that have we have had in Run 1 (’18/19) and 2 (‘21/22) and more
Bespoke infrastructure, building on lots of lesson’s learned in Run 1&2
Take advantage of the full capabilities of CLARA with FEL quality beam
  synchronisation, modelling, controls, machine learning optimisation, etc
Notes: Run 1 and Run 2 – evidenced by new experiments in 2
Started to see benefits of CLARA with stability and feedbacks in Run 2

## Slide 6
CLARA & FEBE Overview
PI Laser:
Variable longitudinal pulse shape
Linac 1
RF Gun:
100 Hz
250 pC
CLARA
Phase 1
Notes: 400Hz Technological proof of concept

## Slide 7
CLARA & FEBE Overview
PI Laser:
Variable longitudinal pulse shape
Linac 1
Linac 2
Linac 3
Linac 4
Variable Bunch Compressor
Variable R56
Low T566
4th Harmonic
Cavity
Dechirper
RF Gun:
100 Hz
250 pC
CLARA
Phase 1
CLARA
Phase 2
Notes: 400Hz Technological proof of concept

## Slide 8
CLARA & FEBE Overview
PI Laser:
Variable longitudinal pulse shape
Linac 1
Linac 2
Linac 3
Linac 4
Variable Bunch Compressor
Variable R56
Low T566
4th Harmonic
Cavity
Dechirper
FEBE Arc
Variable R56
FEBE Mask
Flexible design
FEBE Hutch
FEC1
FEC2
100 TW Class Laser
FEBE experiments will benefit from:
Improved beam quality
Highly flexible beam delivery
Improved beam diagnostics & characterisation
RF Gun:
100 Hz
250 pC
CLARA
Phase 1
CLARA
Phase 2
CLARA
FEBE
Notes: 400Hz Technological proof of concept

## Slide 9
FEBE Design Principles
Flexible compression pre arc & Mask
Matching Section + diagnostics
2 Interaction Points
Post-IP spectrometer line
~250MeV
Radiation shutters
Laser
FEBE arc is designed to mitigate CSR
100 TW Class Laser is delivered from roof & coupled to beamline
Potential for PM dipole in the second chamber for broadband energy spectrum measurements.
Sliding shield door

## Slide 10
FEBE Hutch
Large hutch, 2 large chambers, Double IP, lots of diagnostics space!
Beamline loaded with diagnostics!

## Slide 11
Diagnostics
Arc, matching:
  Beam position monitors and YAG stations
  Beam arrival monitor
  CTR/CDR bunch compression monitor
Hutch:
  BPMs, YAG/OTR, ICT
  FEC2 diagnostics suite to be offered, shown right
Dump:
  OTR imaging station
  Faraday cup in energy spectrometer
Short permanent dipole magnets (drive/witness separation, low-res spectrometer)
OTR/YAG/collimator, dielectric streaker
Dielectric streaker cont.
Vertical screen (low-res spectrometer)
Placeholder for multiple additional diagnostics (to be defined)
Empty space, possible use for additional diagnostics
Illustrative only
Suite to be finalised

## Slide 12
FEBE Hutch
LASER In Periscope
LASER Out & Dump
CLARA
250 MeV
Up to
600 MeV
FEC#2
Can support PM Dipole
Chamber doors and feeds to be finalised
FEC #1
Laser focus
Primary IP
Notes: Chamber designs still to be finalised

## Slide 13: FEBE acceleration energies
Up to 250 MeV
>600 MeV
250 – 600 MeV
Accelerated beam charge and rep. rate subject to meeting radiation shielding power limits
250 MeV from CLARA linacs
Up to 600 MeV can be transported to FEBE Dump
>600 MeV can be generated, provided safely dumped in FEBE Chamber 2
Notes: ONE of the things is novel acceleration

## Slide 14: Examples of built-in infrastructure
Gas delivery lines and differential pumping designed in from ground up
Large stable chambers, big doors, can be used at atmosphere
Space outside chambers for in-vacuum antechambers or breadboards
Electron beam diagnostics suite in FEC2
Laser delivered to focus in FEC1
Notes: Non-exhaustive

## Slide 15: Beam parameters
Planned
Subject to change

## Slide 16
  Offered parameters to evolve, based on development time
  ‘Day 1’ → Nominal
Beam parameters
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5
RMS t [fs] | 100 | 50
σE/E [%] | <5 | <1
RMS x [µm] | 100 | 20
RMS y [µm] | 100 | 20
εN x @ 250 MeV [µm] | 5 | 2
εN y @ 250 MeV [µm] | 5 | 2
Important: all parameters to be confirmed through measurement using appropriate diagnostics.

## Slide 17
  Offered parameters to evolve, based on development time
  ‘Day 1’ → Nominal → R&D
Beam parameters
  R&D: dedicated effort required beyond standard operations, and/or new diagnostic technology required
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | <5
RMS t [fs] | 50 | ≤50
σE/E [%] | 1 | <1
RMS x [µm] | 50 | 1
RMS y [µm] | 50 | 1
εN x @ 250 MeV [µm] | <5 | 1
εN y @ 250 MeV [µm] | <1 | <1
Notes: PEAK current ~4kA simulated Max
Bad longitudinal profile and transverse profiles
~2kA seems workable in simulation

## Slide 18
R&D beam parameters: users interested in these beam options are encouraged to approach ASTeC with a view to research collaboration
Require level of ASTeC effort beyond standard CLARA operations
Flexibility in CLARA means we could potentially achieve exotic setups e.g.
  Longitudinal electron beam profile tailoring, including multi-bunch:
  Photo-injector laser pulse shaping
  FEBE mask
Beam parameters

## Slide 19: Beam parameters – take homes
Going to be better than in BA1
Subject to continuous improvement
Diagnostics will improve over time with R&D
Keep community informed of commissioning progress before “Day 1”
Want to hear from community about experiment ideas before proposal phase
Notes: Want to hear so we are confident our commissioning plans and priorities are aligned with community needs
No commitments to study or test ideas

## Slide 20: Conclusions
FEBE represents a step change in our infrastructure and potential to perform high impact experiments
Flexibility is at the heart of the design to support & futureproof for our community
FEBE will leverage the full CLARA R&D project
  FEL quality beam, synchronisation, modelling, controls, machine learning optimisation, etc.
Looking forward to commissioning and hearing new and exciting ideas from the community

## Slide 21: Backup slides

## Slide 22
FEC2 includes removable PM dipole spectrometer. Features include:
Diagnostics
  Broad bandwidth: 250 MeV – 600 MeV – >1 GeV
  Modular design: sections can be replaced if damaged, length reduced as function of energy
  Deflection of ebeam down, matched door panel for viewports/cameras
200 mm per module, up to 1000 mm total length
Simulated trajectories as a function of energy
Vertical (down) beam deflection

## Slide 23
FEBE arc mask
Vital component for beam driven acceleration (drive/witness)
5mm thick tungsten plate, x/y translation. YAG screen included at station.
Works with PI laser shaping & CLARA beam transport
Test mask to be installed on ‘Day 1’, design to be iterated based on commissioning.
Designed with ease of access in mind,
flexibility to change tungsten plate
x
ρ
100 mm vert. travel
+/- 10mm horiz. travel
Holes are
sketched
only

## Slide 24
x2 BPM, x1 screen per cell
  CSR ports on all dipoles
Mask at high dispersion point
Beam Arrival Monitor (BAM)
Coherent Transition Radiation Bunch Compression Monitor (CTR-BCM)
ICT
Before beam enters hutch we have timing, bunch length and charge
Diagnostics in Arc
YAG
BPM
YAG+MASK
BAM
ICT
YAG+BCM

## Slide 25
Diagnostics in hutch
X4 screens, up and downstream of chambers
X4 BPMS – entrance and exit, either side of FMBOX2 (centre of hutch)
Beamline ICT between FEC1 and FEC2
Beam axis, optics, losses all accounted for in hutch
BPM
Quad + Corr.
Quad + Corr.
YAG
FMBOX1
FEC1
FMBOX2
FEC2
ICT

## Slide 26
Diagnostics in dump line
YAG +OTR YAG screen for emittance measurement post experiment
  Low emittance/high brightness beams
Up to 600 MeV variable dispersion spectrometer + Faraday Cup
  Large Dia. YAG (98mm)
BPMs pre & post dipole
CSR extraction line on dipole
  Potential non invasive longitudinal diagnostic
Post hutch we have emittance, energy, energy spread, charge
YAG + OTR
Large Dia YAG
F-Cup