## Slide 1: LHCb Mighty Tracker and VELO mechanics and cooling
Oscar Augusto de Aguiar Francisco
on behalf of the Mighty tracker and VELO Upgrade UK groups
Future UK Silicon Vertex & Tracker R&D Workshop
Birmingham – UK
September 7th-8th , 2022

## Slide 2: LHCb Upgrade II
Smaller pixels with timing
Timing and better resolution
Better resolution
Low momentum tracking
Low momentum PID
high granularity inner region with timing
high granularity inner region and additional shielding
Mighty Tracker:
Silicon inner area + scintillating fibers
Focuses of this talk
Schedule
2021-2024: Research and Development phase
2024: Technical design reports
2024-2026: LHCb Upgrade Ib
2025-2030: (R&D+) Production phase
2030-2031: LHCb Upgrade II

## Slide 3: LHCb VELO Upgrade 1 (Mechanics/Cooling)
*only mentioning the UK contributions
Module production (talk)
Cooling (Oxford/Manchester)
Glueing, cabling and wire-bonding (Manchester)
Quality control (Manchester)
Detector assembly
Base (Oxford)
Detector mechanics (Liverpool)
Module Installation and testing (Liverpool/Manchester/Oxford)
Transport to CERN (Liverpool)
Commissioning at CERN
Metrology (Liverpool/Manchester)
Alignment and reconstruction (Manchester)
Credit: McCoy Wynne
Detector transport
Module production
Detector assembly
Detector installation
© 2022 CERN
credit: Amy O’Connor/STFC UKRI

## Slide 4: LHCb VELO Upgrade 2
Scenario A:
Similar layout to U1
5.1 mm distance to the beam
RF shield similar to U1
Possibility of module replacement (yearly) if modules can resist up to neq/cm2 (50fb-1)
Possibility of module replacement (yearly) if modules can resist up to 10^16 neq/cm2 (50fb-1)
Scenario B:
12.5 mm distance to the beam
much lighter shield (or no shield)
Smaller pixel (~42 with binary readout)
Smaller pixel (~42μm with binary readout)
Material before the second hit needs to be reduced (0.5% X0) to keep VELO U1 performance
neq/cm2 for 350 fb-1
10^16 neq/cm2 for 350 fb-1
Scenario A:
Scenario B:
Conceptual design VELO Upgrade II with small microchannels cooling plates and RF shield integrated to the modules

## Slide 5: VELO Cooling (Manchester/Oxford)
Smaller microchannel coolers to reduce the overall cost
More challenging to integrate (interface between pipes and coolers)
Cooling structure could be potentially re-used (NA62 talk)
Potentially better cooling performance
Potential collaboration Oxford and 3T (?)
Cheaper and more flexible design
Easier to integrate (cooling plant)
Another idea: integrated with high thermal conductivity materials (link)
Potential collaboration with Royce Institute (Sheffield) and University of Manchester (MECD - Mechanics department)
Simplified prototype
for early studies

## Slide 6: VELO RF shield (Oxford)
Carbon copper or aluminium composite to replace beam-facing section (or maybe all) of RF box
Tested prototypes:
Copper-Carbon Composite (0.07 mm total)
Aluminium-Carbon Composite (0.09 mm total)
Carbon copper or aluminum composite
Next steps: Optimization of the minimum Cu/Al thickness and impedance, Radiation tests
Ultra-thin
Merged primary/secondary volumes
Innermost region reduction in thickness from 150 um to 20-30 um
Kept under tension and moves with electronics
Next steps: Stress-relieving in the foil to allow cylindrical shape, tensile breaking load, baking, impedance
Could have the same radiation length as an ultra-thin aluminum shield
Main goal
Reduce the dominant contribution to the material budget before the second hit
*More information can be found here
Developed shape maintained in first ~100 mm from collar
Instrumentation end-collar
Single foil

## Slide 7: LHCb Upgrade II
Smaller pixels with timing
Timing and better resolution
Better resolution
Low momentum tracking
Low momentum PID
high granularity inner region with timing
high granularity inner region and additional shielding
Mighty Tracker:
Silicon inner area + scintillating fibers
Focuses of this talk
Schedule
2021-2024: Research and Development phase
2024: Technical design reports
2024-2026: LHCb Upgrade Ib
2025-2030: (R&D+) Production phase
2030-2031: LHCb Upgrade II

## Slide 8: LHCb Mighty Tracker
LHCB-TDR-023
Upgrade 2
Mighty Tracker = Silicon + Scintillating fibre
Upgrade 1b
(1080mm x 600 mm)
Upgrade 2
Geometry
2-3-4-5-5-4-3-2
Module
(528 mm x 200 mm)
Run 5 and 6
𝐿_𝑖𝑛𝑠𝑡=1.5×〖10〗^34 𝑐𝑚^(−2) 𝑠^(−1)
7.5 times higher than Upgrade 1 luminosity
Radiation up to MeV neq/cm²
Radiation up to 6×〖10〗^14 MeV neq/cm²
Sizeable radiation damage to the fibres in the inner region
High occupancy (up to 20%/fiber)
Solution
Scintillating fibres to cover most of the surface
UK institutes are involved with the development of the inner region based on silicon detector technology (HV-CMOS, Eva’s talk)
Schedule
An intermediate upgrade is being considered for the Run 4 (Upgrade Ib, 2025/26, purple region)
Fibres must be replaced in the inner region to keep same performance during LS3
Full geometry upgrade on 2031
Run 5 and 6
Solution
Scintillating fibres to cover most of the surface
UK institutes are involved with the development of the inner region based on silicon detector technology (HV-CMOS, Eva’s talk)
Schedule
An intermediate upgrade is being considered for the Run 4 (Upgrade Ib, 2025/26, purple region)
Fibres must be replaced in the inner region to keep same performance during LS3
Full geometry upgrade on 2031
*More information can be found here

## Slide 9: Layer Design
28 modules per layer
26 long modules and 2 short
Front and back of the modules are populated
~3 per layer (18 in total)
SciFi station
Silicon layers

## Slide 10: Cooling
Baseline solution based on polyimide tubes embedded in a carbon foam
The operating temperature is driven by the chip operation requirements ()
Several cooling options are being considered depending on the operation temperature
  Novec 649, Ethylene Glycol
  is not excluded but it would require metal pipes (additional material budget)
Carbon foam
Carbon fiber
Polyimide tubes

## Slide 11: On going activities in UK
Mechanics
Chip arrangement (Manchester/Imperial)
Mechanical support/integration (Manchester/Imperial)
Detector enclosure/Thermal insulation (Liverpool/Imperial/Manchester)
Mechanics/Thermal finite element analysis (Manchester/Liverpool)
Cooling
Small prototypes (Manchester/Liverpool)
Thermal performance studies (Manchester/Liverpool)
Carbon fibre integration to the carbon foam (Liverpool)
Samples assembly (Manchester/Liverpool)
Module assembly and metrology (Manchester/Liverpool)
Material Budget (RAL)
*only mentioning the UK contributions
Small carbon foam sample
40mm x 40mm x 2 mm
Insulation separation
Small prototypes
X/X0 = 0.845%-2.761%
Metrology
Cooling routing
Material budget

## Slide 12: Summary
LHCb VELO Upgrade 2
Mighty Tracker
Two scenarios with different cooling/mechanics implications
A: Modules 5.1 mm from the beam, High radiation (1017 neq/cm2)
B: Modules 12.5 mm from the beam, Lower radiation (1016 neq/cm2)
More strict material budget for a similar performance (U1)
R&D in cooling exploring 3D printing techniques
Focus on the inner region R&D based on silicon detector
Potentially replaceable modules due to high radiation
Single body 3D printed or with integrated smaller microchannels plates
R&D in RF shield to reduce the material budget contribution
Mechanical design and integration concepts well stablished
Cooling baseline solution based on polyimide tubes embedded into carbon foam
Assembly/cooling progressing from small samples to (sub-)module size
CO2 based solution as back-up plan depending on the final operational temperature
Material budget contributions well understood
Consolidation based on the mechanics/cooling optimization and services
Ultra-thin
Carbon copper or aluminum composite
Thank you for your attention!

## Slide 13: Backup slides

## Slide 14: LHCb SciFi: Fibre
Excellent talk presented last year (link)
The scintillating fibres are 250 um diameter
Charged particles excited the electrons in the fibre which decays in order of nanoseconds producing light (400-550 nm)
6 fibres layers are combined to create a module layer
CERN

## Slide 15: LHCb SciFi: Station
128 modules (50 cm by 5 m) are organized in the xuvx geometry in 3 tracking stations
  u- and v-layers are tilted by and respectively
  The position over y is estimate based on the x-layer and the stereo layers
Order of 1% per layer
Mirror at the around y=0 reflects the light back to the SiPM located at the top and bottom of the modules
Covers a large area (30 m2 per layer)

## Slide 16: LHCb SciFi (U2)
Main goal of the scintillating fibres R&D is the mitigation of the radiation damage
Silicon photomultiplier with reduced pixel area to minimize cross talk, minimize noise, lower dark current and shorter the recovery time
Micro-lenses recover light that would go to a dead area (+20% light yield)
Reduced number of fibre per detector plane (smaller cluster and lower material budget)
Cryogenic cooling (-150C) to reduce the SiPM noise by around 3 orders of magnitude with respect to Run 3

## Slide 17: LHCb Mighty Tracker (Performance)
In Upgrade 2 conditions:
Considering the Silicon and SciFi regions, an overall efficiency above of 90% and ghost rate below 30% is obtained using standalone algorithms for long tracks with momentum higher than 5 GeV
The silicon region brings improvements in the reconstruction efficiency and ghost rate. The ghost rate is expected to be significantly improve with algorithm optimizations
LHCB-TDR-023

## Slide 18: LHCb Mighty Tracker (Performance)
LHCB-TDR-023
The momentum resolution is dominated by the resolution over the bending plane (LHCb x axis)
Performance comparable with U1 is obtained with pixels with
The baseline pixel width brings an improvement up to 50% for high momentum long tracks
Smaller pixels are also important to distinguish different tracks in high occupancy areas

## Slide 19: Dead areas

## Slide 20: Cooling
Single phase allows operation at lower pressures
  Polyimide pipes (density: 1.42 g/cm2) suitable to relative low pressure (e.g.: water cooling, order of 1 bar or lower (ALICE ITS))
  Titanium pipes (density: 4.5 g/cm2) suitable to relative higher pressure (e.g.: CO2 evaporative cooling, safety pressure validation 183 bar (LHCb VELO/UT))
Polyimide offers a lower material budget compared to stainless steel or titanium tubes
Relatively smaller surface power dissipation per area compared to the other detectors
  ~1W/cm2 VELO U1 vs 0.16 W/cm2 MT CMOS
No need to install additional capillaries or orifices to equalize the flow distribution
Comparison of the material budget
(Ph.D Thesis M. G. Marzoa)

## Slide 21: Radiation length
Carbon Sheet
Flex tape
Silicon sensor
Carbon foam
Cooling tube
Wire
bonds
Service
Hybrid
More information can be found here

## Slide 22: LHCb Upgrade Schedule
Current: Upgrade I being finalised/commissioning
2017: Expression of interest
2018: Physics case
2022: Framework Technical design report
2021-2024: Research and Development phase
2024: Technical design reports
2024-2026: LHCb Upgrade Ib
2025-2030: (R&D+) Production phase
2030-2031: LHCb Upgrade II
Upgrade II
Now

## Slide 23: Mechanics
Carbon Fibre Mounting Frames
Inner station will require its on mechanical support and thermal insulation due to its operational temperature (0C or below)
Initial calculations indicate that an additional ~10% power due to the convection and radiation (amounting to a total of ~60kW for 6 layers)
A carbon fiber mounting frame will be required to provide the stiffness while the insulation will be provided by Armaflex or Airex. Further FEA studies are on going, to minimize the contribution from the insulation
Upgrade Ib layout