## Slide 1: ICS at FEBE
Alex Morris
University of Liverpool
29/09/2022
ICS - Inverse Compton Scattering
CLARA - Compact Linear Accelerator for Research and Applications
FEBE - Full Energy Beam Exploitation
Outline:
Summary of experiment
Electron Beam parameters
Laser parameters
Collimation of gamma beam
Gamma source parameters
Optical Cavities future work

## Slide 2: Summary of experiment
ICS experiment using the upgraded FEBE parameters at Daresbury Laboratory to produce a low bandwidth gamma source
Head on collision between a 250 MeV electron bunch and pulse from a Ti:Sapphire laser (800 nm) to produce 1.48 MeV gammas
Gamma source will be collimated to reduce the bandwidth
Initially the collimated number of photons will be reduced to ~1000 photons per interaction, therefore for a detector with ~0.1% efficiency there will be only 1 photon detected per interaction. This will allow us to fully characterise the source

## Slide 3: Electron Beam
CLARA accelerator & FEBE upgrade
Electron beam parameters
Angal-Kalinin, D. et al. (2020). Physical Review Accelerators and Beams, 23(4), 44801. https://doi.org/10.1103/PhysRevAccelBeams.23.044801

## Slide 4: Laser
Ti:Sapphire laser
Nd:YAG laser

## Slide 5: Collimation of Gamma Source
Gamma source will be collimated to reduce the bandwidth of the source and to reduce the flux before impinging on a detector 10 m away.
The flux is reduced so that a detector would not be saturated and single photons events can detected, ~1000 photons per interaction event (assuming an efficiency of detector of 0.1%). The detector will have an energy resolution of ~1 keV to characterise the source over many interactions.
Detector
Interaction point

## Slide 6: Gamma source parameters

## Slide 7: Optical Cavities future work
Optical cavities recirculate the laser pulses to store power in the cavity
Can be used to increase the effective repetition rate of the laser pulses
Joe Crone, thesis
Carstens, H. (2016). Enhancement cavities for the generation of extreme ultraviolet and hard x-ray radiation.