## Slide 1: LhARA IAB Review Accelerators and Technology WP3: Proton and ion capture
Christopher Baker
(on behalf of WP3)

## Slide 2: Capture work package
Holistic approach to project, with feedback and synergy
Take output from upstream components, laser source (see WP2), as input
Tailor beam as required for transfer line capabilities (see WP6) and end-station requirements (WP4, WP5)

## Slide 3: Beam parameters for Capture section
See WP2 & WP6 for details
 | Input | Output
Energy range | 0 – 20 MeV | 13 – 17 MeV
Divergence | 50 mrad | ~1E-6 mrad
Flux (proton no. / pulse) | 1010 | >109
Radius | <1 cm | <4 cm
Length | ~8ns | ~8ns
Repetition rate | 10 – 1000 Hz | 10 – 1000 Hz

## Slide 4: Capture system overview (see WP6)

## Slide 5: Simulations - Beam
Particle tracking
  BDSIM, GPT, VSIM
  Ideal behaviour, approximated, & simulated fields
HT Lau PhD Thesis Imperial College London (2021)

## Slide 6: Simulations – Plasma
Appl. Sci. 11 4357 (2021)

## Slide 7: Lenses - Magnetic field (solenoid)
Focussing strength proportional to magnetic field strength (current density)
Normal conducting or Superconducting options
  Non-trivial design – Windings, thermal, jackets, etc.
  Financially expensive – Materials, specialists
  Power intensive – Electrical and cooling
  Limited flexibility
  Well known technology
  Commercially available
Risk mitigation programme includes preliminary solenoid design efforts

## Slide 8: Lenses - Electric field (plasma), Gabor Lens
Focussing strength proportional to plasma density
  V. high E-fields (& hence focussing strengths) possible
    Dictated predominantly by applied voltages
Existing Gabor lens attempts use high-temperature discharge plasma
  Shot-by-shot synchronised with ion source
  Each plasma is quasi-stable
  Plasma established by limited control of initial conditions
  No known successful implementation despite many decades of effort
Proposed Gabor lens will take a different approach & build upon knowledge of equilibrated non-neutral plasmas

## Slide 9: Existing experimental lens efforts
Appl. Sci. 11 4357 (2021)
Proc. IPAC2016 TUPMY024
Ecloud ‘18 Proc. 143 (2020)
Phys Rev STAB 14 121301 (2011)

## Slide 10: Existing non-neutral plasma
Rw = 2.86cm
(Rp/Rw < 0.2)
1014 – 1015 m-3

## Slide 11: Existing plasma in ALPHA at CERN
Length ~ 10 cm
Radius ~ 0.5 mm (at 1T)
Density 1012 -1014 m-3
Phys Rev Lett 120 025001 (2018)
1013 – 1014 m-3

## Slide 12: Plasma parameters
 | Preliminary | Pre-construction | Final
Diameter | 1 cm | 3 cm | 3.5 cm
Plasma Length | 10 cm | 1 m | 1.2 m
Density | ~1013 m-3 | 5x1014 m-3 | 5x1015 m-3
Space-charge potential | 20 V | 2 kV | 50 kV
Focal length | 1000’s m | 10’s m | 1 m
B-field | 0.03 T | 0.1 T | 0.15 T
Iterative & parameterised approach in preliminary & pre-construction phases

## Slide 13: Plasma parameters
preliminary
final

## Slide 14: Current Apparatus (preliminary activity)
source
MCP/P-screen
Electrodes
Solenoid
B
28.1 cm
4.1 cm
source

## Slide 15: Proposed Apparatus (preconstruction phase)
~2m
B~0.1T
P-screen
source
Electrodes

## Slide 16: R&D Philosophy
Cautious approach
  Built upon decades long experiences
Iterative approach
  Confirm simulation methods & feedback into multiple designs & apparatus upgrades
  Vary single parameter (as far as possible)
    Analyse using Machine Learning due to correlations
  Confirm ‘known physics’ (scaling laws) in new apparatus

## Slide 17: Risks / mitigations
Being unable to create a suitable plasma:
  Density
  Size (radius, length)
  Timescales
  Possible technical/engineering solutions
    Utilise inbuilt redundancy – e.g. Increase confining fields, compartmentalise plasma
    Modify designs – e.g. Increase apparatus size
  Should be identified in simulations!

## Slide 18: Lens options
End of preconstruction phase report to provide recommendation
Why not implement magnetic from outset?
  Magnetic lens implementation as challenging as electric lens
  Electric lens lay some groundwork (magnet design)
  Limited magnetic vs. significant electric flexibility
  Significant lifetime cost savings using electric
  Significant technology transfer opportunities for electric

## Slide 19: Resources
Current ITRF Scoping project provides limited preliminary activity resources
  Enables profitable studies for preconstruction phase apparatus design
  Limited by one junior postdoctoral researcher
    Enough for 4 FTE personnel!
Existing apparatus at Swansea (& internationally) to be employed for studies
Existing international expertise employed for efficiency
Timeline identifies years 2, 5 (& 7) as critical
  Resource shortfall early can be recovered at later stage (at non-linear & higher integrated cost)

## Slide 20: WP3 Personnel
W. Bertsche
M. Charlton
S. Eriksson
T. Dascalu
J. Fajans
J. Wurtele
B. Bingham
R. Hugtenburg
J. Purden
A. Knoll
E. Bennet
PDRA, etc.

## Slide 21: Summary
Breadth of personnel & support to ensure success of work package
  Experimental, theoretical, medical, plasma, and accelerator physicists
  HPC and supercomputer engineering support
  Mechanical engineering support
No known fundamental issues foreseen
Decades of large project experience
Significant experience developing non-neutral plasma, and techniques, for both study and use
Recognise risks and challenges (and opportunities)
  associated with taking different approach
  associated with advancing individual non-neutral plasma aspects
  associated with combining many state-of-the-art aspects
  current non-ideal funding profile also increases overall risk

## Slide 22: Questions?

## Slide 23: Additional slides

## Slide 24: Storage
Rw = 1.27cm
(Rp/Rw<0.2)
1015 – 1016 m-3
Notes: Densities comparable to Gabor lens, but at shorter lengths!
20% fill factors
Stored ‘unchanging’ for days at ~kV, Tesla fields

## Slide 25: Interrogation & control
1014 – 1015 m-3
Notes: Densities comparable to Gabor lens, long lifetime (although unspecified, likely annihilation limited by cooling gas)

## Slide 26: Lifetimes (static)
Phys. Rev. Lett. 50 167 (1983)
Phys. Plasmas 1 1123 (1994)
Phys. Rev. Lett. 44 654 (1980)
Phys. Fluids 29 2015 (1986)
Rp/Rw ~0.2
Notes: Low density (~10^13 m^-3), low field (<kG), low pressure, low fill-factors (<20%)
Metre-lengths studied
Previously illustrated homogeneity improvement (somewhat uncharacterised) x50 lifetime

## Slide 27
Solenoid requirements
Equivalent field of a solenoid
1st solenoid most demanding
  Choose nominal design with 1 m long coil (Gabor lens flange-to-flange space is 1.157 m)
Solenoids 2 to 5
  Different design (for lower material cost, power consumption)

## Slide 28
Choice of material
Normal conducting
Superconducting
Very high current density compared to conventional conductors
Negligible power consumption
Complicated structure: rigid coil former + insulating cryostat (large space requirement around the coil)
The cryostat/cooling infrastructure needs careful maintenance
Cost of superconducting coils is significantly higher than the cost of conventional conductor
(Hollow copper conductor)
Very common design in many accelerator magnets
Efficient cooling
  water in direct contact with the source of heat
Coils potted in resin are typically very robust
Each cable has to be insulated
  adds complexity and requires more space
Weight of the coils is typically high
Cooling and electric circuits are interwoven, but need separation at the their ends
  pressure drop leads to complex cooling circuits for large coils + increased risk of water leakages
Aim of this design exercise: evaluate the requirements and performance of a normal-conducting solenoid that is suitable for LhARA

## Slide 29
SC solenoid for LhARA
Preliminary design and analysis (A. Beqiri)
Nb-Ti
2-stage cryo-cooler (45 W)
Coil: 1 m, 1.3 T, 250 A, 2 layers

## Slide 30
SC solenoid for LhARA
2-D magnetic and thermal model

## Slide 31
NC Solenoid–param. space

## Slide 32
NC Solenoid–Graded coil design
Use more than one transverse size for the copper cable
Increase the diameter of the cooling channel in the layers further away from the bore
  by keeping the conducting area constant
2 layers, cable size C
2 layers, cable size B
2 layers, cable size A
A
B
C

## Slide 33
400 A NC Solenoid
26 total layers
Graded coil
  3 types of cable
Each point is a different configuration with
  layers, cable type A
  layers, cable type B
  layers, cable type C

## Slide 34
NC Solenoid–2D FEMM Models
400 A
1000 A
2000 A
400 A
1000 A
coil
cover
Field on axis

## Slide 35
1000 A NC Solenoid–specifications
T
19 cm thick coil
925 kg
125 kW

## Slide 36
Simulation capabilities
The instability was observed in PIC simulations
Range of plasma lengths and densities limited by CPU time
Analytical model also available
Several critical parameters
  Number of electrons
  Plasma length and radius
  Plasma temperature
Plasma Simulations
(A) Diocotron mode

## Slide 37
Plasma Simulations
(B) Stable electron plasma
Simulation capabilities
Transverse/Longitudinal plasma profile
Can provide field maps for beam tracking
Simulation times limited to 10s of s
Plasma length
Plasma radial profile
Analytical models also available:

## Slide 38
Plasma Simulations
(C) Instabilities

## Slide 39
http://dx.doi.org/10.23732/CYRCP-2020-007.143
Aim: focus high intensity ion beams–improve focusing quality and reduce the emittance growth
(+ space-charge compensation)
GL tested so far:
>20 years of investigations in Frankfurt
“The formation of an electron cloud in the GL2000 is expected to take at least longer than in the previously investigated lenses.”
30 kV
50 kV
(rp=5 cm)
6 kV
6.5 kV
<30 keV Ar-, He- beams
<130 keV, 35 mA Ar1 beams

## Slide 40
Types of lenses at IAP, Frankfurt
O. Meusel, 2010
K. Schulte, 2006

## Slide 41
Beam transport measurements
1.2 mA, 440 keV, He+ beam
O. Meusel, HIAT2012
Lens filling degree
Beam emittance growth

## Slide 42
Beam transport measurements
He+ beam, emittance dominated transport (test performance of the lens as focusing device)
IPAC2013, THPWO021
GSI, 2012
aberrations

## Slide 43
Pulsed high-field solenoids
< 19.5 T, 2 or 3 pulses/min.
S1, S2: 40 mm bore diameter
14° half-angle geometrical acceptance
Measured transmission (18.6 MeV protons)
  50.6% (dual solenoid)
  28.6% (single solenoid)
Particle loss due to single solenoid
Limited aperture
Spherical aberrations (highly divergent protons travel closer to the windings)
GPT sim.
protons at source (251 MeV)
https://doi.org/10.1038/s41598-020-65775-7

## Slide 44
Active plasma lenses
1 mm-diameter Ar gas-filled capillary, 33 mm length
13 mm behind the tape drive target
transport efficiency through the APL (protons >1.5 MeV)
https://www.nature.com/articles/s41598-022-05181-3
APL
DOI: 10.1103/PhysRevLett.115.184802