## Slide 1
A Green Next Generation Ion Beam Analysis Facility
Dan Faircloth
Low Energy Beams Group Leader
Olli Tarvainen
Ion Source Physicist
STFC Rutherford Appleton Laboratory,
ISIS Neutron and Muon Source

## Slide 2
Ion Beam Analysis (IBA)
IBA uses MeV ion beams to measure elemental depth profiles in the near-surface layer of solids
The perfect tool for studying thin films and ion implantation technologies for:
            Microelectronics
            Opto-electronics
            Sensors
            Batteries
            Polymers (deuteration)
            Material modification

## Slide 3
RF ion source or
duoplasmatron
e.g. He+
5-8 bar SF6
sample
detector
high voltage terminal
Typical IBA Acceleration Schemes and Sources
MV
“single ended”
Very compact and hard to access ion source

## Slide 4
sample
detector
stripper
(gas cell or foil)
high voltage terminal
Typical IBA Acceleration Schemes and Sources
A zoo of difficult to use and unstable negative ion sources:
Caesium sputter
Charge exchange
Volume
e.g. H-
“tandem”
5-8 bar SF6
MV

## Slide 5
Large tanks full of high pressure SF6 requiring regular access

## Slide 6
SF6 is the most potent greenhouse gas known. It is 22,800 times more effective at trapping infrared radiation than an equivalent amount of CO2 and stays in the atmosphere for 3,200 years
1 kg SF6 “lost” = 23 tonnes of CO2
Approximate mass of SF6 in one IBA system = 50-500 kg
Approximate loss of SF6 each maintenance access = 3-50 kg
Between 1 and 10 maintenance accesses per year

## Slide 7
sample
detector
RF ion source or
duoplasmatron
e.g. He+
5 bar SF6
high voltage terminal
up to +5 MV
How to remove SF6?

## Slide 8
sample
detector
e.g. He+
How to remove SF6: An RFQ?
Pros:
Compact
Positive ion sources
High energy no problem
Variable frequency complex but allows variable energy
Cons:
Expensive
Uses 100’s of kW
Acknowledgement to Alan Letchford

## Slide 9
sample
detector
RF ion source or
duoplasmatron
e.g. He+
5 bar SF6
high voltage terminal
up to +5 MV
How to remove SF6?

## Slide 10
sample
detector
RF ion source or
duoplasmatron
e.g. He+
high voltage terminal
How to remove SF6: Air insulation?
MV ?

## Slide 11
FNAL 750 kV column
ISIS (NIMROD) 665 kV column
665 kV to 750 kV in approximately 2-3 m
SF6 still used in column!

## Slide 12
1 MV DC HV Platform for ITER NBI-
6.25 m high insulators
5 m clearance
SF6 still used in feed line!

## Slide 13
sample
detector
RF ion source or
duoplasmatron
e.g. He+
high voltage terminal
How to remove SF6: Air insulation?
MV systems are impractical without SF6

## Slide 14
sample
detector
e.g. Xe27+
high voltage terminal
By using high charge state ions the required accelerating voltage can be greatly reduced
How to remove SF6: Air insulation + high charge state ions
This approach obviously rules out using light ions, however ToF ERDA and material modification are still possible
+500 kV

## Slide 15
Time-of-Flight Elastic Recoil Detection Analysis (ToF-ERDA)
ToF-ERDA is a material characterisation method revealing the depth profile of the elemental composition of materials.
Example: metal tri-layer on silicon-oxide substrate
Many uses:
Electronic devices sensors
Functional surface coatings Catalytic surface chemistry Energy applications
Battery technology
etc.

## Slide 16
Time-of-Flight Elastic Recoil Detection Analysis (ToF-ERDA)
Best suited for light elements including H, Li, C, N and O.
These elements cannot be detected using photon-based (x-ray) methods.
Hydrogen is “invisible” to Rutherford Backscattering Spectrometry (RBS), which makes ToF-ERDA unique.
Simple principle:
Bombard the sample with heavy ions
Measure the velocity and energy of the recoiling particles
Use known energy loss in material to obtain depth profile
Lighter than beam particles are ejected, scattered beam
provides information on heavier elements.

## Slide 17
Time-of-Flight Elastic Recoil Detection Analysis (ToF-ERDA)
Time-of-Flight “gates” for timing signals –> recoil velocity
Gas-filled co-incidence
detector to measure
recoil energy
Elemental depth
profile including
impurities

## Slide 18
Typical low-energy ToF-ERDA ion beams
Beam | Energy
35/37Cl | 3 - 6 MeV
79/81Br | 8 - 11 MeV
127I | 9 - 16 MeV
The required particle flux at the sample is 1-10 pnA
Lower limit: Reasonable measurement time, typically less than an hour / sample.
Upper limit: The maximum count rate of the energy detector.

## Slide 19
Limit the platform voltage to 500 kV for an SF6 free design
Beam | Energy
35/37Cl | 3 - 6 MeV
79/81Br | 8 - 11 MeV
127I | 9 - 16 MeV
Ion | Charge state | Energy
40Ar | 6+ … 12+ | 3 - 6 MeV
84Kr | 16+ … 22+ | 8 - 11 MeV
136Xe | 18+ … 32+ | 9 - 16 MeV
1-10 pnA of
these charge states
we need
we need an Electron Cyclotron Resonance (ECR) ion source

## Slide 20
ECR Ion Source Magnetic Fields
Superposition of solenoid and sextupole fields

## Slide 21
Permanent magnet ECR ion sources
SUPERNANOGAN
DECRIS-PM

## Slide 22
1~5：PM rings
6, 7：soft iron rings
8~11：soft iron plates
12~14：auxiliary elements,
15：hexapole
16：coil
525 kg of PM material
Dubna ECR Ion Source

## Slide 23
Commercial permanent magnet ECRIS
Costs approx. £1M

## Slide 24
Permanent magnet CUBE-ECRIS
Quadrupole minimum-B structure with very simple PM array fulfilling so-called ECRIS scaling laws
160 kg of PM material

## Slide 25
Permanent magnet CUBE-ECRIS
CUBE-ECRIS
Electrostatic quadrupole doublet
m/q-analysis magnet
(4) Faraday cup
(5) Emittance scanner

## Slide 26
Permanent magnet CUBE-ECRIS
Argon charge state distribution with oxygen buffer gas
Charge state | Current [A] | Flux [pnA]
6+ | 21 | 3500
7+ | 18 | 2570
8+ | 25 | 3130
9+ | 14 | 1560
10+ | - | -
11+ | 1.5 | 140
12+ | 0.3 | 25
All argon particle fluxes > 10 particle nano-Ampere!
The CUBE-ECRIS ion source exceeds the IBA-concept requirement for 3-6 MeV argon.
Unpublished data

## Slide 27
Permanent magnet CUBE-ECRIS
Krypton (enriched 84-isotope) charge state distribution
Charge state | Current [A] | Flux [pnA]
17+ | 1.25 | 100
18+ | 0.73 | 40
19+ | 0.23 | 12
Krypton particle fluxes > 10 pnA for charge states < 19+
At the moment the CUBE-ECRIS ion source at
500 kV platform can reach 9.5 MeV
energy with krypton.
Already relevant for the IBA-application!
Unpublished data

## Slide 28
Permanent magnet CUBE-ECRIS
Xenon (enriched 136-isotope) charge state distribution
Charge state | Current [A] | Flux [pnA]
18+ | 4.9 | 270
19+ | 4.55 | 240
20+ | 2.7 | 135
21+ | 1.5 | 70
22+ | - | -
23+ | 0.5* | 22*
24+ | 0.2 | 8
Xenon particle fluxes > 10 pnA for charge states < 21+ and > 1 pnA for charge states < 24+
At the moment the CUBE-ECRIS ion source at
500 kV platform can reach 12 MeV
energy with xenon.
Already relevant for the IBA-application!
*Enriched 131-isotope
Unpublished data

## Slide 29
Permanent magnet CUBE-ECRIS
One possibility to increase the beam currents of high charge state Kr and Xe beams is to increase the microwave power.
The high charge state currents are power limited as shown here for argon.
Unpublished data

## Slide 30
Permanent magnet CUBE-ECRIS
One possibility to increase the beam currents of high charge state Kr and Xe beams is to increase the microwave power.
The high charge state currents are power limited as shown here for krypton (enriched 84Kr isotope).
Unpublished data

## Slide 31
Permanent magnet CUBE-ECRIS
One possibility to increase the beam currents of high charge state Kr and Xe beams is to increase the microwave power.
The high charge state currents are power limited as shown here for xenon (enriched 131Xe isotope).
Unpublished data

## Slide 32
CUBE-ECRIS
Electrostatic quadrupole doublet
m/q-analysis magnet
(4) Faraday cup
(5) Emittance scanner
Between 1-2 kW
burnt in the dipole

## Slide 33
Adjustable field permanent magnet dipole for charge state selection
Allows selecting charge states at ion source potential of  10 kV

## Slide 34
Physics design and simulation
Engineering design and assembly
Field measurement and validation
More details in Alex Bainbridge’s Talk

## Slide 35
Adjustable field permanent magnet dipole for charge state selection
Perfect match between simulation and
measured field with varying tuner position
Excelllent field uniformity radially across the magnet pole,
B/B < 5x10^-4 (the specification is 1x10-3)
This “net zero dipole magnet” has other applications:
Accelerator mass spectrometry
Isotope separation
More details in Alex Bainbridge’s Talk

## Slide 36
Novel ToF-ERDA accelerator concept – status and next steps
Beam transport tests with CUBE-ECRIS in 2023

## Slide 37
sample
detector
ECR ion source
e.g. Xe27+
500 kV high voltage platform
Novel ToF-ERDA accelerator concept – status and next steps
ToF-ERDA
Accelerating column

## Slide 38
Novel ToF-ERDA accelerator concept – status and next steps
500 kV high voltage deck and air-insulated acceleration column commercially available
www.pelletron.com

## Slide 39
Novel ToF-ERDA accelerator concept – status and next steps
Courtesy of Mikko Laitinen, University of Jyvaskyla
Modern ToF-ERDA tool, with state-
of-the-art hydrogen detection
efficiency and automation options
available for purchase from the
University of Jyvaskyla

## Slide 40
All building blocks for a green ToF-ERDA facility exist.
We plan to apply for funding for the next phase in 2023

## Slide 41
Opportunities for STFC and the UK?
National Thin Film Deposition and Characterisation Centre
(Proposed large-scale project on STFC priority projects list)
ISIS Materials Characterisation Laboratory
Surrey Ion Beam Centre and EPSRC
UK Accelerator Institutes (Cockroft and John Adams)
STFC is a unique organisation at the forefront of science and technology
STFC is the natural leader for this project
We have all the technical capabilities required

## Slide 42
Benefits Summary
Increased reliability and stability of the ion source
Reduced operational effort (turn-key system)
Reduced ion source maintenance effort
Reduced laboratory footprint of the equipment
Vastly reduced emissions
Reduced power consumption

## Slide 43
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 44
@STFC_matters
Science and Technology Facilities Council
Science and Technology Facilities Council
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.