## Slide 1
Reduction in wall-plug power for high power RF systems
Graeme Burt
Lancaster University

## Slide 2: Acknowledgements
This presentation will cover two key technologies to reduce the wall plug power required by RF systems, as part of two separate projects involving CERN and Lancaster
HE Klystrons
Igor Syratchev (CERN/ Project Leader), Nuria Catalan Lasheras, Zaib Un Nisa (CERN), Anis Baig (Lancaster), Jinchi Cai (UESTC)
FRT
Alick MacPherson (CERN/Project Leader) Nick Shipman, Amelia Edwards (Lancaster), Ilan Ben Zvi (CERN)

## Slide 3: High Efficiency Klystrons

## Slide 4: FCC-ee: Energy Conversion
Grid to DC:
RF power generation!
RF distribution!
losses in cavities
RF to beam
Note: largest impact by RF power generation
From E Jensen

## Slide 5
105 MW
Average RF power needs of the large-scale HEP Accelerators Studies.
The klystron efficiency impact on the FCCee power consumption.
Example of the efficiency upgrade from existing 65% to 80%.
Potential saving are 1.04 TWh in 10 years (84 MCHF in 10 years).
Reduced environmental impact (cooling and ventilation)
Reduced installation cost (stored energy in modulators).
Reduced maintenance cost (klystron life time).
R&D on increasing the useable efficiency is worth every penny/cent invested!
 | Klystron eff. 65% | Klystron eff. 80% | Difference
RF power needed for 3TeV CLIC | 105 MW |  | 
DC input power | 161.5MW | 131.25MW | -30.25MW
Waste heat | 56.5MW | 26.25MW | -30.25MW
Annual consumption (5500 h assumed) | 888 GWh | 721.9GWh | -166.1 GWh
Annual cost (50MCHF/MWh assumed) | 44.5 MCHF | 36.1 MCHF | -8.4 MCHF
Electricity installation dimensioned for | 161.5MW | 131.25 MW | -20.6%
CV installation dimensioned for | 56.5 MW | 26.25 MW | -53.54%
3.0 TeV CLICe+e- ; pulsed, 1.0 GHz, PRF total = 180 MW

## Slide 6
E field expansion in the drift tubes causes beam reacceleration when it leaves the output cavity.
Ohmic loses are proportional to the operating frequency.
Space charge depression is a partial conversion of the beam kinetic energy into the potential DC energy of beam traveling in the drift tube.
Bunch saturation is optimal, when all the elections populate only the useful RF phase bucket leaving the anti-bunch empty.
Bunch congregation is a normalized elections velocity spread along the bunch. It has an optimal value for every given bunch length.
Bunch stratification is a radial dependence of the bunch length and congregation. The ideal bunch should not have such a dependency.
Radial bunch expansion happens during beam deceleration in the output cavity in the presence of external solenoidal magnetic field.
Reflected electrons could be generated if some of the above effects are not balanced.
SLAC B-factory CW
0.478GHz, 1.25 MW
Factors limiting efficient RF power extraction
Efficiency 61%
Arrival plane
Driven by klystron general parameters.
Driven by RF design and space charge effects.

## Slide 7: New Klystron Concepts
How do we achieve bunch saturation? We cause the core of the bunch to oscillate while focusing the anti-bunch electrons slowly. There ae 4 ways to do this:
Bunch-Align-Collect (BAC): Using lots of RF cavities closely spaced
Core oscillation method (COM): Using the beams space charge forces
Core stabilization method (CSM): Using higher harmonic cavities
Two stage (TS): Making COM shorter by using a low beam energy and post-accelerating

## Slide 8: New Klystron Concepts
How do we achieve bunch saturation? We cause the core of the bunch to oscillate while focusing the anti-bunch electrons slowly. There ae 4 ways to do this:
Bunch-Align-Collect (BAC): Using lots of RF cavities closely spaced
Core oscillation method (COM): Using the beams space charge forces
Core stabilization method (CSM): Using higher harmonic cavities
Two stage (TS): Making COM shorter by using a low beam energy and post-accelerating

## Slide 9: New Klystron Concepts
How do we achieve bunch saturation? We cause the core of the bunch to oscillate while focusing the anti-bunch electrons slowly. There ae 4 ways to do this:
Bunch-Align-Collect (BAC): Using lots of RF cavities closely spaced
Core oscillation method (COM): Using the beams space charge forces
Core stabilization method (CSM): Using higher harmonic cavities
Two stage (TS): Making COM shorter by using a low beam energy and post-accelerating
2nd & 3rd harmonic cavities
Anti-bunch strongly focused

## Slide 10: New Klystron Concepts
How do we achieve bunch saturation? We cause the core of the bunch to oscillate while focusing the anti-bunch electrons slowly. There ae 4 ways to do this:
Bunch-Align-Collect (BAC): Using lots of RF cavities closely spaced
Core oscillation method (COM): Using the beams space charge forces
Core stabilization method (CSM): Using higher harmonic cavities
Two stage (TS): Making COM shorter by using a low beam energy and post-accelerating

## Slide 11
1/1.5D Wave-beam interaction module. Beam dynamic simulation (single beam and MBK).
Electro-Magnetic module.
Bunched beam generator module.
Simulation of IOT and output couplers with bunched beam
Coupled cavities module.
Special EM simulator of the coupled cavities with or without external loading. Coupled eigen frequencies and 2D field maps.
Monotron oscillations module.
Simulates the threshold of monotron oscillations in the RF cavities (klystron stability issues)
Klystron optimizer module.
Parameters scaling module.
KlyC: Large signal 1/1.5D klystron simulator [1].
Fast and accurate klystron simulation tools developed at CERN/Lancaster
Electrostatics module.
Magnetostatics module.
Electron beam tracking module.
CGUN (electron beam tracking)
[1] J. Cai, I Syratchev, G. Burt ‘KlyC. The 1D/1.5D large signal computer code for the Klystron simulations. User Manual. Version 6. (included CGUN for the 2D electron beam optics simulation).
CERN-ACC-2022-0008 ; CLIC-Note-1177, Link: https://cds.cern.ch/record/2812568?ln=en.

## Slide 12
Efficiency performance of the selected commercial klystrons and the new HE klystrons.
Project |  | Technology | Industrial partner
LHC 400 MHz, 350 kW CW | 70% *) | CSM | Thales
FCC 400 MHz 600 kW CW | 80% | TS MBK or CSM | Thales?
FCC 800 MHz 1.3 MW CW | 80% | TS MBK or CSM | Thales?
ILC 1.3 GHz 10 MW pulsed | 85% | TS MBK | Thales/Canon/CPI
CLIC 1 GHz 24 MW pulsed | 85% | TS MBK | Thales/Canon/CPI
X-band 8 MW pulsed | 57%*) | COM | Canon
X-band 50 MW pulsed | 70%*) | COM | CPI
36 GHz 2.5 MW | 35% | HOM MBK | On hold
Project |  | Technology | Industrial partner
LHC 400 MHz, 350 kW CW | 70% *) | CSM | Thales
FCC 400 MHz 600 kW CW | 80% | TS MBK or CSM | Thales?
FCC 800 MHz 1.3 MW CW | 80% | TS MBK or CSM | Thales?
ILC 1.3 GHz 10 MW pulsed | 85% | TS MBK | Thales/Canon/CPI
CLIC 1 GHz 24 MW pulsed | 85% | TS MBK | Thales/Canon/CPI
X-band 8 MW pulsed | 57%*) | COM | Canon
X-band 50 MW pulsed | 70%*) | COM | CPI
36 GHz 2.5 MW | 35% | HOM MBK | On hold
*) Means retrofitting an existing tube
Ultimate limit?

## Slide 13
 | E37113 at factory | E37117 design
Voltage, kV | 154 | 154
Current, A | 93 | 94
Frequency, GHz | 11.994 | 11.994
Peak power, MW | 6.2 | 8.16
Sat. gain, dB | 49 | 58
Efficiency, % | 42 | 57/ FCI
Life time, hours | 30 000 | 30 000
Solenoidal magnetic field, T | 0.35 | 0.4
RF circuit length, m | 0.127 | 0.127
VKX-8311A
Retrofit design
Re-used solenoid.
Re-used cathode
Increased power gain (10 dB)
Retro-fit High Efficiency (57%), 8 MW 12 GHz klystron (Canon)
HEX8
E37113
E37113
HEX8

## Slide 14: LHC CSM RF System – a 1st step for validation
A. Beunas: “Towards High Efficiency Klystrons for LHC”, FCC Week, Brussels, 2019
TH2167
TH2167HE
CST PIC Simulation: output cavity to collector
KlyC simulations
A. Buenas, I. Syratchev, J. Cai

## Slide 15: Fast Reactive Tuners

## Slide 16: FRT Concept
An Fast reactive Tuner (FRT) is a shorted co-axial structure containing a ferro-electric element
RF power flows into the FRT and is reflected back to the cavity
Voltage applied to the ferro-electric changes its permittivity
Permittivity change  Phase change of the reflected power  Cavity frequency change
Usually, the FRT would require its own port, although other arrangements have been proposed
Operates outside cryomodule at room temperature and does not mechanically deform cavity
Tuning speed measured at less than 600ns, limited by HV circuit
HV Line
RF Amplifier
Load
Circulator
FPC
FRT
FRT Antenna

## Slide 17: Use cases: microphonics suppression
For low beam loading machines RF power is dominated by microphonics
The effect of microphonics can be reduced passively or actively
  Stiffening of cavity
  Isolation of noise sources
  Active feedback e.g. piezo tuners
Residual microphonics require over-coupled FPC
Typically, RF power required is still many times larger than for critical coupling case
Decreasing QL

## Slide 18: Use cases: microphonics suppression
FRTs are an excellent tool for microphonics suppression
  High Tuning speed ~600ns measured limited by external HV circuit
  No excitation of mechanical modes
  Simple transfer function/negligible phase delay at frequencies of interest
Peak and average RF power reduced by and respectively
Increased dielectric and conductor losses at higher RF frequencies reduce effectiveness
FRTs can be combined with other suppression technologies
  E.g. piezo tuners
Estimate FRTs could still beneficial up to ~2-3 GHz
  Not experimentally verified
Case study: RF power for PERLE vs QL with and without FRT
Estimated FRT FoM vs RF frequency

## Slide 19: Microphonics suppression results
Lower order Mode of UK4R crab cavity at 374MHz
  Very stiff  very low levels of microphonics  used vibration generator
Euclid designed prototype FRT
No slow tuner  operated in SEL mode
Chiller, phase shifter, vibration generator
Deliberately simple purely integral feedback used
  More performant solutions surely possible
FE-FRT temp.
Bath temp.
regulation on
bunker opened
Euclid FE-FRT prototype
Temperature regulation with chiller
UK4R on insert
Phase shifter on top plate
Vibration generator

## Slide 20: Microphonics suppression results
Vibration generator set to 37Hz
Spectral density also shows good suppression at higher frequencies e.g. ~600Hz
Peak deviation with correction 1.2Hz
N.B. long transmission line, lossy brazing
  Low FoM
  Little to no RF power reduction
F
No correction
With correction

## Slide 21: Use cases: transient detuning
RF Amplifier
Load
Circulator
FPC
FRT
FRT Antenna
HV Line
Beam + fixed detuning

## Slide 22: Use cases: transient detuning
RF Amplifier
Load
Circulator
FPC
FRT
FRT Antenna
HV Line
Beam + transient detuning

## Slide 23: Conclusion
With better cavity tuning and improved klystron efficiency significant reductions in the required wall-plug power to drive RF systems can be achieved
Klystron efficiency can be improved by an additional 10-15% which could reduce the power need of a collider by 166 GW-hr per year (100 times the yearly output of the solar cells in the DL car-park)
Fast reactive tuners can reduce power demands
  for low beamloading machines by reducing the overhead needed for microphonics
  For machines with reactive beamloading by switching the frequency during abort gaps