## Slide 1
Radioactive Waste in a Sustainable Accelerator Facility:
Lessons from ISIS
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
>30,000 particle accelerators in world
Notes: To edit the background image, select ‘Format’ from the PowerPoint menu and ‘Slide Background’ from the drop-down menu. Within the new list of options that appears on the right of the screen, select the ‘File’ button under ‘Insert picture from’ and select your image from your file browser. Please remove or amend the image credit if you are using a different image to the one provided.

## Slide 5
Notes: To edit the background image, select ‘Format’ from the PowerPoint menu and ‘Slide Background’ from the drop-down menu. Within the new list of options that appears on the right of the screen, select the ‘File’ button under ‘Insert picture from’ and select your image from your file browser. Please remove or amend the image credit if you are using a different image to the one provided.

## Slide 6
Formation of Radioactivity
Electron Accelerators
Not (usually) significant < 13 MeV
radioactivity from secondary photo-nuclear interactions
Generally less significant than proton accelerators
Proton/ion Accelerators
Threshold reactions can occur at almost all energies
- activation of accelerator
At higher energies, spallation and neutron production starts
- activation of surrounding material
Complex nuclear reactions and nuclear cascades form radioactivity
Long lived radionuclides are relevant for waste management

## Slide 7
Scale of Radioactivity
Radioactivity is measured in
disintegrations per second, Becquerel (Bq)
Hazard is measured in
Sieverts (Sv)

## Slide 8
Impact of Regulation
Highly regulated sector
Large differences between national regulation and policies
Optimum solutions will be different for different nations
Germany
  Strict and proscriptive regulation system
  Risk based approach allows for controlled recycling of radioactive waste
  France
  Zoning system
  Waste from specified zones always radioactive, regardless of activation
  UK
  Strict, but goal setting system
  Does not allow recycling of radioactive waste
Notes: Replace this guidance text with your own bullet pointed content.
For further guidance please see https://www.bdadyslexia.org.uk/advice/employers/creating-a-dyslexia-friendly-workplace/dyslexia-friendly-style-guide

## Slide 9
Low Activity
Low Level Waste
(LA-LLW)
Higher Activity
Waste (ILW/HAW)
Activity
Quantity
of Waste
“legally not
Radioactive”
Lemon &
Herb
Mild
Low Level
Waste (LLW)
Hot
Extra Hot
Scale of Radioactive Waste
Recycling
Specialist Landfill
National Repository
Geological Disposal

## Slide 10
Prevent
Recycle
Reduce
Reuse
Dispose
Environmental
Legal duty to apply Best Available Technique (ALARA) to minimise
  Volume
  Activity
  Harm
Everything above free-release limit either;
  Treated get below free-release limit,
  Buried in the ground, or
  Stored in specialist facilities
  Solid waste must be isolated from human environment
  Primary harm is lost resource, not radiation

## Slide 11
Social: Public Perception
National & Local Policy
Regulation
Organisational Culture
Often outweighs Economic and Environment considerations
Consequence
Very low limits for recycling or reuse
Poorly optimised regulation
Slow decision making
High Costs

## Slide 12
Low Activity
Low Level Waste
Intermediate
Level Waste
Mild
Spicy
Low Level
Waste
Hot
Hell
Recycle Profit
£100/te –
£8,000/te
Landfill
~£2,000/te
LLWR
~£10-20,000/te
ILW
>£1,000,000/te
Economic: Cost
Waste Category | Current Volume | Disposal Cost
LA-LLW | 1,140 te | ~ £2.2 M
LLW | 100 te | ~ £1.5 M
ILW | 70 te | ~ £ 70 M
What would it cost to dispose ISIS current waste right now?
This is just disposal cost
“legally not
Radioactive”

## Slide 13
Economic: Capacity
Accelerators can generate some highly active hazardous wastes
ISIS lacks capability to retrieve, sort, size reduced package and immobilise our higher activity wastes.
UK lacks capacity for disposal
  GDF in early planning stages
Waste must be safely store for ~20-90 years
  GDF schedule 2040 - 2108

## Slide 14
Radioactive Waste at ISIS

## Slide 15
Lifetime Radioactive Waste
Typical Medical LINAC | ~0.3 tonne 1
Typical PET Cyclotron | ~100 – 500 tonnes1
ISIS Neutron Source | ~40,000 tonnes2
European Spallation Source | ~60,000 tonnes3
UK Nuclear Station | ~30,000 – 60,0000 tonnes2
Total Forecast UK Radioactive Waste | ~5,000,000 tonnes2
1 – IAEA NW-T-2.9, Decommissioning of Particle Accelerators, 2020 2 – UK Radioactive Waste Inventory, 2022 (Approximations converted from m3) 3 – Decommissioning Plan for European Spallation Source, EPJ Web of Conferences 153, 05022 (2017)
There are over 30,000 particle accelerators in the world
ISIS radioactive waste
150 – 300 tonnes of radioactive waste per year
~30,000 – 35,000 tonnes decommissioning
Notes: To edit the pie chart data. Click on the chart, Chart design, and choose select data or edit chart data in excel.

## Slide 16
Accelerator operation started at RAL in 1950s
ISIS started operation in 1984
By 2017 reached a peak on site of
        ~2,500 tonnes radioactive waste
    ~40 PBq waste
    Waste not sustainably managed!
ISIS Waste Problems

## Slide 17
Focus on waste reduction started in 2017
Build capability & facilities
Develop methods
Improve standards and culture
Dispose of waste legacy
Establish sustainable waste management systems
To date disposed of 65% of the legacy waste
Average ~100 tonnes/a (60%) diverted to recycling
Waste Reduction
Chart: 
| Reuse/recycle | Landfill | Incineration | Other
 | 115 | 72.0691 | 3.694 | 0.2111

## Slide 18
Investing in remote handling infrastructure
Will provide a long term (sustainable) capability to segregate, characterise and package higher activity wastes
Support ISIS maintenance and re-use of highly active components
Waste Remote Handling

## Slide 19
Lessons to Learn
Understand what you expect to generate
Plan and mange through the full lifecycle
Minimise
Segregation
Processing
Storage
Disposal
Adequate facilities
Plan for site legacy after operation

## Slide 20
Segregation
Separation of non-active or low active materials
Separation of material types
Design for segregation
Characterisation
Careful measurement allows release of materials for recycling
Decay Storage
Storage until short lived radionuclides have decayed
Minimise Beam Loses
Reduces incidental activation of materials
Minimise, Segregate & Divert Waste
Material Selection
Choosing the right materials minimises long lived activation
Plastic / Wood
Aluminum
Iron / Steel
Stainless Steel
Increasingly Challenging Nuclides

## Slide 21
  Decay storage is powerful tool
  Our regulators limit ISIS to 7 – 15 years storage, depending on material
  Challenges to consider
  Space
  Facilities
  Hazard
  Future Commitment
Decay Storage
Chart: Decay Time (Years)
| 0.1 | 0.2 | 0.3 | 0.5 | 0.7 | 0.9 | 1 | 2 | 3 | 5 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 300 | 400 | 500 | 600 | 700 | 800 | 900
Fraction | 0.96999 | 0.94114 | 0.91338 | 0.86095 | 0.81228 | 0.76702 | 0.74556 | 0.56636 | 0.43526 | 0.26202 | 0.077305 | 0.060908 | 0.048089 | 0.038054 | 0.030189 | 0.024017 | 0.019165 | 0.015344 | 0.012331 | 0.009949 | 0.0080619 | 0.003038 | 0.0013247 | 0.00038578 | 0.00016514 | 8.7166e-05 | 5.2647e-05 | 3.5402e-05 | 2.6201e-05 | 2.1119e-05 | 1.826e-05 | 1.6635e-05 | 1.5704e-05 | 1.5167e-05 | 1.4854e-05 | 1.4668e-05 | 1.4555e-05 | 1.4482e-05 | 1.4434e-05 | 1.4399e-05 | 1.4371e-05 | 1.4348e-05 | 1.4202e-05 | 1.4031e-05 | 1.3863e-05 | 1.3696e-05 | 1.3531e-05 | 1.3369e-05 | 1.3208e-05
Typical decay curve for ISIS activated carbon steel
  Median time for ISIS steel to decay for recycling;
  LA-LLW = 15 years
  LLW = 50 years
  ILW = 3,500 years

## Slide 22
Setting a Challenge: Shutter Design
Highly activated
TS1 Shutter ~9 tonnes
TS2 shutter ~3 tonnes
Don’t have a disposal solution
Potential £millions per shutter
Not uniformly activated
Opportunities
  Material selection?
  Ease of disassembly?
  Re-use shutter?

## Slide 23
ISIS TS1 Project
  Target Services Area
  Forecast 192 packages
  Created 189 packages
  Disposal achieved <18 months
  Success due to…
  Prior planning
  In-situ
    - segregation
    - packaging
    - sampling
    Co-operation between waste and project teams
    Facilities and capability

## Slide 24
@ISISNeutronMuon
isis.stfc.ac.uk
STFC
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.