## Slide 1: Medical Instrumentation for LhARA
Narender Kumar

## Slide 2: Overview
Motivation and clinical benefits of Hadron Therapy
Background and R&D
Measurements at UoB's Scanditronix MC40 cyclotron
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 3: Hadron beam therapy
Clear healthcare benefits for certain cancer types;
Significant investment through NHS and private facilities in the UK;
Optimization of Medical Accelerators (OMA) network identified key R&D challenges:
  Significant time goes into Q&A
  New technology solutions needed for novel treatment modalities such as FLASH, LhARA
  Desirable machine operation modes not currently possible due to lack of non-invasive (online) diagnostics
CNAO Synchrotron, image courtesy CNAO.
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 4
Diagnostics for proton beam overview
*A. Smith et. al. Med. Phys. 36, 2009
Measure beam properties in an accelerator:
  Current, position, profile, emittance, energy
Treatment beam measurements:
  Dose
  Dose profile
Beam monitors and position in M.D. Anderson proton beam nozzle*
Deliver the prescribed amount of dose to the target location!!
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 5
SEM Grid
Faraday cup
Credit: B. Walasek-Höhne, GSI and G. Kube, DESY
Still the Golden standard for online dose monitor!
Ionisation chambers
Advantages: Robustness, uniformity, easiness of operation, minimal perturbation
IC array: Dose distribution, spatial resolution is not great (5-8mm)
Multi layers IC: Check the beam range, energy, and stability
Scintillating screen
Diagnostics for proton beam overview
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 6
Medipix3
Collaboration with ASI & Nikhef, Netherlands
Medipix3 & EBT3 film comparisons
Medipix3 is a CMOS pixel detector readout chip.
Colour imaging and dead time free operation
First tests with Medipix3 detector in a clinical proton therapy environment
  High proton flux (~10^10 ions/s)
EBT3 Gafchromic films
Result from EBT3 film
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 7: Existing diagnostics
High resolution
Reliability
Validity
Interceptive
Ongoing calibration
Beam perturbation
Limited live feedback
B. Walasek-Höhne, GSI and G. Kube, DESY
S. Giordanengo & M. Donetti, arXiv:1803.00893
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 8: Gas Jet Monitor - Novel diagnostics solution
No beam perturbation
Online monitoring
Superior error detection
1
Minimally invasive
Enabling technology for FLASH and Mini-Beam treatments
Active machine regulation based on live feedback becomes feasible
3
Novel treatments and improved operation
No mechanical parts interact with the beam
All key parameters monitored remotely
Significantly reduced maintenance
2
Significantly reduced calibration time
1
2
3
USP
N. Kumar, C.P. Welsch, et. al, Physica Medica 73, p 173-178 (2020).
S. Jolly, C.P. Welsch, et al., “Technical challenges for FLASH proton therapy“, Phys Med 2020 – Galileo Galilei Award, best paper in 2020
“Non-Invasive Gas Jet In-Vivo Dosimetry for Particle Beam Therapy”, contributed talk at IPAC21
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 9: Building up on previous developments
Gas jet shaping
MCP
Phosphor screen
Detector
Ionization
Ion extraction
Visible light
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 10: Capitalizing on pioneering STFC-funded technology
Nozzle Chamber
Skimmer Assembly
Gas Separator
Skimmer Chamber
Third Skimmer
Imaging System
Interaction Chamber
Moveable Gauge Chamber
Dump Chamber
~3 m
“Gas jet monitor R&D is world leading” – CI SAC (2019)
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 11: Different setups at the Cockcroft Institute
Monitor for keV beams
HLLHC prototype
HLLHC working instrument
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 12: Measurements with protons at UoB MC40 cyclotron
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Beam Parameters
Beam Species: Protons
Beam Energy: 28 MeV
Beam Current: 150-750 nA (on FC1)
Beam Collimator Area: 4-100 mm2
Interaction chamber
125 µm
Ti foil
125 µm
Ti foil
Beam
dump
Proton
beam
(in vacuum)
Beamline
(ending with Ti foil)
Proton
beam
(in vacuum)
Proton
beam
(in air)
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 13: Measurements with protons at UoB MC40 cyclotron
Beam collimator Area= 100 mm2
Integration time = 1second
Gas Pressure in Interaction chamber = 1.2 ×10-5 mbar
σ = 5.4mm
Beam current at FC1= 150nA
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Beam collimator Area= 4 mm2
Integration time = 20seconds
Gas Pressure in Interaction chamber = 1.2 ×10-5 mbar
σ = 6.4mm
Beam current at FC1= 150nA
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 14
Simulation Results
GEANT4 simulations
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 15: Updated design
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Nozzle Chamber
Skimmer Chamber
Interaction Chamber
Port for Laser Interferometry measurements
More flexible design for nozzle skimmer assembly and tuning
Compact system: total length ≈ 1m
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 16
FZP-based QuantumJet: STFC IPS FOF
UHVD Collaboration
Key Features
  Sub-mm gas jet
  Analogous to wire scanner
  Using FZP as central element
  Profiling of high intensity beams
Work in Progress
  Chamber and holder designed for FZP
  Experiments were conducted using pinholes
  Pinhole size varies from 1mm to 50um
  Next step is to test the FZP (atom sieve)
  Test has started from 03rd Oct. 2022
Illustration of Fresnel Zone Plate used for the generation of focused quantum gas jet
Second Skimmer
Gas Jet
Quantum Gas Jet
Fresnel Zone Lens
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 17
Measurements Results
Beam profile images obtained for various pinholes diameters: (a) 500µm, (b) 200µm, (c) 100µm and (d) 50µm. The integration time for each image is 6, 9, 30 and 300 seconds respectively
X beam profile obtained for various pinholes diameters: (a) 500µm, (b) 200µm, (c) 100µm and (d) 50µm
Y beam profile obtained for various pinholes diameters: (a) 500µm, (b) 200µm, (c) 100µm and (d) 50µm
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 18: Summary
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Advanced instrumentation is key to maximize benefits from proton/hadron beam therapy;
Clearly identified clinical benefits – reduction of QA time, giving medical experts additional safety during treatment;
Significant challenges remain for advanced treatment modalities such as FLASH or the LhARA initiative: There are no solutions at the moment for high dose treatment, high spatial and time resolution. This needs comprehensive R&D between leading academic and clinical groups.
NOVEL END-STATION DEVELOPMENT: CONSULTATION 1; 14th Dec. 2022

## Slide 19: Thank you for your attention
Special thanks to
I. Maltusch, O. Stringer, J. Wolfenden, H. Zhang, T. Price, C.P. Welsch, J. Yap