## Slide 1: EPAC Compressor
ISTAC Meeting, December 2022

## Slide 2: Compressor Overview
Objective
Routinely compress EPAC pulses to 1 PW without introducing degrading effects to the laser pulses for experiments.
Pre-compressor.
  3-colour CW alignment + pilot beam
Beam expansion to 220mm.
Chamber and Opto-mechanics.
Compressor Optics.
Post-Compressor Diagnostics.
  Pulse duration, contrast, near-field, far-field, darkfield, wavefront, spectral phase.
1
2
3 & 4
5
Pulse energy out | 30 J
Pulse duration | ≤ 30 fs FWHM
Pulse repetition rate | 10 Hz, 1 Hz, Shot on demand
Input beam size | 220 mm FWHM
Input beam shape | Circular, super-Gaussian
Transmission Bandwidth | 750 – 860 nm

## Slide 3: Compressor Chamber
Installation method covered in “Installation status and forward plan” talk later today.
Resin Base
Floor Plate
Breadboard
Strengthening
Rib
Loading Rail
Detailed analysis and manufacture awarded to Added Value Solutions, they provided Vulcan OPPEL compressor chamber and ELI-NP and ELI Beamlines target chambers.
Breadboard and breadboard supports isolated from chamber structure to minimise optic movement.
Chamber delivery scheduled Oct-23
Formed of 2 sub-compressors in an L-shape design.
Notes: An order for the compressor chambers & flexible inter-connection has been placed with AVS of Spain who specialise in equipment for the Science & Space markets. They offer a design, analysis, manufacture & test services which should ensure a well-integrated package when complete.
The manufacturing design is nearing completion, the overall structure & appearance are close to the original proposed design concept, some changes are necessary based on the structural design analysis results.

## Slide 4: Compressor Grating Mounts
Better than 2 μrad pointing stability is required from the grating mounts.
VOPPEL Grating Mount Testing: achieved <0.5 μrad stability and 0.2 μrad resolution.
This mount is compatible within the current EPAC chamber space. A future revised design will consider thermal performance and grating cooling capability.
Optical Diagnostic
VOPPEL/EPAC Grating Mount
Encoders
Optical encoders used in closed-loop for precise and accurate motion.
Optical diagnostic projected a 120mm beam onto a mounted mirror. This is retro-reflected back to a position sensitive detector (PSD).
Notes: The optic mounts lower stages will be a modified version of the Voppel mounts which in testing have shown to be a stable platform for both mirror & grating operation.

## Slide 5: Compressor Gratings
Apertures | 300 x 300 mm , 760 x 300 mm
Line density | 1480 lines / mm
Incidence angle | 37.24° (Littrow), 10° out-of-plane.
Peak fluence @ 1PW | 80mJ / cm2 (30 fs)
Requirements:
Efficient diffraction, >90% per grating for 750-860 nm.
High damage threshold. Tested and proven > 200mJ / cm2 LIDT in vacuum for long-term 1 PW, 10 Hz.
Minimal deformation. Optic sag (gravity) + Thermal Expansion (1PW, 10Hz) < 80 nm.
  Modelling capability.
  Engineering solutions. Passive/active cooling.
  Thermal expansion induced by laser absorption from the grating coating.
Ongoing optic/engineering challenge.
G3
M1
G4
G1
G2
50 J In
30 J Out

## Slide 6: Grating Options - 1
2. Hybrid (Gold + dielectric). DISCONTINUED
  Plymouth Grating Laboratory (PGL) investigated a gold grating with multilayer-dielectric (MLD) overcoat.
  96% diffraction efficiency (modelled) + 2.7% absorption.
  Aspect ratio of dielectric fins too narrow and unstable.
Etched Glass Grating + Gold Overcoat | 
Supplier | Diffraction Efficiency
PGL | 94% modelled
LLNL | 93.8% modelled, 91.5% measured
JY Horiba | 
LLNL also produce Chrome/HfO2 grooved sublayer with + Au overcoat:
94.3% efficiency measured.
ELI-Beamlines, L3-HAPLS Gratings
1. Gold.
  ~4.9% absorption. Previous modelling indicated active cooling is required for 10 Hz operation.
  (Uncooled) CLF Gemini observed white deposit over time. RF cleaning was applied when efficiency dropped to <80%, recovering to ~90%.

## Slide 7: Grating Options – 2
3. Multi-layer dielectric (MLD).
  PGL also developed for the CLF a new coating to work at the EPAC diffracted + out-of-plane angle. A highly-reflective interference coating is laid with a thick SiO2 top layer for the grating to be written.
  98% diffraction efficiency (modelled)
  <<0.01% absorption modelled
Four 50 mm aperture MLD test samples manufactured
Test sample(s) LiDT and diffraction efficiency investigated

## Slide 8: MLD: Diffraction Efficiency
Modelling indicated <0.01% absorption in the coating layers and an efficiency minima at 725nm, outside the EPAC laser bandwidth.
PGL measurement
Additional 3.5% output energy loss.
Manufacturability question over short wavelength DE for 50 mm samples.
  Recently commissioned CLF Gemini MLD gratings DE correctly centred at 800nm, with an absorption peak at 743nm.
  PGL is performing some modelling to understand the source of error and methods to monitor & correct during coating.
Measurements of the DE has highlighted an absorption peak at 750nm, verified by narrowband power measurement at this wavelength.
Notes: Significantly narrower bandwidth capability, with rapid fall off

## Slide 9: MLD LIDT Testing (Lidaris)
Further assessment required at 1M-on-1 (underway) Raster scan 10,000-on-1 (underway)
Measured: 360 mJ/ cm2 catastrophic LiDT,
89 mJ / cm2 ‘colour mode’ LiDT
Colour Mode Damage
Catastrophic Damage
370 mJ/cm2,
damage after
16 pulses
164 mJ/cm2,
damage after
10,000 pulses
Impact of colour mode damage on compression and efficiency poorly understood.
A test sample was characterised at an LiDT facility.
Notes: One of the test gratings were sent to Lidaris facility for detailed characterisation of the laser induced damage threshold (LiDT) under vacuum. 50fs, 10Hz pulses of 180 μm diameter were used.

## Slide 10: MLD LiDT Testing (in-house, CLF)
LiDT test performed with Gemini TA2 50 fs, 10 Hz beam.
Catastrophic damage detected with online diagnostic.
1mm beam diameter.
Energy ramp at each target site, which anneals the coating.
100-on-1 LiDT energy ramp up measured >400 mJ / cm2
10,000-on-1 (with annealing). LiDT > 280 mJ / cm2
EPAC 1PW
LiDT
(Catastrophic)
B6
B1….
1mm beam profile on sample
Scatter Diagnostic
Burst1-5
Notes: Add catastrophic image
Separate slide ATA2 test

## Slide 11: Cooled Substrate
Substrate
Two 160 mm x 130 mm ULE 7973 low expansion fused silica substrate with a cooling channel were manufactured.
One was silver coated as mirror and the other sent to PGL to manufacture a cooled gold grating.
Cooled substrate mounting scheme
Leak tested under pressure in air and in vacuum.
Beam pointing instability from water pressure/flow:
  6 μrad @ 0.5 Bar, 12 μrad @ 1 Bar.
Static water pressure dependence on reflected wavefront observed.

## Slide 12: Cooled Mirror Testing
Vacuum
Window
Sample
The water-cooled silver coated mirror substrate was heated with 120W 800nm diode laser beam diameter 2w=50mm, in air and under vacuum.
Water temperature dependence observed.
We overlooked the absorption of the window!
Significant heating and deformation (~250 nm) observed.
Notes: Water turbulence, solutions?

## Slide 13: Grating Substrates
Use low co-efficient of thermal expansion (CTE) glass ceramic to minimise distortion due to thermal loading .
All materials considered have varying grades/classes of materials with improved CTE tolerance:
Zerodur (Schott).
  High bubble content -> polishing problematic.
  Thermal Hysteresis -> CTE variance.
ULE 7973 (Corning).
  Preferred substrate from all grating manufacturers.
  Very long lead times (stopped manufacture).
  ULE 7972 (Corning) possible alternative.
Clear-ceram-Z (Ohara)
  Comparable to Corning ULE and available with relatively short lead time.
Material | Thermal conductivity (W/m.K) | Specific Heat (J/g.C) | Thermal Exp Coeff (ppm or e-6)
Corning 7980 | 1.38 | 0.768 | 0.569
Schott Zerodur | 1.46 | 0.8 | hysteresis
Corning 7973 | 1.31 | 0.767 | 0.03
ClearCeram Z | 1.51-1.52 | 0.777 | 0.015
Notes: >>More introduction thermal loading
>>Slide 7973 vs 7972. and/or overlay CTE graph
Low expansion Glass Ceramics have amorphous and crystalline phases in the material.
Amorphous phase has positive CTE but the crystalline phase has negative CTE.
Control of the ratio of these phases allows them to compensate each other resulting in net zero CTE.
The zero CTE point is usually at 20°C, but can be tailored.
However, each batch will have slight variations so there can be a +/-10°C difference in the zero point depending on grade.
The CTE variance with temperature is in the Ansys model parameters

## Slide 14: Cooled Gold Modelling
Continued thermal modelling is needed to benchmark to experimental results, assess the use of alternative substrates to ULE 7973 and evaluate the impact of structural + thermal deformations on the gratings surfaces.
G2/G3 Thermal deformation.
30W absorbed
  Current modelling confirms 1 Hz uncooled operation will have negligible, ~3 nm, deformation of grating surfaces.
  Revise passive cooling, like use of high emissivity UHV coatings to increase passive radiative cooling effects (80% of heat extraction).
  Optimize active cooling design
Notes: Quote thermal only

## Slide 15: Grating Summary
 | Cooled gold gratings | MLDs | Uncooled gold gratings
Substrate Material | Low availability, ULE 7972 under investigation. | Low availability, ULE 7972 under investigation. | Different options available Identified one option (Clear Ceram Z)
Diffraction efficiency | Good | Require more stable production from manufacture | Good
Design maturity | Require cooling channel design, discussion with substrate manufacture and mount design. | Confirm LiDT. | Performance proved @ 1Hz
Readiness | Cooled grating test required. Not available for commissioning. | Long manufacture time, colour mode damage and longevity require investigation. Not available for commissioning. | Different suppliers available. Available for commissioning
Max rep. rate to specs | 10Hz | 10Hz | 1Hz

## Slide 16: Conclusions
Compressor vacuum chamber on track and tested similar grating mounts.
Manufactures and tested a first cooled substrate with silver coating, gold grating under manufacture.
More investigation is required on thermal load of input window.
MLD grating promising for 10Hz operation, further test and development required.
Low availability of Corning 7973, different substrates under evaluation (Clear Ceram Z and Corning 7972).
Proposing to use uncooled gold grating for test compression and 1Hz commission while developing MLD & cooled gold grating.
Waiting gold cooled grating sample for testing, further development required.
Notes: Footprint G2/G3 full size

## Slide 18: Prototype Cooled Mirror Testing
Vacuum
Window
Sample
A water-cooled 160 mm x 130 mm ULE 7973 silver coated mirror substrate was heated with 120W 800nm diode laser under vacuum.
Stable & leak tested under pressure & under vacuum for many hours without issue.
Testing is necessary to determine viability of cooling scheme under vacuum when scaled to full aperture gratings.
Cooled substrate mounting scheme
Substrate
Notes: Water turbulence, solutions?

## Slide 19: Cooled Mirror Testing - 2
Tested 3 different windows in air using uncooled ULE 7973 mirror:
Corning 7980 20mm thick;
Corning 7979 20mm thick;
Sapphire 2mm thick
Water cooling at T = 21 C and p = 0.5 Bar
Sapphire window lower impact on the wavefront.
Sapphire window was used to test three mirrors under vacuum:
Zerodur, gold coated;
ULE 7973 uncooled, silver coated;
ULE 7973 cooled, silver coated.

## Slide 20: Cooled Mirror Results
Static water pressure dependence on reflected wavefront observed.
Water temperature dependence observed.
  New heating problem found! Significant window heating and deformation (~250 nm) observed. Looking into using sapphire laser windows as alternative to fused silica.
Beam pointing instability from water pressure/flow:
  6 μrad @ 0.5 Bar. 12 μrad @ 1 Bar.
  x8 larger mass of full-sized gratings likely to damp this.
IN PROGRESS
Future:
Results with sapphire vacuum window.
Test substrate (130 x 160 mm) with cooled metallic grating in manufacture.
Notes: Update (image/graphs) on sapphire window?
Future: recoat to gold, also a gold grating coming.
Water pressure effect.
Water turbulence, solutions?

## Slide 21: Grating Substrates
Use low co-efficient of thermal expansion (CTE) glass ceramic to minimise distortion due to thermal loading .
All materials considered have varying grades/classes of materials with improved CTE tolerance:
Region of negative CTE below zero point – heat input will cause contraction
Zero point can vary per batch, which makes modelling accuracy difficult
Zerodur (Schott).
  High bubble content -> polishing problematic.
  Thermal Hysteresis -> CTE variance.
ULE 7973 (Corning).
  Preferred substrate from all grating manufacturers.
  Very long lead times (stopped manufacture).
Clear-ceram-Z (Ohara)
  Comparable to Corning ULE and available with relatively short lead time.
Notes: >>More introduction thermal loading
>>Slide 7973 vs 7972. and/or overlay CTE graph
Low expansion Glass Ceramics have amorphous and crystalline phases in the material.
Amorphous phase has positive CTE but the crystalline phase has negative CTE.
Control of the ratio of these phases allows them to compensate each other resulting in net zero CTE.
The zero CTE point is usually at 20°C, but can be tailored.
However, each batch will have slight variations so there can be a +/-10°C difference in the zero point depending on grade.
The CTE variance with temperature is in the Ansys model parameters

## Slide 22
Pump A
Pump B
EPAC Pump Laser
EPAC Front End
Ti:Sa High Energy Amplifier
Green conversion
Compressor
Beam propagation

## Slide 23: Compressor
Compressor tender closed with no bids – AVS submitted late bid.
Signed-off breadboard and base-plate designs.
Resin base will be applied between floor plate and concrete floor.
Have undertaken vibration modelling to confirm that relative displacements won’t impact on performance.
Rails will be used to install the mounts into the chambers.
VOPPEL grating mounts demonstrating <0.2µRad stability.
Resin Base
Floor Plate
Breadboard
Strengthening
Rib
Loading Rail

## Slide 24: Optic Sag: Structural Modelling
Grooves machined into sides of gratings are used for mounting.
Faces point ±37.24° down/upward -> sag susceptibility.
  300mm square input/output gratings have 3 edge contact points.
  760mm long intermediate gratings have edge 6 contact points.
Further optimisation of mounting locations are planned to minimise structural deformations.
-84nm pk-pk
69nm pk-pk

## Slide 25: Grating Size
Cooled substrate has a maximum size of 550 x 260 mm leading to spatial apodization between 750 to 850 nm.
However this will have minimal impact on the spectral shape of the pulse.
G1
G2
G3
G4

## Slide 26: Gold - Thermal Modelling
Modelling (Ansys) to inform 1 Hz and 10 Hz grating performance.
  Grating surface temperature. Aim: < 50°C.
  Surface deformation. Aim: < 80 nm (structural + thermal).
Passive cooling by radiative emission (~80%).
  Investigating high emissivity UHV coatings.
Development of active cooling solutions by forced convection and conduction ongoing.
Gold Grating, ULE 7973 | G1, G4 (300 x 300mm) |  | G2, G3 (760 x 300mm) | 
 | 1Hz | 10Hz | 1Hz | 10Hz
Thermal Eq. Temp | 33°C | 118°C | 25°C | 59°C
Thermal (pk-pk) | 13nm | 233nm | 3nm | 184nm
Structural (pk-pk) | 69nm |  | 84nm | 
Combined (pk-pk) | 70nm | 280nm | 82nm | 136nm
G2/G3 Thermal deformation.
30W absorbed
G1/G4 Thermal deformation.
30W absorbed
Notes: Quote thermal only

## Slide 27
The periscope after compressor to reduce height to 650mm – for access to optics.
There is only enough space for a single level horizontal motorised translation
BL3 can pass over top of BL1,BL2.
Post - Compressor
Periscope
Diagnostics
Switch-Yard
Switch-Yard
Beam Dump

## Slide 28
Leakage transmitted through a mirror.
OAPs then used to downsize beam to ϕ30mm.
Wedged mirror then used to separate a high energy and low energy mode with 2 beams going into diagnostics suite.
Option for a pick-off mirror to be inserted into beam for sub-aperture diagnostics line.
Diagnostics

## Slide 29: Delivery
EA1
EA2
Laser Areas
Ground Floor
1st Floor
2nd Floor
Laser Areas

## Slide 30: Pre-Compressor CW beam expanders

## Slide 31: IR CW beam expander scheme
Full aperture
LASER
COMPRESSOR ALIGNMENT RETRO
Fl= 2 m Achromatic lens, identical to Output diagnostic lens, also same overall design as VSF lenses with difference surface radii (same diameter and surface thicknesses)
Spatial filter
10 deg
MAKO
ON TO SLIDE IN MIRROR
LASER
LASER
Spatial filter
Fibre combiner?
~750 nm
~850 nm
~800 nm

## Slide 32: Blue beam expander + on shot IR Retro
Ø ~17 mm
LASER
FAST STABILIATION MIRROR
THROUGH MIRROR
ON SHOT RETRO
Spatial filter
10 deg
MAKO
Fl= 2 m Achromatic lens, identical to Output diagnostic lens, also same overall design as VSF lenses with difference surface radii (same diameter and surface thicknesses)
Full aperture
FL=500 mm
FL=150 mm

## Slide 33
MAKO
Edmund Optics 6” parabolic mirror fl =1219.2 mm
32-072-522
4” Beam splitter 0.8° Wedge 90% R
2” 50/50 Beam splitter
20 deg
DUMP
Thorlabs - Position Sensitive Detector (PSD) PDP90A
Pre-Compressor Pointing Overlap and Stabilisation Diagnostic
400 & 900nm
400 & 750-900 nm
Full aperture
MAKO
Camera
TTS 0 deg mirror @800 plane parallel AR 900&400
xx deg tilt
WFS
MAKO
NF
WFS
FF f/40
Filter wheels
0.2% LEAKAGE THOUGH MIRROR
2.7E11 W/cm2 ?
400 & 750-900 nm
750-850 nm
IF

## Slide 34: PSD channel
Note: 70 mm beam

## Slide 35: Far Field channel
Note: 70 mm beam

## Slide 36
Overview
Introduction
  A number of independently mounted optics (in a fixed trajectory) are arranged to direct a low laser beam leakage through a vacuum chamber.
  The highly stable collimated low power laser beam enters at Ø220mm and exits as a collimated beam size of Ø30mm. This requires two of the optics to be parabolic; one is used for beam focussing, the other for beam collimation
  The vacuum chamber and all components must be able to operate at high vacuum level (1 x 10-6 mbar)
  Access to components inside chamber will be from above (chamber will be vented for access)

## Slide 37
Mount 3
Mount 1
Mount 2
Mount 4
Mount 6
Mount 8
Mount 9
Mount 10
Mount 5
Laser beam trajectory and optic mount locations
2000
Beam in
Beam out
Mount 7

## Slide 38
Vacuum chamber and mirrors
Beam in
Beam out

## Slide 39: Suggested Output Diagnostics Layout
SEQUOIA
CM Pairs
Pickoff
Low Energy
High Energy
f=1000 mm
f=-200 mm
f=-200 mm
f=1000 mm
f=100 mm
φ=30 mm
φ=6 mm
φ=30 mm
SSA
Pickoff NF
Spectrometer
f=25 mm
f=250 mm
φ=6 mm
WP
PFT
Polariser
NF
WFS
FF
DF
Filter Wheel
Pickoff FF
FC/LX
SPIDER
f=250 mm
f=1000 mm
f=100 mm
f=100 mm
f=300 mm
f=200 mm
f=200 mm
f=200 mm
φ=3 mm
φ=3 mm
f=200 mm
f=200 mm
f=200 mm
Blue NF
Blue FF
f=1000 mm