## Slide 1
Data Management in EPAC
ISTAC report

## Slide 2: Outline
Overview of the Data Management in EPAC
Update on Data Management System Development and Testing
End-to-End Testing
CT in EPAC
Next steps

## Slide 3: Recap:Top-Level Data Management Architecture
Broker
Instruments (DAQ)
Short-term data store
Direct access
Long-term data store
Data archive
Data analysis
Data access
Fast & extensible Pipelines
Data services
Located in EPAC building
Located in Scientific Computing Building
~100-200TB
Expandable
Being spec’d
Most of these are being prototyped

## Slide 4: Top Level Data flow and control
Data
Control

## Slide 5: Detailed structure of DMS
File writer
Pulse ID generator
Control system interface
DAQ manager
DAQ manager: an intermediate DAQ organizer with a developer interface. Useful for commissioning/test experiments.
You can specify the number of laser, destination folder for the data streams etc.
Developer interface
Devices – scalars
Devices – waveforms
Devices – images
IOC
IOC
IOC
ADKafka
EPICS-Kafka forwarder
Data is recorded using EPICS and sent to Kafka
We have an option of a local storage, but the main storage will be in the Scientific Computing Infrastructure.
Local file storage
Facility Data Pipeline (SCD)
Upload manager
Operations Gateway
DAaaS
Kafka stores all data briefly. Anything connected to Kafka can choose what data it consumes.
Data in Kafka can be accessed through a user interface during this time
Kafka
Short-term data display
DAaaS
Experiment orchestrator
Experimental Orchestrator will provide more advanced data control scans and feedback-based experiments.
Specialised GUIs could be provided for different purposes
GUI
GUI
GUI

## Slide 6: Detailed structure of DMS
DAaaS
Experiment orchestrator
Experimental Orchestrator will provide more advanced data control scans and feedback-based experiments.
Specialised GUIs could be provided for different purposes
GUI
GUI
GUI
Devices – scalars
Devices – waveforms
Devices – images
IOC
IOC
IOC
ADKafka
EPICS-Kafka forwarder
Data is recorded using EPICS and sent to Kafka
We have an option of a local storage, but the main storage will be in the Scientific Computing Infrastructure.
Developer Interface
File writer
Pulse ID generator
Control system interface
DAQ manager
Local file storage
Facility Data Pipeline (SCD)
Upload manager
Operations Gateway
DAaaS
Experimental Orchestrator will provide more advanced data control scans and feedback-based experiments.
Specialised GUIs could be provided for different purposes
Kafka
Short-term data display
Developer interface
Kafka stores all data briefly. Anything connected to Kafka can choose what data it consumes.
Data in Kafka can be accessed through a user interface during this time
DAQ manager: an intermediate DAQ organizer with a developer interface. Useful for commissioning/test experiments.
You can specify the number of laser, destination folder for the data streams etc.

## Slide 7: Outline
Concepts of Data Management in EPAC
Update on Data Management System Development and Testing
End-to-End Testing
CT in EPAC
Next steps

## Slide 8: DAQ: EPICS areaDetector will be the first interface
Widely used in synchrotron and accelerator beamlines (eg. Diamond, ISIS, ESS, ESRF…) and ELI
Basic parameters for all detectors – E.g. exposure time, start acquisition, etc.
Easy to implement new detectors – Single device-driver C++ file to write.
Middle-level plug-ins to add additional capability: Simple analysis, file saving, etc.
  – Device independent, work with all drivers
(An EPICS framework to support 2-D detectors)
areaDetector will be used for almost all diagnostics in EPAC

## Slide 9: DAQ interfaces with the control system
1. Follow a set of instructions provided by DAQ and Experimental Orchestrator*
  e.g. rotate a sample through 180 degrees in 1-degree steps and take data for 1 second at each angle
2. Associate each piece of data with a unique Shot ID
3. Provide plugins to DAQ (EPICS AD)
Collaborating with Diamond and ISIS on this
CLF staff in Diamond on secondment
*Described later
Three main requirements for the control system
Notes: Tine to update the diagrams

## Slide 10: End-to-end data flow
Timestamp from FPGA
EPICS areaDetector
Data Pipeline 1
The DAQ system to send data to live feed or Kafka, along with metadata
Kafka will keep all data in a log. This data buffer means we don't need to write data to files immediately
Experiment: 456
200 laser pulses starting at 1228
Detector2
Mode: 4
Gain: 27 dB
Detector3
Mode: 3
Gain: 13 dB
Data Pipeline 2: Direct File Writing
Data from multiple instruments directly written into NeXus file
Diamond takes this approach for high data-rate detectors (Odin)
EPAC will have this option for certain detectors (eg. Hexitek)

## Slide 11: Progress update
Drivers for most detectors exist already and have been tested successfully
Drivers are developed where built-in modules are not available (eg. Raptor camera driver)
Control System Studio provides the stand-alone interface for display during the commissioning
We are planning to use Blazor for more complex displays that aggregate data from many instruments and provide advanced features (configurable layouts, user-profile preferences, access controls etc.)

## Slide 12: Data Broker Benchmarking
Servers now setup in TA1. Will provide
  Stress test for Kafka
  Stress test for networks
  Testing DAQ modules/AD-Kafka
  Throughput
  Latency
  HDF5 writers
  Local storage
This should be scalable to EPAC
Benchmarking in collaboration with ISIS and Diamond

## Slide 13: Data Broker Benchmarking
Data rate vs Processing speed tests for Kafka servers in TA1
Tests show that we can easily cope with 2GB/s data rates with just 3 servers
This is scalable to higher values but this is good enough for the first few years of EPAC by adding more servers
Diamond has also tested Kafka up to 10Gb/s

## Slide 14: Data Broker Benchmarking
Latency could in principle limit the “real time” nature of data processing
We can get to <100ms level latency at the moment
Latency vs throughput can be tuned further by improving the network speed, installing SSD’s etc. and by adding more servers
This will not be an issue for most of what we want to do in EPAC

## Slide 15: Data access from Kafka
Multiple complementary solutions will be needed for display of live and recent data
Routine live data display will be through EPICS archiver – exploring Grafana (same as what ELI is using) for this.
Developing plugins to access image data from Kafka (ImageJ)
By integrating with ImageJ, users will have access to a wide variety of image analysis tools without needing to write any code.
This plugin can display live data, or it can fetch data from a given timestamp. It can also load data from a given time range into an ImageJ stack.

## Slide 16
A data discovery, visualisation and analysis tool for EPAC operational data
  Diagnostic data from EPAC
  Controls/options when viewing images and traces
  In-built functions and filters
  Plotting functionality - including exporting data and plots
  Advanced search interface
  Coping with larger amounts of data
Low and high-fidelity mock-ups have been produced to facilitate discussion with potential users and guide software development

## Slide 17: Outline
Concepts of Data Management in EPAC
Update on Data Management System Development and Testing
End-to-End Testing
CT in EPAC
Next steps

## Slide 18
End-to-End Testing (integration)

## Slide 19
End-to-End Testing: control system interface

## Slide 20
End-to-End Testing: live display with Kafka

## Slide 21
End-to-End Testing: End-to-End DAQ

## Slide 22: Outline
Overview of the Data Management in EPAC
Update on Data Management System Development and Testing
End-to-End Testing
CT in EPAC
Next steps

## Slide 23: Interactive reconstruction under development
Developed by CCPi/SCD
Interface for two main stages: pre-processing and reconstruction (FBP)
Develop the tools for pre-processing
Agnostic to the reconstruction algorithm
Interface for interactive reconstruction
  Different stages will have different views and interactivity
  Controls include: definition of ROI, voxel size, filter
  Run full & partial reconstructions
  View output data with CILViewer

## Slide 24: Current Status
Pipeline for CT recon with
Handles Nexus & lab-based XCT data files
Processing:
  Beam profile correction
  Transmission to Absorption Conversion
  Centre of Rotation Correction
Reconstruction
GUI
Interactively configure process list
Export of process list for re-running
Interactive data visualisation in each step
DAaaS deployment

## Slide 25: GUI
Process List
User creates their own process list adding any number of pre-processing and recon steps.
Writing out resulting dataset is optional – a big time saver.
Option to save process list to file, allowing it to be run again.
Example of interactively choosing reconstruction volume of interest
Configuration parameters for current step

## Slide 26: CT beamline prototype
Shadowgram with diffuse backlight
Line by line conversion to sinogram
Binary light sinogram
“Visible Hull” reconstruction
3D model reconstruction
Imaging system
Diffuse backlight
Rotational sample stage
Imaging system
Plan is to integrate this with the GUI solutions SCD is developing
Setting up a Computer Tomography test beamline in TA2/TA1
Needs coordination of multiple system components
  Experimental Orchestrator
  Control/Drive System
  DAQ
  Data Management System Elements

## Slide 27: Work in progress
Future Additions
Centre of Rotation Correction
  Manual adjustments
  Dual Slice
Fast low-res reconstruction
Viewer enhancement to show full-size data
Iterative reconstruction
Real-time CT (ReCAST 3D)
Work in Progress
Loading in process lists from files.
Investigating beam profile correction procedures from EPAC and WMG
Improving ease of interaction with the viewer
Development driven also by feedback from wider CT community via CCPi
Workshop in the New Year to discuss specs and capabilities and get feedback

## Slide 28: Outline
Overview of the Data Management in EPAC
Update on Data Management System Development and Testing
End-to-End Testing
CT in EPAC
Next steps

## Slide 29: Experimental orchestrator and user interface for DAQ
Will allow users to do scans/experimental runs in an automated way (i.e. move drives, move sample, adjust diagnostic settings, triggers etc.). This is what makes Diamond DAQ user-friendly
Will allow users to pick and choose diagnostics for acquisition
Allow specific triggering/timing requirements for diagnostics
Visualisation of some data and custom live analysis
Diamond uses GDA – this is going to be replaced by Bluesky. This orchestrate experiments (i.e. move drives, take data, do scans etc.)
We might use a consultant for this work (ex. Diamond)
Data Acquisition System Backend
User interface
View data live
Control instruments
Control data recording
WP9
Data Management System
User interface
View data live
Control instruments
Control data recording
Notes: * Bluesky should be thought of as a toolbox or framework rather than a complete system. It's a set of tools we can use to build a system, and we can use a few of them or all of them. * I don't think there's a standard UI for Bluesky; at least not yet. * Bluesky and GDA go beyond Mirage and DARB: they don't just acquire data, they orchestrate experiments. That is, they can move motors around to do scans, and Bluesky even has some experimental features to have a shared scan "queue" that multiple users can edit. *Bluesky is starting to look very promising. It may significantly reduce the amount of work we need to do, but it won't do everything for us. We probably want our own software developers to work on it, since we can't rely on other facilities producing (and releasing!) exactly what we need.

## Slide 30: Data Pipeline for EPAC – by SCD
  DAaaS
  Analyse data without downloading it
  Share software environments and code
  Data stored online for some time (few months)
  Later transferred to tape archive (long-term)
Data storage
  Provide DOIs to data sets
  Make sure data is searchable
  FAIR data
Data curation and cataloguing tools
  Download data files
  Special bulk data transfer systems
Data access
Data Analysis
SCD is developing a data pipeline for EPAC
Working to design end to end pipeline, accounting for existing tools, services, and expertise in SCD.
Currently doing a gap analysis to enable full programme of work
Existing tools have funding and development plans in place – funded by SCD, IRIS, ALC and EPAC

## Slide 31
Scientist in the facility performing experiment
Scientist analysing their experimental data
Scientist/facility scientist choses which user data to preserve/publish alongside instrument data and edits/amends/adds any additional metadata
Publicly accessible FAIR data
Data Pipeline for EPAC – by SCD

## Slide 32
DAaaS is already in use in our facilities
2021 October
04/10/2021 Gemini Onboard
2021 November
01/11/2021 Artemis Onboard
15/11/2022 DAaaS Introduction Video issued to users
2021 December
12/2021 User group mail set up:
CLF-DAaaS-user-contact@stfc.ac.uk
12/2021 User Feedback meetings with Gemini and Artemis
2022
03/2022 3-month Review meetings with Gemini and Artemis
06/2022 Data Services Group will work on Backup and Archive Solution

## Slide 33: Summary and outlook
Currently developing, prototyping and testing different components for data management in EPAC
Have setup strong collaborations with Diamond, ISIS and Scientific Computing Department – have over 25 people contributing to various elements
A good fraction of DAQ is being prototyped
CCPi/SCD developing a large part of CT solution – CLF will do integration/laser-specific pre-processing. Planning to test these in the CT beamline in Astra
Data storage and curation policies being developed
There is now an opportunity to have joint studentships through ALC
https://www.scd.stfc.ac.uk/Pages/Ada-Lovelace-Centre-Studentships.aspx

## Slide 34: Storing Deleting data may be equally important
Dealing with Commercial-sensitive data (will be working with Diamond on this):
  Identifying commercially sensitive experiments from beginning
  Sensitive experiments get an identifier like in Diamond: IN and SN
  Developing different policies for IN-tagged experiments in terms of storage and access
  Provision to delete data after a stipulated time
  Data upload to client’s servers (eg. Globus)
In discussion with DSTL/MoD regarding MoD data handling

## Slide 35: Overview
Many diagnostics and detectors producing data at high repetition rates
  Current estimates ~ 5 GB/s peak – 10Hz, if we move all data through system
Data transfer may not be very easy
  Data volume/experiment could be significant; will need centralised storage and management.
  Annual data volume could be 1-2 PB at the start (but could be theoretically 10’s of PB, if we chose to save everything),
  Depends on operational modes –we will need to be choosy
Data analysis packages need to be included
  Remote analysis may be necessary because of data volumes
  Not all users will have the capability for specialised data analysis tools (eg. Computer Tomography)
Acquire
Store
Analyse
Archive

## Slide 36: Data doesn’t flow through control system
Low fidelity data will be used for visualisation,
where time is not important.
Modular by design
It sits outside EPICS Channel Access
Multiple layers of areaDetector enables different data treatments

## Slide 37
Design challenges: will Kafka slow things down?
Having Kafka may be a solution for a facility like EPAC with 100’s of diagnostics
However, there may be a performance impact for very high data rates
Diamond tested Kafka up to 10GB/s with 2/3 standard servers and it performed fine
They decided against it only because it needed to access files in between and since Diamond doesn’t have 100’s of diagnostics that keep changing, they didn’t have the benefit of Kafka
For high-data rate processing, we plan to have a Hybrid system where the metadata can be routed through Kafka while the data itself can be written directly to storage
Next steps:
Recruiting a specialist
Benchmarking the system in Astra

## Slide 38: Laser-driven sources: additional complications
  Conical beam
  Radiation intensity, pointing, and beam profile are liable to change from one laser pulse to the next. This may require special pre-processing plugins
  May need flatfield information every shot. This, in principle, can be obtained but need to incorporate into Savu
  Will need special plugins to pre-process images with phase contrast enhancement
  Filters for “special noise patterns” by hard x-rays depositing their energy in a shower across multiple nearby pixels

## Slide 39: Day 2 technical/operational Challenges
Data Management
  Timing System and Time Stamps: How do you identify a pulse? Need a compatible solution with the control system. Planning to use FPGA. Will prototype this
  Designing the system to cope with data rates/volume: Benchmarking planned using existing facilities (eg. TA1): Planning to work with Diamond on this
  Storing Data is Expensive (~0.5M/PB): forming a data archiving policy is important. SCD doing the development
Computer Tomography
  Integration of CT components can be tricky. Need specialised knowledge and effort.
  High-resolution tomographic reconstruction is computer-intensive. Will require dedicated HPC access. Exact solution TBD
  Real-time CT is in R&D stage. Developments ongoing in Diamond and ISIS, which we aim to exploit – with dedicated effort. Recruitment for a CT person underway but very low number of applicants

## Slide 40: Data Storage
Finished file
Transfer to main data store
Store in EPAC building temporarily. 2-4 weeks
Scientific Computing Department

## Slide 41: Digital Lab book
Implemented in ELI
Replaces the “hard-copy” lab books used for experiments
Records all the associated “metadata”
Allows users to perform on-the-spot calculations on the data and save the results
We may want to have a “standardized solution” - makes it easier for the user community

## Slide 42: Data pipeline 2 : Direct File Exporter
Route 1
Route 2
Instrument
Experiment: 456
200 laser pulses starting at 1228
Detector2
Mode: 4
Gain: 27 dB
Detector3
Mode: 3
Gain: 13 dB
Data from multiple instruments directly written into NeXus file
Diamond takes this approach for high data-rate detectors (Odin)
Message
From: Detector3
Timestamp: 1234
Data:
Metadata:
  Mode: 3
  Gain: 13 dB
Data Acquisition software:
EPICS areaDetector
Timestamp from FPGA

## Slide 43: Data pipeline 1 : Data acquisition
Instrument
Data Acquisition software:
EPICS areaDetector
Live display in control rooms
Timestamp from FPGA
Message
From: Detector3
Timestamp: 1234
Data:
Metadata:
  Mode: 3
  Gain: 13 dB
The DAQ system to send data to live feed or Kafka, along with metadata
Kafka will keep all data in a log. This data buffer means we don't need to write data to files immediately
For really high-data rates, Kafka may reduce performance
EPAC will have option to directly store data from high-data rate instruments (eg. Raptor, Hexitech)

## Slide 44: Data Broker – Apache Kafka
Kafka is a platform for processing streams of data
  Widely used in businesses
  Used for scientific data in ISIS and ESS
Services communicate by sending messages to each other
Data can be embedded in messages or saved in another system
Messages retained for some time
Storage capacity can be expanded
Instruments
Data written to files
Data processed live
Any other capabilities

## Slide 45: Dealing with Data
Acquire
Acquire
Store
Acquire
Acquire
Acquire
Option A: Instruments feeding into one data store directly
Quite fast
Direct recording requires dedicated data pipelines per instrument
Architecture can be cumbersome
Significant organisational and scalability issues, especially with changes and future upgrades

## Slide 46: Concept of a Data Broker
Acquire
Acquire
Broker
Acquire
Acquire
Acquire
Store
Option B: Add an intermediate “data broker”
Decoupling data producers from consumers makes it easier to:
Change/expand the data store (including file format)
Add new instruments – much more scalable
Add new data consumers e.g. live processing/display for some data
Keep a buffer of raw data
Monitor the whole process
Capturing data in real-time from event sources in the form of streams of events; storing these event streams; manipulating, processing, and reacting to the event streams in real-time as well as retrospectively; and routing the event streams to different destination technologies as needed

## Slide 47: Automation via script