## Slide 1
How do you make electronics work in the space environment?
Mike Salter
Electronics Development Lead

## Slide 2
About Me
Electronic Engineering
Background in CCD imaging for high-reliability space applications, including:
GOES (NASA)
World Space Observatory (Roscosmos)
PUNCH (NASA)
Now focussed on bringing new Quantum technologies into orbit:
Electronic systems lead on SpeQtre, a QKD demonstration mission.
Electronic development lead for Cold Atom applications.
Image © NASA SDO

## Slide 3
Two Big Questions
What is it about the space environment that limits us flying ground-based electronics?
What are our options for doing something about it?
Image © NASA SDO

## Slide 4
Typical Electronic System
Microprocessor and/or FPGA
Interfaces
Power Management
Memory
Specialist Function ICs
Generic I/O, ADCs, Housekeeping
Image © Raspberry Pi Foundation

## Slide 5
Thermal
Mass
Radiation
Vibration
Vacuum Compatibility
Power
Data Handling
Spacecraft
Design
Considerations
Reliability

## Slide 6
Common component rated temperature ranges:
  Commercial 0°C to +70°C
  Industrial -40°C to +85°C
  Military -55°C to +125°C
Relates to junction temperature, therefore linked to power dissipation and operating environment. Typical spacecraft electronic subsystem temperature range: -20°C to +50°C
Thermal expansion and contraction of PCBs is a key design driver.
Thermal
Image © Alter Technology

## Slide 7
Thermal
Mass
Radiation
Vibration
Vacuum Compatibility
Power
Data Handling
Spacecraft
Design
Considerations
Reliability

## Slide 8
Voids / Delamination
Tin Whiskers
Pure tin finishes common in COTS parts, risk of dendrite growth. Lead-alloy solders widely used in space industry.
Outgassing
Careful selection of materials to avoid outgassing effects, soldermask prohibited in some specifications.
Vacuum Compatibility
Image © NASA, Pinksy/Hester - Raytheon

## Slide 9
Thermal
Mass
Radiation
Vibration
Vacuum Compatibility
Power
Data Handling
Spacecraft
Design
Considerations
Reliability

## Slide 10
Mitigation strategies against failures, resulting from FMEA / FMECA
Design for assembly:
  Component pad dimensions to provide optimal solder joint forming.
  Allowance for staking on higher mass components.
De-rating of components specifications, often in excess of 50%.
PCB trace thicknesses and separations increased.
Via annular rings increased.
ECSS specifications (e.g. ECSS-Q-ST-70-12C Design of Printed Circuit Boards) provide a detailed reference.
Reliability by Design

## Slide 11
Thermal
Mass
Radiation
Vibration
Vacuum Compatibility
Power
Data Handling
Spacecraft
Design
Considerations
Reliability

## Slide 12
Radiation
Ionising radiation poses a big challenge for electronic systems.

## Slide 13
Single Event Upsets
D-Type Flip Flop
(used as type memory storage)
AND Gate
NOT Gate
D
Q
CLK
Ionising radiation can cause “bit-flips” in logic and memory.
Radiation Effects

## Slide 14
Single Event Upset Mitigation – Triple Voting
Majority Voter
Signal A
Signal B
Signal A
Signal B
Signal A
Signal B
Radiation Effects
Preserving long-term memory storage, especially program configuration memories, is a significant challenge.

## Slide 15
Single Event Latch-Up
  Ionising radiation causes a large current to flow between power rails.
  Can be recovered by turning the device off and on again
  Silicon process can be designed to remove latch-up susceptibility
NOT Gate
Radiation Effects

## Slide 16
Two Big Questions
What is it about the space environment that limits us flying ground-based electronics?
What are our options for doing something about it?
Image © NASA SDO

## Slide 17
What’s the mission context?
High Performance
Flagship Science Mission
New Space Constellation
Low Cost
Short Lead Time
Educational CubeSat
Reliability Requirement
Technology Demonstration
High
Medium
Medium
Low

## Slide 18
Radiation-hardened and with rated performance to a specified level.
e.g. Texas Instruments TPS7H4001-SP
      TID = 100-krad(Si) RHA
      SET/SEFI characterized to LET = 75 MeV-cm2/mg
      SEL/SEB/SEGR immune to LET = 75 MeV-cm2/mg
Wafer traceability, quality assurance
Lot acceptance testing to Military or Space Standard
Typically a large price tag, not insignificant minimum order quantity and long lead-time.
Look out for emerging “New Space” products.
“Space-Qualified” Components

## Slide 19
Radiation Performance Testing
Vibration/Thermal performance with destructive physical analysis
Lead surface re-finish
Lot traceability
  Wafer inspections
  Anti-counterfeit measures
Lifetime Testing / Burn-in
“Cautious COTS” enables high-performance devices on high-reliability missions but…
NOT Cheaper, NOT Quicker
(for a single spacecraft!)
Up-screening COTS parts

## Slide 20
What’s the mission context?
High Performance
Flagship Science Mission
New Space Constellation
Low Cost
Short Lead Time
Educational CubeSat
Reliability Requirement
Technology Demonstration
High
Medium
Medium
Low

## Slide 21
Orbit and lifetime has a big impact on radiation and reliability requirements.
At LEO, many groups have success with a buy-and-fly “Carefree COTS” approach.
iPhones, Raspberry Pi’s and many other ground-based systems have worked in-orbit.
Heritage, or use of known parts, can give some confidence but COTS process variation makes it impossible to quantify the risk.
CubeSat providers have a successfully and repeatedly flown a wide-range of COTS-based subsystems, typically developed incrementally over many years.
The High-Risk Approach

## Slide 22
What’s the mission context?
High Performance
Flagship Science Mission
New Space Constellation
Low Cost
Short Lead Time
Educational CubeSat
Reliability Requirement
Technology Demonstration
High
Medium
Medium
Low

## Slide 23
“Clever COTS” - Can you get 80% of the risk reduction, for 20% of the cost?
Deep understanding exact susceptibilities in each part technology, likelihood of occurrence in planned orbit, and impact on instrument operation.
Careful parts selection helps you design out risk, and minimise it elsewhere.
Awareness of outstanding risks allows thorough hierarchy of mitigation strategies, focussed on preventing damage to instrument operation.
Targeted component-level up-screening and testing where needed, focussed on identified risks.
Subsystem / Instrument environmental testing (e.g. proton irradiation) can help gain confidence and verify top-level mitigation strategies, but may give limited insight on where issues occur.
The Tricky Middle Road

## Slide 24
Final Thoughts
Capabilities of small-satellites have increased rapidly, with a huge potential for advanced technology demonstration payloads at a lower cost.
The industry is learning how to best to deliver these type of projects.
Design electronics with a route-to-space in mind.
Image © NASA JPL - MarCO

## Slide 25
Thank you
@RAL_Space_STFC
ralspace.stfc.ac.uk
RAL Space
RAL Space