## Slide 1
ITRF WP3 Radiobiology Synchrotron Study
Mark Johnson | Accelerator Physicist (ASTeC) Office A50 | STFC Daresbury Laboratory | Warrington WA4 4AD
mark.johnson@stfc.ac.uk
Mark Johnson | ITRF Six-Month Review
21/03/2023
1272-pa1-wp3-prs-0002-v0.1-six-month-synchrotron

## Slide 2
Introduction
ITRF WP3 Context
ITRF WP3 aims to compare options based on conventional technologies against the baseline LhARA facility design
This includes the evaluation of a synchrotron, with a injector based on established ion sources and pre-acceleration methods
Currently parameterising a small synchrotron design, adapted from work published by the CERN NIMMS project
At present, we are not considering the synchrotron as a drop-in replacement for the LhARA FFA

## Slide 3
Design Basis
Compact, Room Temperature Synchrotron
Key Requirements:
  Synchrotron is primarily designed for the most likely radiotherapy ions (H+, 4He2+ and 12C6+), without excluding heavier ions in future
  Aim for stored intensities compatible with FLASH regimes, of order 1010 ions per spill
  Machine fits within the circumference of the LhARA FFA (21.86 m) with similar beam energies
  Use accessible, conventional technologies e.g. room temperature magnets

## Slide 4
Examples
CERN NIMMS and ELENA
NIMMS have proposed compact synchrotron designs for 12C6+ and 4He2+ ions [1,2]
Designs target FLASH dose rates, at relatively high energies (430 MeV/u for 12C6+) relevant to clinical treatment
NIMMS designs build on CERN experience with small hadron synchrotrons like ELENA [3]
Slow-cycling synchrotron designs (~1 Hz)
Above: ELENA decelerator at the CERN AD Below: Render of the NIMMS 4He2+ synchrotron design
[1] H.X.Q. Norman et al., Proc. IPAC ‘22, THPOMS028 (2022)
[2] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[3] V. Chohan et al., Extra Low Energy Antiproton Ring (ELENA) and its Transfer Lines – Design Report, CERN-2014-002 (2014)
~5 m

## Slide 5
NIMMS 4He2+ Design
Helium Ion Synchrotron
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] X. Zhang, arXiv:2007.11787 [physics.acc-ph] (2020)
Small (~33 m circumference) synchrotron [1] comprised of three achromat lattice cells [2]
Room-temperature 60° sector dipoles operating up to 1.65 T, enable 4He2+ acceleration to 250 MeV/u
Dispersion-free straights accommodate injection, extraction and RF hardware

## Slide 6
ITRF Synchrotron Design
Scaled NIMMS Layout
Synchrotron (~21.3 m circumference) based on a scaled version of the NIMMS synchrotron design [1]
  1.30 T sector dipole magnets with a small defocusing gradient
  QF1 quadrupoles used for working point adjustment
  QF2 quadrupoles used for dispersion cancellation
Parameter | Value | 
Dipole radius [m] | 1.45 | 
Dipole field [T] | 1.30 | 
Max. Rigidity [T m] | 1.89 | 
Ion Species | H+ | 4He2+, 12C6+
Max. Energy [MeV/u] | 80* | 33.4
Orbital Frequency [MHz] | 5.48 | 3.67
*Limited by assumed RF cavity bandwidth (1.5 – 5.5 MHz) Dipoles can accommodate protons up to 155 MeV
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)

## Slide 7
Machine Footprints
Approximately to Scale
Left: NIMMS 4He2+ synchrotron (33.0 m) Above: LhARA FFA (21.9 m)
Right: ITRF WP3 synchrotron (21.3 m)

## Slide 8
ITRF Synchrotron Design
Optics and Key Parameters
Parameter | Value
QF1 strength [m-2] | 3.23
Maximum βx, βy [m] | 7.20, 9.92
Maximum Dx [m] | 1.98
Betatron Tunes Qx, Qy | 2.33, 0.71
Natural Chromaticities ξx, ξy | -4.36, -5.10
Optimised the lattice using a semi-analytic model to maximise the accessible range of working points
Optics are tuned near a third-order betatron resonance to enable RF knockout beam extraction [1]
[1] R. Taylor et al., J. Phys.: Conf. Ser 2420 012101 (2023)

## Slide 9
ITRF Synchrotron Design
Optics and Key Parameters
Parameter | Value
QF1 strength [m-2] | 3.72
Maximum βx, βy [m] | 8.95, 13.63
Maximum Dx [m] | 1.98
Betatron Tunes Qx, Qy | 2.67, 0.52
Natural Chromaticities ξx, ξy | -6.66, -6.80
Optimised the lattice using a semi-analytic model to maximise the accessible range of working points
Optics are tuned near a third-order betatron resonance to enable RF knockout beam extraction [1]
[1] R. Taylor et al., J. Phys.: Conf. Ser 2420 012101 (2023)
Synchrotron tuning range includes two viable working points

## Slide 10
Beam Injection
Injector Chain
NIMMS propose [1] a conventional injector chain based on CERN Linac 4
  Multiple ECR sources are envisioned, based on the SEEIST [2] injector and commercial Supernanogan source
  RFQ followed by one (two) DTL tanks to inject ions (protons) at 5 MeV/u (10 MeV)
Injection energies are primarily influenced by [3]
  Multi turn injection dynamics
  Space charge tune shift
  Stripping foil efficiency
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] U. Amaldi et al., A Facility for Tumour Therapy and Biomedical Research in South-Eastern Europe, Vol. 2 (2019)
[3] E. Benedetto, CERN-NIMMS-Note-008 (2022)
Above: Commercial Supernanogan ECR source generating up to 2 mA H+ or 200 µA C4+ Below: Schematic layout of NIMMS He synchrotron and injector

## Slide 11
Beam Injection
Multi Turn Injection
Parameter | Values |  | 
 | H+ | 4He2+ | 12C6+
Linac Current [mA] | 2.00 | 1.00 | 0.20
Injection Energy [MeV/u] | 10 | 5 | 5
Orbital Period [µs] | 0.49 | 0.69 | 0.69
Ions after 15 Turns [1010] | 5.51 | 1.94 | 0.13
Space Charge Tune Shift | -0.15 | -0.02 | < 0.01
Ions are accumulated over several turns via MT injection or “phase space painting”.
Injection is typically limited to 15 – 20 turns, ~60% efficiency
Estimate the maximum stored intensity based on the SEEIST injector parameters [1] and Supernanogan ECR source.
Injection is not thought to be space charge limited.
[1] U. Amaldi et al., A Facility for Tumour Therapy and Biomedical Research in South-Eastern Europe, Vol. 2 (2019)

## Slide 12
Beam Injection
Multi Turn Injection
Parameter | Values |  | 
 | H+ | 4He2+ | 12C6+
Linac Current [mA] | 2.00 | 1.00 | 0.20
Injection Energy [MeV/u] | 10 | 5 | 5
Orbital Period [µs] | 0.49 | 0.69 | 0.69
Ions after 15 Turns [1010] | 5.51 | 1.94 | 0.13
Space Charge Tune Shift | -0.15 | -0.02 | < 0.01
[1] U. Amaldi et al., A Facility for Tumour Therapy and Biomedical Research in South-Eastern Europe, Vol. 2 (2019)
Ions are accumulated over several turns via MT injection or “phase space painting”.
Injection is typically limited to 15 – 20 turns, ~60% efficiency
Estimate the maximum stored intensity based on the SEEIST injector parameters [1] and Supernanogan ECR source.
Injection is not thought to be space charge limited.

## Slide 13
Beam Extraction
Work in Progress
Like NIMMS [1], we expect to use slow extraction using RF knockout (RFKO) at the third order resonance.
Extensive simulations have been carried out for the NIMMS and PIMMS (CNAO, MedAustron) designs [1].
Typical extraction timescale of ~100 ms to 1 s
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] R. Taylor et al., J. Phys.: Conf. Ser 2420 012101 (2023)
Figure: Simulation of 104 particles extracted via RFKO over 100 ms [1]

## Slide 14
Conclusions
Thank you for listening
A preliminary synchrotron design for ITRF WP3 has been established
Layout is adapted from well-developed designs proposed by CERN NIMMS
Synchrotron optics, beam energies and intensities are increasingly well defined
Currently assessing beam extraction and corresponding dose rates
ITRF WP3 Contributors:
Hywel Owen (STFC ASTeC)
Karen Kirkby (Univ. Manchester)
Elena Benedetto (CERN and SEEIST)
Mark Johnson | Accelerator Physicist (ASTeC) Office A50 | STFC Daresbury Laboratory | Warrington WA4 4AD
mark.johnson@stfc.ac.uk

## Slide 15
Bonus Slides

## Slide 16
Documentation
Bonus Slide 1
Most synchrotron documentation held on the ITRF TD server \\fed.cclrc.ac.uk\Org\NLab\ASTeC-TDL\Projects\tdl-1272 ITRF\pa1 - CDR\acc - Accelerator
Synchrotron parameter sheet 1272-pa1-acc-para-0001-v0.3-synchrotron-parameters.xlsx
MAD-X lattice file 1272-pa1-acc-code-0001-v0.3-synchrotron-lattice.madx
WP3 documentation \\fed.cclrc.ac.uk\Org\NLab\ASTeC-TDL\Projects\tdl-1272 ITRF\pa1 - CDR\wp3 - Conventional Technology