## Slide 1: Dual Readout Calorimeter
Iacopo Vivarelli
University of Sussex

## Slide 2: Short summary

## Slide 3: Calorimetry (former TF6 of Detector roadmap)
DRD kick-off meeting took place on 12th January.
Work split in 3 + 1 “tracks”:
  Track 1: Sandwich calorimeters with fully embedded electronics (connects with UK work on Calice, FOCAL/DECAL – CMS upgrade?
  Track 2: Liquified Noble Gas calorimeters (not immediately relevant for UK (?)).
  Track 3: Optical calorimeters (connects with UK activities on dual-readout/fibre based R&D)
  Track 4: Alternative or transversal proposals (no connection with UK?)
Request for proposals sent from DRD coordinators with deadline 24th March.

## Slide 4: Track 3 – Optical calorimeters
University of Sussex part of an international proto-collaboration including institutions from Korea, US, Italy for R&D on dual-readout for e+e-colliders.
R&D fully integrated in ECFA process since the beginning (R. Ferrari (Pavia and INFN) is one of the conveners of the DRD).
  DRD presentation about dual-readout
  Test beams performed in 2021 and 2022 (EM-size prototypes). One more planned for 2023 (towards had-size prototype).
  A few recent publications: arXiv:2203.04312, Instruments 2022 6(4), 59, arXiv:2202.01474.
Total funding for activities ~ 4M currency units to INFN/Korea/US for construction of hadronic-size fibre-based prototype + Crystal based dual readout.
Challenges:
  Tens of millions of SiPM readout to be read. Digital SiPM?
  Increase Cherenkov light collection efficiency. Blue/near UV fiber + SiPM?
  Timing to resolve energy deposits at different points in the fiber.
  Develop a calibration system.

## Slide 5: Overview
2021 test beam: EM performance test of capillary tube mechanical structure
  Tested with beam at DESY and CERN
  Characterised in terms of linearity, resolution, granularity
Taken from https://doi.org/10.1088/1748-0221/17/06/P06008
Option with a crystal-based, dual-readout EM section
Superior EM and Had resolution
Suitable for particle flow applications

## Slide 6: Immediate future – hadronic size prototype

## Slide 7: UK contribution to track 3
University of Sussex funded via AIDAInnova, capital equipment and CG.
Current: simulation, performance, test beam analysis, monitoring ands DAQ, optical fibre characterisation, SiPM timing performance measurement.
Mid-term feasible contributions:
  Fibre characterisation for Had-size prototype, monitoring and DAQ.
  Fibre+SiPM calibration system for calorimeter.
  Trasverse to multiple DRDs: Digital SiPM (connection with, e.g., noble liquid caloriemeters, tracking (SciFi) LiquidO, etc.)
Connections that could be explored: crystal work in the US.

## Slide 8: Connections with smaller – mid-term projects
Intersecting with DRD activities: small(er) size physics projects may need calorimeters on the short term:
  E.g. Forward Physics Facility – some experiments see large UK involvement
    For example: FASER2 will need a 1x3x3 m3 high-granularity calorimeter on the timescale of a few years.
  Potential to be able to address “system” issues on a system of a feasible size. Should be integral part of the R&D programme.

## Slide 9: More details

## Slide 10: IDEA (Innovative Detector for Electron-positron Accelerators)
See here for additional information
Magnet and iron return yoke
μRwell
Dual-Readout Calorimeter
Drift Chamber
Vertex Detector
Key points:
  Silicon VTX detector plus ultra-low material drift chamber.
      Minimised multiple scattering for momentum range of interest.
    Thin solenoid in front of the calorimeter.
  Single, dual-readout calorimeter for EM and HAD calorimetry.
    But option to have a crystal, dual-readout EM section.

## Slide 11: Dual readout calorimetry
Non-compensating calorimeters: response to em part different from that to non-em part. h/e < 1.
<fem> energy dependent ⇒ Non-linear calorimeter response to hadrons.
<fem> fluctuations largely determine energy resolution ⇒ sampling the hadronic shower with two calorimeters with different e/h boosts energy resolution.
For a review about dual readout calorimetry, please see S. Lee, M. Livan, R. Wigmans, Rev. Mod. Phys. 90, 025002.

## Slide 12: IDEA full simulation
G4 simulation of IDEA calorimeter:
  For the calorimeter: Cu absorber, 1 mm fibers, 1.5 mm pitch.
130 M fibers channels:
  Excellent angular resolution, lateral shower shape sensitivity (if full granularity is retained).
  No longitudinal segmentation out of the box.
Full simulation including drift chamber and solenoidal magnetic field available
  Already based on edm4hep. Integration with DD4hep ongoing.
  See https://github.com/HEP-FCC/IDEADetectorSIM.

## Slide 13: Full simulation performance in a nutshell
Electrons
Pions
Position precision
(Full granularity readout)
All plots taken from https://arxiv.org/pdf/2203.04312.pdf

## Slide 14: Longitudinal segmentation via timing
Assume to read out full signal from SiPM sampled at 10 GHz.
  Full SiPM response integrated in simulation/digitization output.
FFT of signal yields individual fiber hits and high-precision (< 100 ps) timing.
Unlocks full longitudinal information about energy deposit.
Combined with dual readout information allows in-shower cluster identification.
See S. Kho’s talk at Calor 2022.
truth
reco
S+C view
After clustering

## Slide 15: Bucatini calorimeter
Basic calorimeter unit: one brass capillary tube of 2 mm external diameter hosting a fiber (1 mm diameter).
EM-size prototype (10x10x100 cm3) put on beam (twice) in 2021.
  9 modules, each 16 x 20 capillary tubes.
Readout:
  M0 read with SiPM (one per fiber).
  M1-8 read by 2 PMT each (one for Cherenkov, one for Scintillating fibers).

## Slide 16: TB calibration procedure
SiPM equalisation obtained with multiphoton spectrum plus intercalibration of high and low gain.

## Slide 17: Results (bucatini calorimeter)
After calibration with electrons, linearity within 1% over a wide range of enegies.
Excellent lateral shower shape development measurements.

## Slide 18: Not just bucatini
2022 test beam at SPS - testing different mechanics and readout options (lead by Korean team).
Testing different mechanical options including a 3D printed modules.
First time on beam - data taking was a big success - results to come.

## Slide 19: Dual readout with crystals
LYSO (1 X0 - timing layer) + 2 layers of PWO (1x1 cm2) inside the IDEA solenoid.
Crystals read out by SiPM:
  Dual readout obtained with separation in frequency of Cherenkov light.
High granularity, high energy resolution for the EM section.
Hadron calorimeter unchanged with respect to fiber-only configuration.
Single pion response
Taken from https://doi.org/10.1088/1748-0221/17/06/P06008

## Slide 20: Particle flow
A simple PF algorithm implemented for crystal + fibres calorimeter.
  Track-to-calo match based on difference between expected response and track momentum.
  Further refinement and enhancement possible, but implementation good enough to see potential.
  More complex, machine-learning options for PF being explored as part of AIDAinnova for the fibre calorimeter.
45 GeV jets
45 GeV jets

## Slide 21: Crystal + fibre calorimeter - results
Performance studies done on events with jets for a few different configurations:
  No dual-readout (DRO) no Particle Flow Algorithm (PFA) applied.
  With DRO but no PFA.
  With DRO and PFA.
DRO recovers linearity of the calorimeter response and improves resolution. PFA further boosts resolution.
  4.5% at 50 GeV easily reached.

## Slide 22: The future: prototype with hadronic containment

## Slide 23: A truly international effort
Funding for Dual-readout-connected activities:
  AIDAinnova partially supports activities related to R&D for fiber/optics/SiPM + monitoring + simulation studies for fibre calorimeter.
  Significant (o(1 M) currency units each) from DoE for crystal-DRO, Korea and INFN for fibre calorimeter full containment efforts.

## Slide 24: Summary
IDEA implements a fibre dual-readout calorimeter as default option:
  Good EM energy resolution, excellent lateral shower shape and position determination. Excellent hadronic energy resolution.
    Proof of principle of longitudinal shower shape sensitivity through timing
  EM-size capillary tube (Bucatini) prototype tested on beam in 2021. 3D-printed prototype + full extraction of SiPM signal tested on beam in 2022.
  Toward the development of a fully scalable - hadronic-size prototype (mainly INFN and Korea).
Crystal EM-section promises to deliver excellent EM energy resolution and performance while boosting hadronic performance (via intrinsic longitudinal segmentation and PF).
The international effort for Dual Radout at e+e- colliders is growing:
  Three large grants + AIDAinnova will support the R&D over the next future.
Plenty of ideas and room for further collaboration:
  If you are interested: Subscribe on egroups.cern.ch to idea-dualreadout@cern.ch.

## Slide 25: Backup

## Slide 26: Dual readout calorimeter at work
RD52 (Pb)
Leakage counters
Ancillary detectors

## Slide 28: Particle identification
Compare electron and pion shower shapes (20 GeV)
Consider also Time of arrival of signal to SiPM (fiber propagation and SiPM + electronics time response parametrised in full sim)
Combined performance: ε = 99.5%, fake ~1%

## Slide 29: Tau decay identification

## Slide 30: Single hadron response - linearity
Dual readout signal largely recovers linearity while vastly improving resolution.
20 GeV pions
NIM A 866 (2017) 76

## Slide 31: Shower shape
Single particle shower shape
  Using full implemented granularity
Work in
progress

## Slide 32: How events look like (full granularity)
e- 40 GeV
40 GeV
40 GeV
Di-jet

## Slide 33: Angular resolutions
The use of the single fibre granularity yields the ultimate angular resolution of the calorimeter.
Position obtained as the energy-weighted fibre mean
Fit with
Electrons
Pions

## Slide 34: Calibration with electrons
Light yield chosen according to TB results
After tower equalisation, energy deposited by electrons used as pe/GeV calibration factor
50 GeV electrons
40 GeV electrons - S channel
40 GeV electrons - C channel

## Slide 35: as a photon candle
Using 5M events and clustering opposite calorimeter hemispheres as photons.
Dedicated calibration corrections for impact point on tower
Using tower granularity (estimated use of full granularity further improves mass resolution by 20%)
Combined mass resolution ~ 2 GeV

## Slide 36: Single pion response
Scintillation signal
Cherenkov signal
Uniform response from different hadrons with a single

## Slide 37: Jet response
Studied in di-jet events so far (reconstructed with ee_genkt algorithm in two exclusive jets)
Separately reconstructing S, C and truth-level jets.
Event cleaning: central jets only considered; reject events with muons or neutrinos or poor containment.
Two options considered (with and without 1X0 of additional “tracker” material):
Calo only
+ dedicated calibration
Calo + charged
+ dedicated calibration
(Sum charged component and total energy, then correct for double counting)

## Slide 38: Jet response
Dual readout achieves linearity with a resolution of 30%/√E with constant term ~ 0.5%
Resonances studied with