## Slide 1: Detectors & Physics
Physics with Detectors
Detectors for Physics
Physics of Detectors

## Slide 2
A disclaimer: Today’s talk:
Physics of Detectors ONLY
Detectors for Physics
Physics with Detectors
50 YEARS
Amos 2017

## Slide 3
Radiation Detection Physics @ Weizmann
Very low pressure (mbar) ultra-fast MWPC Heavy-Ion imaging detectors
Single-phase noble-liquid detectors
Dual-phase noble-liquid detectors
From mbar of gas – to – noble liquids
n physics
Dark Matter
Brugger et al. Nature 1989
Search for Strange Matter

## Slide 4: Novel noble-liquid detector concepts Amos Breskin
http://arxiv.org/abs/2203.01774
*
for more details:
https://doi.org/10.1088/1748-0221/17/08/P08002
*

## Slide 5: Why noble-liquid detectors?
Why noble-liquid detectors?
  High density  higher interaction probability;
  High scintillation and ionization yields  VUV photons & Ionization-electrons
  Scalability (Xe cost >>> Ar)
What are the challenges ?
  Rare events  large volumes, high radiopurity & background discrimination, very high sensitivity
How?
  Charge readout (with/without multiplication)
  Light readout (primary scintillation & electroluminescence) with PMTs, SiPMs etc.
HEP
Calorimetry
Nucl Phys
LAr
LXe
LAr

## Slide 6: DM & n physics
DM:
low deposited energy (keV) by nuclear recoils  low detection thresholds
 charge multiplication & efficient scintillation-photon recording
 background-radiation discrimination
Neutrino physics:
High m charge deposits (few 104 e/mm)
 Can operate without charge multiplication
multiplication would ease electronics & lower thresholds

## Slide 7: Single-phase TPC concept
Single-phase
Charge collection
3 wire planes or
Multilayer perforated PCB
PMTs  t0
t1
Charged particles ionize the noble liquid;
~ few 104 e-/mm in LAr
Electrons drift to, and induce charge on anode wires (2D);
Primary-scintillation light provides the e- drift time
 third coordinate;
 3D spatial reconstruction from wire planes;
Charge collection with no multiplication
 good only for large deposited charge
(e.g. neutrino physics)
Largest: ICARUS, DUNE...
(t1 – t0) ve
( In 2 DUNE modules)

## Slide 8
270t
760t
68,000t
170t

## Slide 9: Single-phase: neutrino physics
DUNE: Future 68-Kton LAr
Fermilab Long Baseline Neutrino Experiment
Photo: Inside a single module…
Electro-magnetic shower
Hadronic shower

## Slide 10
Dual-phase TPC concept - DM
The EL-photon readout can be substituted by charge readout: electron avalanche multiplication.
e.g. in: LEM (THGEM).
So far low gain.
PMTs
PMTs
Noble liquid
Vapor
EL-photon readout

## Slide 11
Dual-phase: Dark Matter searches
XENONnt, LUX-ZEPLIN (LZ), PNDA X, DARWIN/G3
8.5t 10t 4t 50t
Future 50-ton LXe
DARWIN/G3
Dark-matter observatory
XENON-LZ-DARWIN (XLZD consortium)
PMTs
PMTs
~3m
XENONnt
@ Grand Sasso

## Slide 12
DARWIN/G3 50t LXe observatory for DM & neutrino physics
Aalbers et al 2023 J. Phys. G: Nucl. Part. Phys. 50 013001
DAWIN/G3
Low background
DARWIN/G3
current
 50t x 20Y

## Slide 13: Why new concepts?
Dual-phase detectors: Problems
Current expected problems with large-volume detectors, affecting resolution & efficiency:
 liquid-gas interface instabilities - spontaneous electron emission, gas gap variations (tilt),
electron extraction efficiency into liquid.
Low energy deposits  need multiplication
Limited avalanche gain in noble gases  electroluminescence multiplication
Single-phase detectors:
Current limit: No multiplication in liquid.
 OK only for large energy deposits.
Stable primary-charges multiplication & efficient detection in both configurations
 lowering detection thresholds (& cost?)
e-
L
G
LXe
Extraction field Eextr
Drift field ED
e-
Electron emission efficiency vs

## Slide 14: Single-phase TPC: novel concepts

## Slide 15: Why single phase?
To overcome liquid-gas interface problems in large dual-phase detectors:
Only single-phase can be “face-to-face” and “horizontal”:
 Half of HV for equal field; avoids effects of sporadic bubbles
“Radial geometry” possible
New concepts: potentially lower detection thresholds
E
NL
sensors
E
E
NL
sensors
sensors

## Slide 16
Pawel Majewski 2006
Idea: A spherical Single-Phase LXe DM detector
CsI
WIMP interaction scintillation photons@ electrons;
Photons + CsI  pe;
e + pe drift to & multiplied on sphere covered with micro-structure charge multipliers.
Multiplication in liquid difficult

## Slide 17: Originally proposed: Liquid Hole-Multipliers LHM in single-phase LXe
A.B. J. Phys. Conf. Ser. 460 (2013) 012020
Simultaneous detection of S1 scintillation UV-photons & S2 ionization electrons by a cascade of CsI-coated perforated electrodes.
Electron multiplication via electroluminescence, EL (+ maybe little charge gain) in the holes.
Optical readout (or maybe charge readout)
Observed large signals!
Arazi 2013 JINST 8 C12004
But: LXe prior art:
Electroluminescence (EL) threshold:
~400 kV/cm - on wires
e-avalanche threshold :
~700 kV/cm on wires Aprile 2014
Conclusion:
EL in gas sporadic bubbles Arazi 2015 JINST 10 P08015
CsI
Similar conclusion by Lightfoot 2009
Electroluminescence from THGEM holes / SiPM in LAr
THGEM*
*Thick Gas
Electron Multiplier

## Slide 18
EXOTICS: A “local dual phase” TPC
The bubble-assisted Liquid Hole Multiplier (LHM)
e- & scintillation-photon induced electroluminescence in a bubble, trapped in liquid under a photocathode-coated perforated electrode
EL

## Slide 19
Precise control of the liquid-gas interface, expected:
better S2 resolution
potentially better S2/S1-based background discrimination
CsI
Creating a local “vapor bubble” underneath a “GEM-like” perforated electrode, immersed within a large noble-liquid volume.
The electrode is coated by CsI photocathode.
BOTH: S2 Electrons and S1-induced S1’ photoelectrons drift from the liquid into the bubble.
ELECTROLUMINESCENCE within the bubble  Energy, 2D localization.
Demonstrated in both LXe & LAr.
Arazi et al., 2015_JINST 10 P08015
Arazi et al., NIM A 845 (2017) 218
Erdal et al., 2019 JINST 14, P01028
Erdal et al., 2018 JINST 13 P12008
Erdal et al., 2019 JINST 14 P11021
Bubble-assisted Liquid Hole Multiplier LHM
Principle: Radiation-induced electroluminescence from a bubble trapped in noble liquid

## Slide 20
Waveform structure
Typical waveform of an alpha-particle event, recorded by a PMT below the bubble
S1: primary light passing through holes
S1’: EL light from bubble, by photoelectrons emitted from the CsI photocathode
S2: EL light from bubble, by ionization electrons from track
Erdal, NIMA 845 (2017) 218
PMT
Light yield, resolution & PDE  hole-electrode geometry
Best reached: ~400 photons /e-/4p

## Slide 21
Energy resolution
S2 ~7,000 ionization electrons/event
S1 ~1,700 photoelectrons/event
Erdal, 2018 JINST 13 P12008
R8520 PMT
Ionization electrons  EL
Scintillation-induced photons
 CsI  EL
BUT: Better resolutions expected  possible e- losses @ interface!
Preliminary studies with micro-CT  interface shape varies with E

## Slide 22
Hamamatsu VUV4 quad-SiPM array
(4 6x6mm2 elements); quartz window
Image of a-particles of ring-shaped 241Am source
LHM reconstruction
Phosphor-imaging plate
~4mm
THGEM holes:
F 0.3 holes, 0.7 spaced
Reconstruction resolution of THGEM holes: ~ 200mm RMS
Erdal 2019 JINST 14 P01028
~7000 electrons/event
LXe

## Slide 23: LHM highlights
CsI
GAS BUBBLE
RESULTS in LXe:
Controlled bubble formation & long-term stability S2 E-resolution: 6% RMS for ~3000 electrons
Light yield: ~400 photons /e-/4p
PDE: <5% ; expecting 15%  potentially higher light yield in a DARWIN LHM-TPC
Localization resolution:
reconstruction: ~ 200mm RMS
LHM/SiPM modules
Potential DARWIN LHM-TPC
Light yield: DARWIN TPC
LHM demonstrated also in LAr.
worse resolutions
(lower photon yields)

## Slide 24: NEW: Single-phase - from wires to microstructures
Robust
Modular
Micro Strip Plates
& more!
cathode
UV
cathode
UV
wires
PMT, SiPM, SPAD etc.
Microstructures
Wires
~50 years of Wires in LXe:
Derenzo PRA 1974
Masuda NIM 1979
Aprile JINST 2014
Brown JINST 2022
MSP LXe: gain 10
Policarpo et al. NIMA 1995
UV transparent plate
Printed anode strips
Examples: here multipliers sense S2-e- ONLY
Scintillation S1-photons recorded by photosensors
S1
S2
S1
S2
Goals: Devise other robust high-gain solutions for detecting both S2-e- & S1-photons
EL
EL+CM
e
e
hn
hn
PMT, SiPM, SPAD etc.
or reflective cathode.
hn
e
- - -
e
hn
shadowing EL
Partial hn attenuation
ST strips
Few mm wires or very high voltage wires sagging, staggering

## Slide 25
SINGLE-PHASE LIQUID-MPGD TPC CONCEPTS
Particle interaction in liquid  ionizing electrons & single-photoelectrons (from a photocathode).
pe & e collected onto fine strip anodes (MSP, MHSP, COBRA...).
Charge multiplication (CM) and electroluminescence (EL), occur at high fields on the thin strips.
EL & CM photons detected by nearby photosensors.
Various configurations discussed for e & e + pe detection.
Building-blocks
MSP
THGEM
GEM
MHSP
COBRA
microstructures
hn
hn
hn

## Slide 26: Single-phase with Micro Strip Plates (MSP): S2 e- only
S2: EL+avalanche on strips. S2 Photons detected through VUV-transparent substrate
S1: photons detected (no amplification) by top and bottom photo-sensors (bottom can be replaced by a reflector)
MSGC
Policarpo, Chepel 1995
x10 electron multiplication in LXe with MSGC;
No EL photons recorded
Or a reflective cathode
MSP formed on VUV-transparent substrate, with few-nm thin Ni or Cr electrodes. (>50% transmission@175nm)  small “shadowing”
L-MSP: MSGC, VCC …
Charges deposited in liquid, undergo EL & small avalanche multiplication at high field, near anode strips.
Photons recorded with nearby photo-sensors
The effective light-emission region depends on the MSP type, & potentials applied to the anode & cathode strips, cathode-backplane, and drift field.

## Slide 27
Microstrip Gas Chamber
Oed 1988
MSPs: MSGC & VCC – field simulations
Weakness: discharges a-c limit HV
Benefit: discharge-less.
The substrate separates strips from cathode plane
Field-line simulations: substrate 0.5mm; anode-strips 5mm; cathode-strips 200mm; drift-gap=1.9mm; strip pitch=1mm. Potentials: Va=5KV; Vc=0; backplane: Vb=0; drift: Vd=-300V.
MSGC
E
a
c
cathode plane
substrate
an. & cath.
strips
drift space
drift cathode
e-
+
anode-strips 5mm
a
c
anode-strips 5mm
Virtual Cathode Chamber
Capeans 1997
a
a
a

## Slide 28
MSGC & VCC: similar results @ Va= 5kV But: in practice, not applicable to MSGC
Simulated E vs distance from anode strip: MSGC vs VCC
E vs Dr
Substrate 0.5mm; anode-strips 5-50mm; cathode-strips 200mm; drift-gap=1.9mm; strip pitch=1mm. Potentials: Va=5KV; Vc=0; backplane: Vb=0; drift: Vd=-300V.
Martinez Lema
Martinez Lema
crossing EL threshold ~ 20mm from strip surface. Avalanche threshold ~10mm from surface. (thresholds: Aprile 2014)
EL: 20mm
CM: 10mm
2.5MV/cm
Dr
anode strip
hn

## Slide 29: Setup
Ω ~ 6 %
T ~ 90%
QE ~ 40%
Qtotal (a ) ~ 1 fC
Y ~ 10 photons/e @ 2.0 kV
(discharge limit)
Much higher gains/yields expected with VCC @ higher Vanode
Microstrip Plate - Preliminary results in LXe
Vα = 2.7 kV
Vgrid = -1.7 kV
Vcath = ground
Vback = -2.0 kV
Martinez Lema, Roy, Chepel, Breskin (2022)
PRELIMINARY
From: Bruno Guerard ILL
1mm
Mesh + α source
grid
Microstrips plate
Back plane
Va
Vgrid
Vback
Vanode
Vcathode
a
1mm
0.4mm
f8mm
S1
S2
Single event
PMT
MSGC
Amos Breskin - Noble-liquid detectors - RAL - April 5, 2023
LXe
Charge gain ~ 4
.
.
.
.
.
.

## Slide 30: Single-phase with cascaded THGEM + MSP  S1 & S2
2-stage TPC with CsI-coated L-THEM + L-MSP;
(here L-VCC with S.T. Cr\Ni strips on VUV- substrate)
S2 e- & S1 UV-pe- collected into L-THGEM holes & efficiently* transferred to the L-VCC.
VUV photons emitted by EL + small avalanche near strips, detected through the substrate, by top photo-sensors.
A fraction of S1 photons – detected by bottom photo-sensors or reflected by a reflective-cathode to the CsI.
Option: top L-THGEM surface can be reflective or WLS-coated ( visible-range photo-sensors, glass substrate).
Experimental Transfer Efficiency of e- and pe- through THGEM holes in LXe.
*
Or a reflective cathode

## Slide 31: Effective quantum efficiency Qeff of CsI in LXe
Expected average QEeff in LXe across the entire surface of an electrode, as a function of voltage across the electrode. They were computed (using COMSOL®) for different perforated electrodes; electric field values: Ed=0.5 kV/cm and Et=-1 kV/cm.
Qeff
https://jinst.sissa.it/jinst/theses/2021_JINST_TH_002.jsp
Erdal 2021
GEM, SC-GEM, THGEM

## Slide 32: Single-phase with single Micro Hole & Strip Plate (MHSP)
A single-phase TPC with (here) a CsI-coated L-MHSP.
Both S2 e- & VUV photoelectrons are collected into the L-MHSP holes, drift to MHSP anode strips.
VUV photons by EL + small avalanche near strips, are detected by the top photo-sensors.
Other fraction of S1 photons - detected by bottom photo-sensors (or reflected.
MHSP: Veloso, Rev Sci. Instr. 71, 2371 (2000)
https://doi.org/10.1063/1.1150623
Current technologies few-mm strips possible
avalanche
CsI
e
hn
hn

## Slide 33: Single-phase with Micro-structured electrode
A single-phase TPC with a Liquid micro-structured THGEM multiplier (L-MS-THGEM) coated with CsI. Both S2 ionization electrons and S1 VUV photoelectrons are collected into the holes, drift through the THGEM, towards the micro-structured top surface.
VUV photons emitted by EL + small avalanche at the vicinity of the “anode tips”, are detected by the top photo-sensors.
Other fraction of S1 photons are detected by bottom photo-sensors (or reflected to CsI)
Hao Lin https://doi.org/10.1039/C3TA11889D
EL+CM

## Slide 34: Can we form large-size patterned electrodes?
ARIADNE LAr TPC with optical readout. 50x50cm2 glass THGEM (GTHGEM)
So far, borofloat 33 glass and fused silica glass electrodes (the latter of higher radio purity) produced by abrasive formation of sub-mm holes.
Electrode surfaces coated by resistive ITO film;
Can be patterned, by laser techniques – e.g. to form COBRA-like patterns.
Lowe et al. Appl. Sci. 2021, 11(20), 9450;
https://doi.org/10.3390/app11209450
Thin anode strips and other metallic patterns currently formed in industry: inkjet & photolithographic techniques. (few-micron thin strips on relatively large areas (up to 24”x 24”) already formed on a variety of substrate materials.
See refs in https://doi.org/10.1088/1748-0221/17/08/P08002

## Slide 35: Novel Dual-Phase TPC Concepts In case Single-Phase ones remain a dream…

## Slide 36
Dual-Phase: Cascaded Liquid Hole Multiplier (LHM) – S1 & S2
https://events.camk.edu.pl/event/47/contributions/377/attachments/126/281/LIDINE-2022%20The%20Bubble-Free%20Liquid%20Hole-Multiplier-v2.pdf
S2 electrons and fraction of S1-induced photoelectrons extracted efficiently in liquid through the holes of a CsI-coated immersed L-THGEM electrode. They traverse the interface inducing electroluminescence (EL) in gas phase, mostly in holes of a second perforated G-THGEM electrode. Readout by nearby photo-sensors. Bottom cathode: reflective, or photosensors underneath.
e- & pe- transfer efficiency through THGEM immersed in LXe
a-induced S1 energy resolution
EL in holes does not depend on interface-gap variations
Martinez Lema et al.
PRELIMINARY:
~350 photons\e\4p
cathode
LXe
interaction
e
hn
hn
SiPM
SiPM
SiPM
SiPM
pe
GXe
S1
S2
photocathode
GEM/THGEM
High QE in LXe
EL
G-THGEM
L-THGEM
LXe: increased QEeff by ~x3.5 compared to vacuum!
QEeff in LXe
~30%@175nm

## Slide 37
Current technologies few-mm strips possible
photocathode
High QE in LXe
cathode
LXe
interaction
e
hn
hn
SiPM
SiPM
SiPM
SiPM
pe
GXe
S1
S2
MHSP
e
High field on strip
EL + CM
Dual-Phase: Cascaded Liquid Hole Multiplier (LHM) R&D - S1 & S2
The multiplier: Perforated electrode with thin strips
EXPECTED: higher field larger photon yield & faster signals
COBRA
MHSP

## Slide 38: A potential cascaded LHM DM TPC
CsI L-THGEM
G-THGEM
LXe
Reflective cathode
High CsI QE
 expected high PDE
Unambiguous detection of amplified single photons
Above dark current
Possible to use SiPM, CMOS-SPAD etc.
Lower detection threshold
Transmitted charges detected in G-THGEM holes:
Interface fluctuations not critical
Faster EL signals
No PMTs
Economic
Radio-purity?
No wasted LXe in buffer region

## Slide 39
Dual-Phase: The Floating Hole Multiplier FHM
Better surface-effects control by separation of the two phases;
The liquid phase and the gas should be in thermal equilibrium (at the interface)
Use “rubust” interface: a perforated electrode FLOATING on the liquid surface  e.g. GEM, THGEM, COBRA, etc
Must control the liquid level precisely to have liquid below and gas above.
THGEM
Let it float !
LXe density 2.9 g/cm3
FR4 density 2.00.2 g/cm3
If copper cladding is not too heavy  THGEM should float on the surface of LXe
Cu-clad FR4 PCB
Liq.-Gas interface
Idea V. Chepel

## Slide 40
proof of FHM principle in LXe: Chepel et al. http://arxiv.org/abs/2301.12990
FHM – S2 e- only
S2 electrons extracted efficiently through the interface within holes of a perforated electrode, floating on the liquid. They traverse the interface (under high fields) inducing EL in gas. Readout by nearby photo-sensors.
e
hn
GEM/THGEM
S2
S2 vs Vextr
a-induced S1 & S2
interface
Reduced interface effects and instabilities
PRELIMINARY:
Y~500 photons\e\4p
LXe
0.4mm thick
With 0.4mm thick electrode floating on LXe,
the holes are rather filled with the liquid.
R&D: Thicker electrode:
 expected higher photon yields.
a-induced S2
Energy resolution

## Slide 41
An optional CsI-coated perforated floating electrode allows for detecting both, a fraction of S1 photons (photoelectrons from CsI) and S2 electrons. Both are collected into the holes and traverse the interface (under high fields) inducing EL in gas. Readout by nearby photo-sensors. Under R&D.
S2
FHM – S1 photons & S2 e-
Future R&D

## Slide 42
Significantly smaller free liquid surface – reduced surface instabilities
High electron extraction probability thanks to high field at the interface
 Result – reduced single-electron noise
Parallelism between the gate and extraction electrodes
No sagging
No need for fine detector levelling and liquid level control
R&D:
Electrode optimization to maximize light emission from holes
Physics of interface
Photosensitive (CsI) FHM
FHM on LAr: need lower density PCB materials
FHM – potential benefits

## Slide 43
Cryogenic charge multipliers with resistive electrodes
Motivation: Charge multiplication in noble gases limited by discharges due to secondary effects to <10 (DUNE)
Goal: Quench harmful discharges by deploying resistive materials in the gas-avalanche multiplier
challenges: find/develop resistive materials of the “right” surface/bulk resistivity at noble-liquid temperature
Vapor phase
Vapor phase
Resistive WELL (RWELL)
Resistive film, e.g. Diamond-Like-Carbon (DLC), on an insulator.
Charges evacuated sideways to ground via resistive layer
Signals are induced on readout anode by charges movement
Resistive-Plate WELL (RPWELL)
resistive plate, e.g. a ceramic material Yttria-Stabilized-Zirconia (YSZ) doped with ferrite oxide (Fe2O3), to readout anode.
Amplified charge travel through the resistive plate to the anode.
THGEM electrode, coupled to readout anode via resistive electrode,
Deposited charges are collected into holes, undergoing avalanche multiplication under VRWELL

## Slide 44
Discharge quenching:
An occasional gas breakdown  very large charge accumulation within holes.
 reduction of the local electric field.
 quenching of discharge energy.
 Prevents damage to electrodes & electronics
A main challenge:
find/develop resistive materials of the “right” surface/bulk resistivity at noble-liquid temperatures (LAr ~87K; LXe ~ 165K).
Resistive FILM: ~ 20GΩ/□
Resistive PLATE: ~ 109-1012Ω·cm
Cryogenic RWELL & RPWELL challenges
Tesi, MPGD2022
https://indico.cern.ch/event/1219224/contributions/5130754/attachments/2566756/4531430/Tesi_MPGD2022.pdf

## Slide 45
Ed=0.5kV/cm
Ed=0.5kV/cm
Ei=5kV/cm
Gain comparison: unquenched THGEM/WELL & RWELL
Quenched
RPWELL
RPWELL
So far, with experiments performed under equal conditions:
RWELL/DLC gain > THGEM (LEM) gain;
RWELL gain > RPWELL gain (but higher quenched-discharges rate
Near zero discharges @ gain < 17
Ar 90K
Quenched
RWELL
WELL
THGEM
G=30
RPWELL
RWELL

## Slide 46
Summary & Outlook
GENERIC R&D
Ideas & concepts for potential improvement of large-volume noble-liquid detectors: DM, neutrino…;
Goal: Effective detection of both, scintillation photons and/or ionization electrons;
Single-phase: various optically-recorded configurations incorporating micro-structured elements;
Dual-phase: Optically-recorded Cascaded (liquid/gas) multipliers, Floating Hole Multipliers, Bubble-assisted Liquid Hole Multipliers – and electrically-recorded Resistive Charge Multipliers;
So far:
Investigations in LXe (with only LHM investigated also in LAr);
Lower PDE and worse E-resolution than expected (electron losses at interface)
Single phase: - Charge & light amplification investigated on MSGC strips in LXe
Preliminary: low due to discharge limits. High amplification expected with VCC plates
Dual phase: - proof of principle for all; ~500 photons/e-/4p
 potential to detect single photons above background with simpler photosensors
- Imaging investigated only in LHM (200mmRMS)
Potential applications: DM, n physics, n/g detection in Nucl. Physics,* Homeland security**…
Many open questions requiring Simulations & exp. R&D (LAr, LXe); R&D on nanostructures, on stability of VUV-photocathodes in noble liquids & on technologies
*Cortesi 2017; **Israelashvili 2017

## Slide 47: Thank you