## Slide 1: 3D stacked technology for HEP
L. Gonella, N. Guerrini
UK Tracker Strategic R&D
Liverpool, 26 June 2023

## Slide 2: What and how
This project proposes to develop a 3D imaging sensor, i.e. a layer with sensor and analogue front-end and a layer with digital processing, connected via 3D vertical stacking technology.
The idea is to arrive at a stitched design through 2 - 3 MPW runs and one engineering run.
  The MPW runs will develop circuit blocks and technology expertise.
  The engineering run would prove the stitched design.
The demonstrator design could target the specification of experiments at e+e- or EIC upgrades, to avoid the extra challenges of high radiation environments.
  Specifications can be discussed further and optimised with the interested UK community.

## Slide 3: Why
Advantages in terms of signal and power distribution for large area sensors.
  With respect to a stitched MAPS sensor technology, the availability of more metal layers would be a significant advantage to route power and signals over large area (up to wafer scale) sensors (cf. challenges of ITS3 wafer scale design).
  A second “digital” layer will also allow the implementation of considerable on-chip processing .
More digital logic density and higher granularity.
Option to use a smaller technology node for the digital layer also available.
  Further increasing the logic density and decreasing the power consumption.

## Slide 4: Further comments
3D stacking is becoming more and more popular for imagers development and as a process is much more mature and reliable.
  The demand is so high that one of TJ four yearly MPWs is for 3D imagers and this figure is likely to increase.
  The HEP community should start to develop expertise with this process.
3D stacking technology distinctive advantages in terms of signal and power distribution will be capable of underpinning larger and faster detectors for x-rays and cryo electron microscopy.
  In particular large sensors for 100keV electron microscopy will benefit from proven and reliable 3D integration.
The close proximity between pixel and progressing/storing electronics is also ideal for large and ultra-fast burst mode imagers, a niche but growing market.

## Slide 5: Resources
Length of the project: 6 years
PhD students
  2 PhD students per year for six years
PDRA/AP: 17
  1 PDRA and 0.5 Ap per year for six years
  2 FTE designers for each MPW, and 4 for the ER
Cash for submissions, £1.3M
  3x £170k for MPW
  1x £800k for ER