## Slide 1: WP3 Mechanics and Cooling
Joel Goldstein & Georg Viehhauser

## Slide 2: Purpose of the WP
Develop technologies and designs to be used in the demonstrator
  Technologies that are advanced, but still have reasonable chance of success
Develop technologies for future trackers
  Activities that go beyond what is standard now, and beyond what designs for near-future experiments (ATLAS, ePIC) can rely on
In principle not limited to a specific silicon sensor technology
For mechanical aspects not limited to a specific flavor (low-mass is a general requirement)
  This includes conductive heat transfer
Main flavor-specific technology is forced convection cooling (gas vs evaporative)
  But even there are some common issues (connections, distributions)
At this point, it is hard to put a price tag on these items
  This depends on the breadth (number of groups) and depth (how far ar our aspirations) of this effort
  The list of activities we will present is a list of possibilities, not necessities
  This will only be clear once groups have indicated their interests
  Providing mechanics and cooling for the demonstrator is a different WP

## Slide 3: Suggested projects I
Low-mass local support geometries and structures
  Structures that maximize moment of inertia and are not joint-dominated
  Shape-optimisation to reduce global and local deformations
  Staves or larger structures (wedges, box channels, cylinders, etc.)
  Structures for bent or inclined modules
Evaporative cooling
  New coolants (N2O, Kr, …) to reduce evaporation temperature (see for example https://indico.cern.ch/event/853861/contributions/4841295/, https://indico.cern.ch/event/1228295/contributions/5394883/)
  Transcritical cycles (https://indico.cern.ch/event/1228295/contributions/5393800/)
Integration of cooling channels in substrate/structure
  Microchannels in Silicon
  Thin-wall cooling pipes co-cured with CF (see ALICE)
  Melting or vaporising pre-forms (e.g. Modified poly(lactic) acid (PLA)) in CF (see https://indico.cern.ch/event/853861/contributions/4867438/)

## Slide 4: Suggested projects II
Additive manufacturing
  Metals (Al or Ti), plastics
  Structural elements (fibrous matrices)
  Components for fluid cooling systems (connections, manifolds, etc.) (https://indico.cern.ch/event/1268355/contributions/5354878/attachments/2629949/4548907/2023-04-17_ITK%20-COOLING-3D-PRINTED-MANIFOLD-INFN-MILANO.pptx)
  Cleaning (https://indico.cern.ch/event/1228295/contributions/5390907/)
  Distributions/ flow guidance for gas cooling
  Printing of fibre-loaded material
  Can we 3D-print a tracker?
Fluid system connection technologies
  Welding/brazing for metallic pipes
  Gluing etc. for ceramics/plastics/silicon
Gas cooling
  Flow design
  Prediction models
  Vibration loads on structures
  Development of instrumentation for local gas flow velocity measurement (MEMS?)
    Either mechanical (vane) or calorimetric (see for example https://www.sciencedirect.com/science/article/pii/S0924424719302559)

## Slide 5: Suggested projects III
Low mass hybrid development
  ??
Robotics Assembly/Disassembly support within structural supports/integration
  Maintenance after irradiation
  Maintenance during operation
  Disassembly after irradiation
Mass production techniques/Robotic assembly and testing
  Says it all
Novel structural materials
  Composites (printable?)
  Ceramics

## Slide 6: Suggested projects IV
Electrical and optical service integration and co-curing
  Co-curing of cables and low-mass tapes
  Co-curing of optical fibres for signals
  Co-curing of optical fibres for stress and displacement measurements/environmental monitoring
Software tools for design and mechanical simulations
  Design and simulation of composite structures
  Simulation of coolant flow (in particular gas cooling)
  Machine learning for structure optimisation/design
    Optimisation of thermal management or mechanical performance, or ultimately both together
    Need inputs for the training