## Slide 1: ITRF WP3 Conventional Technologies
Mark Johnson, Karen Kirkby and Hywel Owen ITRF 12-Month Review
20/09/2023
Mark Johnson | Accelerator Physicist (ASTeC)
Office A50 | STFC Daresbury Laboratory | Warrington WA4 4AD
mark.johnson@stfc.ac.uk
1272-pa1-wp3-prs-0006-v0.1-twelve-month-review

## Slide 2
Introduction
Synchrotron Design
End Stations
Conclusions

## Slide 3: Introduction
ITRF WP3 Context
ITRF WP3 aims to compare options based on conventional technologies against the baseline LhARA facility design
This includes the evaluation of a synchrotron, with an injector based on established ion sources and pre-acceleration methods
Currently parameterising a small synchrotron design, adapted from work published by the CERN NIMMS project
At present, we are not considering the synchrotron as a drop-in replacement for the LhARA FFA

## Slide 4: Design Basis
A Compact, Room Temperature Synchrotron
Key Requirements:
  Synchrotron is primarily designed for the most likely radiotherapy ions (H+, 4He2+ and 12C6+), without excluding heavier ions in future
  Aim for stored intensities compatible with FLASH regimes, of order 1010 ions per spill
  Machine fits within the circumference of the LhARA FFA (21.86 m) with similar beam energies
  Use accessible, conventional technologies e.g. room temperature magnets

## Slide 5: Examples
CERN NIMMS and ELENA
NIMMS have proposed compact synchrotron designs for 12C6+ and 4He2+ ions [1,2]
Designs target FLASH dose rates, at relatively high energies (430 MeV/u for 12C6+) relevant to clinical treatment
NIMMS designs build on CERN experience with small hadron synchrotrons like ELENA [3]
Slow-cycling synchrotron designs (~1 Hz)
Above: ELENA decelerator at the CERN AD Below: Render of the NIMMS 4He2+ synchrotron design
[1] H.X.Q. Norman et al., Proc. IPAC ‘22, THPOMS028 (2022)
[2] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[3] V. Chohan et al., Extra Low Energy Antiproton Ring (ELENA) and its Transfer Lines – Design Report, CERN-2014-002 (2014)

## Slide 6
Introduction
Synchrotron Design
End Stations
Conclusions

## Slide 7: ITRF Synchrotron Design
Overview
Small (~23.88 m circumference) synchrotron based on a scaled version of the NIMMS 4He2+ synchrotron design [1]
† Limited by assumed RF cavity bandwidth (1.5 – 5.5 MHz) Dipoles can accommodate protons up to 155 MeV
Parameter | Value | 
Dipole radius [m] | 1.80 | 
Max. Dipole Field [T] | 1.50 | 
Max. Beam Rigidity [T·m] | 2.70 | 
Ion Species | H+ | 4He2+, 12C6+
Max. Beam Energy [MeV/u] | 105.5† | 83.5
Orbital Frequency [MHz] | 5.50 | 4.97
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] X. Zhang, arXiv:2007.11787 [physics.acc-ph] (2020)
Ring comprised of three achromat lattice cells [2]
Room temperature 1.50 T sector dipoles allow 12C6+ acceleration up to 83.5 MeV/u
Dispersion-free straights accommodate injection, extraction and RF hardware

## Slide 8: ITRF Synchrotron Design
Choice of Beam Energy
Making the synchrotron slightly larger than the LhARA FFA* facilitates higher 12C6+ extraction energies
  Synchrotron: 83.5 MeV/u
  LhARA FFA: 33.4 MeV/u
Higher-energy synchrotron has now been adopted as the baseline WP3 machine design
Extraction energy chosen to provide a maximum irradiation depth of ~20 mm
* Original pre-CDR FFA design, circumference ~21.9 m

## Slide 9: Machine Footprints
Approximately to Scale
Left: ITRF WP3 synchrotron (~23.9 m) Right: LhARA FFA* (~26.7 m)
* FFA design presented to WP1.6 meeting 01/08/2023

## Slide 10: ITRF Synchrotron Design
Beam Optics
The synchrotron design was optimised to maximise the accessible range of working points
Optics are tuned near a third-order resonance (Qx = 2.66) for compatibility with slow, resonant beam extraction [1]
[1] R. Taylor et al., J. Phys.: Conf. Ser 2420 012101 (2023)
Parameter | Value
Optics Functions | 
Max. βx [m] | 8.01
Max. βy [m] | 13.4
Max. Dx [m] | 1.55
Working Point | 
Tune Qx, Qy | 2.66, 0.60
Chromaticity Q’x, Q’y | -3.82, -3.62

## Slide 11: Beam Injection
Injector Chain
NIMMS propose [1] a conventional injector chain based on CERN Linac 4
  Multiple ECR sources are envisioned, based on the SEEIST [2] injector and commercial Supernanogan source
  RFQ followed by one (two) DTL tanks to inject ions (protons) at 5 MeV/u (10 MeV)
Injection energies are primarily influenced by [3]
  Multi turn injection dynamics
  Space charge tune shift
  Stripping foil efficiency
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] U. Amaldi et al., A Facility for Tumour Therapy and Biomedical Research in South-Eastern Europe, Vol. 2 (2019)
[3] E. Benedetto, CERN-NIMMS-Note-008 (2022)
Above: Commercial Supernanogan ECR source generating up to 2 mA H+ or 200 µA C4+ Left: Schematic layout of NIMMS He synchrotron and injector

## Slide 12: Beam Injection
Multi-Turn Injection
Ions are accumulated over several turns via MT injection or “phase space painting”.
Injection is typically limited to 15 – 20 turns, with ~60% efficiency
Estimate the maximum stored intensity based on the SEEIST injector parameters [1] and Supernanogan ECR source.
[1] U. Amaldi et al., A Facility for Tumour Therapy and Biomedical Research in South-Eastern Europe, Vol. 2 (2019)
Parameter | Values |  | 
 | H+ | 4He2+ | 12C6+
Linac Current [mA] | 2.0 | 1.0 | 0.2
Injection Energy [MeV/u] | 10 | 5 | 5
Orbital Period [MHz] | 1.82 | 1.29 | 1.29
Ions after 15 Turns [1010] | 6.19 | 2.18 | 0.15
Max. Space Charge Tune Shift | -0.18 | -0.02 | < 0.01

## Slide 13: Beam Extraction
Particle Tracking Simulations
Like NIMMS [1], we expect to use slow resonant extraction using RF knockout at the third-order resonance
Extensive extraction simulations have been carried out for the CERN PIMMS designs (e.g. CNAO, MedAustron) [2]
Typical extraction timescale of ~100 ms to 1 s
[1] M. Vretenar et al., J. Phys.: Conf. Ser. 2420 012103 (2023)
[2] R. Taylor et al., J. Phys.: Conf. Ser 2420 012101 (2023)
Figure: Normalised beam phase space (a) after excitation of the resonance, and (b) with “extracted” ions at the magnetic septum
Extraction scheme for the WP3 synchrotron is being validated using MAD-X particle tracking:
Locations of extraction hardware
Preliminary specifications for septa
Septum

## Slide 14: Dose Rates
Preliminary Estimates
Indicative dose rates were calculated [1] for a 9 cm3 irradiation volume:
  3 x 3 cm field size
  Depth from 0 – 1 cm
We assume a uniform irradiation using a Spread-Out Bragg Peak (SOBP) approach, and neglect lateral scattering.
Dose rate estimated from the energy deposited during a typical 100 ms slow extraction.
Parameter | Value |  | 
 | H+ | 4He2+ | 12C6+
Ions per Spill [1010] | 5.0 | 2.0 | 0.15
Median Energy [MeV/u] | 23.1 | 23.1 | 42.2
Dose per Spill [Gy] | 20.5 | 32.8 | 13.5
Instantaneous Dose Rate [Gy/s] | 205 | 328 | 135
Average Dose Rate [Gy/s] | 20.5 | 32.8 | 13.5
[1] H.L. Owen et al., Contemporary Physics 55:2, 55-74 (2014)
Equivalent LhARA Calculation
109 protons per pulse 7 ns bunches at 10 Hz
Instantaneous : 6 x 107 Gy/s Average: 4.1 Gy/s

## Slide 15
Introduction
Synchrotron Design
End Stations
Conclusions
Slides from Karen Kirkby

## Slide 16: End Stations
Research Room at The Christie, Manchester
Prof. Ranald Mackay
Dr Helena Kondryn

## Slide 17: End Stations
Research Room at The Christie, Manchester
Research Room End Station
O2: 0.1% - ambient
CO2: 0% - 20%
Temperature: Ambient +4 ºC – 45 ºC
Humidity: Ambient – 100 %
Scanning Area: 20 x 20 cm
6-Axis Robot: 30s between samples
Hotel: 36 samples (54/night)
Automated liquid handling for 96-well plates
Scattered dose to hotel at worst 1.27 mGy/Gy

## Slide 18: New End Station
Working with Don Whitley Scientific
Now fully funded
Second Hotel of Samples Increased throughput
Cooled stage DNA repair FLASH studies
Online microscopy
Utilises same robot
And much more…
New End Station
Existing End Station
New Microscope Fits Here
Can be accessed by robot
Online live imaging

## Slide 19: Conclusions
A baseline synchrotron option for ITRF WP3 has been established, based on designs proposed by CERN NIMMS
The synchrotron achieves a higher 12C6+ extraction energy than the LhARA FFA (83.5 MeV/u)
MAD-X particle tracking simulations are being developed to explore and refine the scheme for slow extraction
Instantaneous dose rates expected to be of order ~100 Gy/s
WP3 REPORT

## Slide 20: Bonus Slides
Mark Johnson | Accelerator Physicist (ASTeC)
Office A50 | STFC Daresbury Laboratory | Warrington WA4 4AD
mark.johnson@stfc.ac.uk

## Slide 21: Christie Research Room
Video
https://www.youtube.com/watch?v=j2QR4PQvaeI