## Slide 1: 3D modelling of FETS-FFA main magnet
Ta-Jen Kuo
Supervisor: Jaroslaw Pasternak, Jean-Baptiste Lagrange
Imperial College London, STFC
10/01/24

## Slide 2
Cross section view of the magnets with coils
5 trim coils (each layer) returning at inner side of magnet and 5 on the outer side
main coil: 100mm x 100mm trim coil: 92.5mm x 10mm
Modified from image produced by Jean-Baptiste Lagrange

## Slide 3
Configuration of doublet magnet (Top view)
F magnet and clamp
D magnet and clamp
Radial clamps
Coils (Red)

## Slide 4
Shape of the trim coil
The circular arc becomes too small if the opening angle is smaller than 2.5 degrees
Hence opening angle of D magnet set to 2.5 degrees

## Slide 5
Opening angles including clamps
Need at least 10 mm margin between each components
Opening angle between F pole and the clamp: 2.13 degrees
F pole: 3.47 degrees
F/D opening angle: 4.03 degrees
D pole: 2.50 degrees
Opening angle between D pole and the clamp: 2.13 degrees
Clamps are 50 mm thick each

## Slide 6
At each radii vary theta and obtain Bz
Separate into negative component (F magnet) and positive component (D magnet)

## Slide 7
Jacobian Matrix
Number 0: Main coil
Number 1-10: Trimcoils with increasing radii
Current optimization
Match maximum Bz of F magnet with the analytic scaling law
Effect of maximum Bz with varying current
GFR ( 3580-4150 mm)

## Slide 8
Coil Number | Current Values (Ampere turn)
0 | 64948.68
10 | 1439.04
9 | 4991.75
8 | 12849.20
7 | 10057.83
6 | 7839.84
5 | 5259.40
4 | 4162.98
3 | 2988.36
2 | 2695.18
1 | 459.00
Current Values in F magnet
Current optimization for F magnet
Central scenario: B0 : -1.344690T, r0 : 4.147222m, k : 7.716500

## Slide 9
Only integrating the negative components for F magnet

## Slide 10
Effect of halving the currents
Each working point may need to be separately optimized

## Slide 11
Spiral angle of the Field
where z is the spiral angle
Looking at directly produces
Results with a lot of noise

## Slide 12
Instead of look at ‘Centre of Mass’ of the Field
Adjusting the pole to correct the spiral
angle of the field?

## Slide 13
Effect of halving the currents
Value of spiral angle changes with the current
Decided not to vary the shape of the pole

## Slide 14
Saturation of the return yoke is along 2T at the thinnest part of the spiral
Top view

## Slide 15
Saturation of the pole is higher than 2.5 T
Bottom view

## Slide 16
Clamp Optimization
Define effective angle , which should be a constant , for F and D separately
(The results were produced before current optimization)

## Slide 17
Focusing on the F magnet for now
Adjusting the clamps improves the results with the magnitude of this correction to be
investigated

## Slide 18
Main coil: 50mm x 200mm Trim coil: 10mm x 92.5 mm
1020mm
430 mm
Gap height 70.5 mm
125 mm
700 mm
700 mm
1 mm margin
between coils and pole
4 trim coils (each layer) returning at inner side of magnet and 6 on the outer side
Wrapping the trim coils at two different height layers can reduce the opening angles
Modified from image produced by Jean-Baptiste Lagrange

## Slide 19
Top view of trim coils in Opera3D
New configuration
Old configuration

## Slide 20
Side view of trim coils in Opera3D
New configuration
Old configuration

## Slide 21
Model in Opera 3D
About 17 mm separation between coils
Of F and D magnet

## Slide 22
New opening angles for the two layers trim coil design
Opening angle between F pole and clamp: 1.2 degrees
F pole: 4.5 degrees
F/D opening angle: 2.25 degrees
D pole: 2.5 degrees
Opening angle between D pole and clamp: 1.2 degrees

## Slide 23
Initial investigation suggests 140,000 Ampere turn required
for main coil

## Slide 24
Further work include:
Simultaneously optimize current for F and D magnet
Adjust clamps to get fringe field extent at each radii as constant
as possible
Produce Enge coefficients for optimized results

## Slide 25
Extra Slides

## Slide 26
To keep the total tune shift within 0.01
• d(k-value) < 0.04
d(spiral angle) < 0.2 degree.
To keep the total tune shift within 0.001
• d(k-value) < 0.004
d(spiral angle) < 0.02 degree.

## Slide 27
Coil Number | Current Values (Ampere turn)
0 | 99298
10 | 12771
9 | 3096
8 | 8697
7 | 11691
6 | 18181
5 | 4399
4 | 4256
3 | 6436
2 | 701
1 | 1407
Current Values in D magnet
Large oscillation in the optimized Bz
Maybe adjust the main coil current first
before starting optimization
Notes: 99298.767827 12771.138507 3096.098208 8697.240151 11691.664170 18181.589041 4399.723572 4256.792730 6436.484317 701.919086 1407.878705 0.12692

## Slide 28
)
Plotting Zeff at different radii

## Slide 29
At the current values optimized for the central scenario, the effective spiral angle of the field seems to be corrected

## Slide 30
However, the effective spiral angle is affected by the current values
Halving all the current values changes the effective spiral angle even with
the pole having a constant spiral angle (30 degrees)

## Slide 31
Focusing on the F magnet for now
Fit a third order polynomial and minus the value at the centre of the GFR
Add the angles to the clamps

## Slide 32
Jacobian Matrix for the k index with the two layer design

## Slide 33
Enge fringe field
For the Simplest case:
Effective Field Boundaries (EFB) chosen at the edge of the pole

## Slide 34
Enge fringe field with higher coefficients
To model the doublet together
+
As two separatable functions of each magnet superpositioned on top of each other

## Slide 35
Enge fringe field fit
Considering only the C1 coefficient
)
(1.221207)
(1.291544)
(1.335177)
C1F = 38.2184742
C1D = 41.3568124
B0 F = -0.79728663 (-0.76257)
B0 D = 0.69796035 (0.65133)

## Slide 36
Enge fringe field fit
Considering up to C3 coefficients