## Slide 1: Report on IPRD23 Siena, Italy 25-29 Sept. 2023 E. Giulio Villani

## Slide 2: Outlook
The IPRD conference
Selected presentations
Summary & conclusions

## Slide 3
SIENA is in Tuscany about 50km south of Florence
An ancient Etruscan settlement, it became Roman colony under the name of Sena Julia
Its importance grew in Middle Ages until became a municipality in 12th century: it flourished in XIV century
Frequent confrontations with neighbouring towns, it was taken over by Florence in 16th century

## Slide 4
Piazza del Campo, that dates back to 14th century, is the heart of the city. The location of the ancient roman forum it boasts 14th century gothic buildings
The horse race (Palio) is held here, 2nd of July and 16th of August
The Duomo, 14th century: one of the best roman-gothic architectural examples.
It hosts works by Nicola Pisano, Donatello, Pinturicchio
An interesting innovative project in A.D. 1300 (floor panels of the Duomo)

## Slide 5
Orto de Pecci (medieval garden)
From the Basilica di San Domenico

## Slide 6
The Seminar is the sixteenth in a series devoted, over a time span of 40 years, to detectors and experiments for high-energy particle physics and astrophysics.
The previous ones were held in San Miniato* (1984, 1986, 1988, 1990, 1993, 1996, 1998) and in Siena (2002, 2004, 2006, 2008, 2010, 2013, 2016, 2019).
The Seminar is focused on advanced technologies in particle physics at collider experiments, and in cosmic ray and astrophysics experiments, including balloon-borne, space-based and ground-based experiments.
The participation of representatives from industry will make it possible to discuss future applications of basic research.
16th Topical Seminar on Innovative Particle and Radiation Detectors (IPRD23)
https://web.bo.infn.it/sminiato/siena23.html
* Around 50 km NE of Siena

## Slide 7
Registered participants: 112
Talks: 111
Registered participants: 129
Talks: 98
MAIN TOPICS
Tracking detectors
Calorimeters
Detectors for X and gamma ray astrophysics
Cosmic ray experiments in space, on the Earth's surface, and underground
Neutrino experiments
Radiation-hard detectors and electronics
Muon-tomography of archaeological and geophysical structures
Detectors for medicine and biology
Large X-ray and muon systems for homeland security control
Simulations and new computing methods, including machine learning techniques
Detectors for environmental controls
Outreach
​ATTENDANCE Attendance will be limited to approximately one hundred and fifty participants.

## Slide 8
Rather diversified range of topics, covering detectors for many applications
Very good technical level of talks and posters
Selected presentations:
  Fast timing , including PPD contribution
  Solar Neutrino
  Muon tomography in archaeology

## Slide 9
Fast timing

## Slide 10: Introduction: Timing for HL-LHC
At the nominal luminosity of the LHC the average number of pp interactions
in a single bunch crossing (pileup) is approximately 23
The planned luminosity upgrade to HL-LHC will increase this number to about 200
The increased spatial pileup line density (number of collisions / unit length along the beam axis) will lead to misidentified tracks
ATLAS simulation of spatial events at HL-LHC with < μ >= 140 pileup
Interaction time of many pp vertexes happening in the same bunch crossing at LHC in the case of ≈50 overlapping events. The vertexes are spaced 10’s of ps apart
Fast timing

## Slide 11: Introduction: Timing for HL-LHC
Track reconstruction becomes particularly critical at high η, when resolution becomes larger than distance between vertices
One solution to suppress the detrimental effect of pileup on reconstruction is to separate vertices in time rather than in space
Simulation of HL-LHC local pileup vertex densities for two values of < μ >= 30 and < μ >= 200 ≃ 1.44 vertices/mm MPV
Resolution of the longitudinal track impact parameter, z0, as a function of η for muons of pT = 1 GeV and pT = 10 GeV using ITk alone
Fast timing

## Slide 12: Introduction: Timing for HL-LHC
The HGTD1 in ATLAS will be placed the gap region between the barrel and the end-cap calorimeter. Two instrumented double-sided layers on two cooling/support disks on each end-cap. Timing sensors used are based on Low Gain Avalanche Detector (LGAD) technology
Position of the HGTD within the ATLAS Detector. Positioned at z = ∓ 3.5 m along the beamline, on both sides of the detector
1 ATLAS Collaboration, Technical Design Report: A High-Granularity Timing Detector 2562 for the ATLAS Phase-II Upgrade, tech. rep. CERN-LHCC-2020-007, CERN, 2020, URL: 2563 https://cds.cern.ch/ record/2719855.
Fast timing

## Slide 13: Teledyne e2v LGAD design
Fast timing
In the LGAD device an additional p+ doped layer (gain layer or GL) is implanted near the pn junction. When depleted the GL creates an electric field high enough to start impact ionization, leading to charge multiplication by a factor G
A standard PIN silicon sensor consists essentially of a pn junction. At depletion it shows an ~ uniform electric field F

## Slide 14: Teledyne e2v LGAD design
Two runs of LGAD fabrication with Teledyne 2ev (Te2v) :
Run I included 1,2, 4 and 2x2 of 1x1 mm2 cells
Size of Run I cells [ um]
Normalized values of GL 11B doping
Fast timing

## Slide 15: Teledyne e2v LGAD design
Second fabrication (Run II) included array of 15 x 15 cells of 1.3 x 1.3 mm2
Size of Run II cells [ um]
Normalized values of GL 11B doping
21 mm
21 mm
Fast timing

## Slide 16: Teledyne e2v LGAD TCAD simulation fabrication process
Full process simulation using Synopsys TCAD to predict doping profiles compared with SIMS measurements
Fast timing

## Slide 17: Teledyne e2v LGAD TCAD simulation Charge collection and gain
during MIP injection
during Laser
injection
Transient simulation to estimate charge collection and gain performed both using Laser (1064 nm) and MIP injection
Gain obtained from ratio of collected charge by LGAD vs. bias compared to charge collected by PIN diode under same biasing conditions
Evidence of gain suppression is observed
Fast timing

## Slide 18: Teledyne e2v LGAD Test setup
COLA board + DUT
IR Laser
Laser drive
Vortex cooler
Infrared Laser (1064 nm -15 ps) charge injection
Gain measured as ratio of collected charges LGAD/PIN
Jitter measured using Split Recombine method at different CFD
Coolers to test irradiated sensors
Fast timing

## Slide 19: Teledyne e2v LGAD test results – Charge collection and Gain
WF2
WF8
WF9
Gain plots using laser injection ~ 0.7 fC
Plot of gain vs. Vbias/Vbv shows similar trend for all flavours tested
TCAD comparison shows good prediction up to ~ 80 %Vbv, lower predicted gain above
T = 21 °C
Fast timing

## Slide 20: Teledyne e2v LGAD test results – timing results
Jitter plots using laser injection ~ 0.7 fC
Minimum jitter ~ 10 ps @ 90-95% of BV using CFD = 25 %
T = 21 °C
Fast timing

## Slide 21: Teledyne e2v LGAD test results – timing results
Timing plot using 90Sr setup
For non-irradiated sensors time resolution of approximately 33 ∓ 4 ps
Fast timing

## Slide 22
Fast timing

## Slide 23
Fast timing

## Slide 24
1
Fast timing

## Slide 25
Fast timing

## Slide 26
Fast timing

## Slide 27
Fast timing

## Slide 28
Fast timing

## Slide 29
Fast timing

## Slide 30
Fast timing

## Slide 31
Fast timing

## Slide 32
Fast timing

## Slide 33
Fast timing

## Slide 34
Fast timing

## Slide 35
Neutrino det

## Slide 36
Neutrino det

## Slide 37
Neutrino det

## Slide 38
Neutrino det

## Slide 39
Neutrino det

## Slide 40
Neutrino det

## Slide 41
Neutrino det

## Slide 42
Neutrino det

## Slide 43
Neutrino det

## Slide 44
Neutrino det

## Slide 45
Neutrino det

## Slide 46
Neutrino det

## Slide 47
Neutrino det

## Slide 48
Neutrino det

## Slide 49
Muon tomography

## Slide 50
First use of muon tomography: L.W. Alvarez et al., Search for Hidden Chambers in the Pyramids, Science 167 (1970) 832.
Muon tomography

## Slide 51
Muon tomography

## Slide 52
Muon tomography

## Slide 53
Muon tomography

## Slide 54
Muon tomography

## Slide 55
Muon tomography

## Slide 56
Muon tomography

## Slide 57
Muon tomography

## Slide 58
Muon tomography

## Slide 59
Muon tomography

## Slide 60
Muon tomography

## Slide 61: Conclusions – IPRD23 Conference
Very good conference, with many interesting talks
Interdisciplinary approach, with detectors for different applications and useful discussions with attendants
Excellent location, with superb catering
Proceedings published in JINST
THANK YOU