## Slide 1: Conceptual development of beamstrahlung photon absorber for FCCee
R. Ximenes, R. Seidenbinder, S. Candido, A. Frasca, A. Lechner, G. Lerner, A. Perillo-Marcone, M. Widorski, M. Calviani (CERN)
C. Carrelli, M. Tarantino (ENEA)
29th October 2024

## Slide 4
Future Circular Collider
e-e+ machine 1st stage
45 GeV  182 GeV, up to 1.4 A current
Ceaveat: we are currently in the feasibility phase, technical choices may change
WORK IN PROGRESS

## Slide 5
Up to 100+ different system will be required (e+ source, collimators, lepton dumps, absorbers etc.)
… and will also include non-conventional systems
A real challenge for BIDs (and other systems)
e.g. 20 MJ with V size of ~20 nm
Beamstrahlung radiation
emitted by an incoming electron in the opposite bunch's collective electromagnetic field at an interaction point

## Slide 6: Beamstrahlung radiation source
M. Boscolo, A. Ciarma, Phys. Rev. Acc. Beams 26, 111002 (2023)
 | Lepton energy | Beam current | Avg. g power | Max g energy
Z0 mode | 45.6 GeV | 1.4 A | 370 kW | ~100 MeV
ttbar mode | 182.5 GeV | 5.4 mA | 80 kW | Few GeV
In case of vertical offsets between beams at the IP, power up to 500-600 kW

## Slide 7
Instantaneous photon fluence exceeding ~1016 g/cm2/s
In order to have reaosnable distance between the machine and the absorber, the latter is placed at about 500 m from the IP
Absorbers require to be relatively large in diameter (>700 mm ⌀)
sx ~4.6 cm
sy ~2.5 cm
sx ~2.2 cm
sy ~2.5 cm

## Slide 8: Considerations & limits of solid absorbers
As a first assumption we considered the use of graphite as absorbing material, capitalizing from the existing CERN’s experience in these types of absorbers
J. Maestre et al. 2021 JINST 16 P11019
A. Francia et al, Phys. Rev. Acc. Beams 27, 043001 (2024)
LHC external beam dump
500-700 MJ, O(10) kW
SPS internal beam dump
±5 MJ, O(300) kW

## Slide 9: Considerations & limits of solid absorbers
Graphite (r=1.2-1.8 g/cm3) is an excellent material due to its robustness and capability for high T operation (& rather good radiation hardness)
Operation in UHV limited to O(1200) °C due to vapor pressure
Higher temperatures only possible under inert gas operation (e.g. (HL)LHC beam dump)
Unfortunately, thermal conductivity is rather poor (50-70 W/m*K), hence material not very adapted for high steady state power deposition for big volumes

## Slide 10: How would a LHC dump solution would perform?
Dump ±700 mm ⌀, L~300/350 cm
Assuming a peripheral cooling, >4000 °C for Z0 operation at 500 kW
  Stresses appears beyond the limit for nominal operation
  Conditions limited by the thermal conductivity of graphitic-material, rather than on external cooling
For the time being, no-go for this option

## Slide 11: What if we go liquid?
We started investigating the option of using pure liquid Pb
  Operational temperature between 400 °C and 480 °C
  Rather insensitive to total power deposited
  No Pb-Bi eutectic system to avoid complex chemistry, requirement to keep temperature under well precise control as well as due to Po production from Bi
  Synergetic with other initiatives at & with CERN
A flowing system of Pb in case of a quasi-CW energy deposition would be a good fit for the requirement of FCCee BS absorber

## Slide 12: Advantages of a liquid Pb absorber (I/II)
Pb is an ”ideal” photon absorber material
Absorption and dissipation of thermal power from the beam is “trivial”
Absence of beam-induced thermo-mechanical stresses
No long-term degradation of dump materials
Dilution of radionuclide inventory within total absorber volume
Flexible waste disposal preparation

## Slide 13: Advantages of a liquid Pb absorber (II/II)
Heat exchanger with coolant medium can be located away from absorber (and could be air)
Known liquid Pb thermo-hydraulics and experience building loops by collaborators
No need for vacuum vessel nor pressure vessel – operation at atmospheric pressure with cover gas
At foreseen operational temperatures, no issue with chemical compatibility, corrosion & erosion on conventional stainless steels (AISI304/316)

## Slide 14: Conceptual implementation of a liquid Pb beamstrahlung absorber
700 mm diameter footprint
Pb collection system
Injection system
Liquid Pb free surface
S. Sorlut
Slide flow oriented at ~8 degrees
Effective free surface Pb thickness of about 30-40 mm, but effective depth seen by photons of >200 mm
Shielding around the dump of 150 cm of Fe
Pb in purified Ar atmosphere at 1 bar(a)

## Slide 15
Conceptual P&ID
Flow rate: up to 350 kg/s
Deposited power: 500 kW
Avg. vel. (dump) : > 1 m/s
Avg. temp. : 400-420 °C (no corrosion)
Piping: DN100/DN300
Material: AISI 304/316
Vertical, mixed axial flow pump
Pressure losses: < 1.5 bar
Main systems:
  Coolant purification system (OCS)
  Cover gas system
  Air cooler
  Filling & drain system
BS dump
Pump & Oxygen control system
Fill & Drain
Air cooler
Cover gas & Oxygen control system

## Slide 16: Integration in the accelerator tunnel
We assume the dump to be located at 500 m from IP, to have sufficient separation between the beamstrahlung line & booster line & as much diluted beam as possible
IP
22 m
500 m

## Slide 17: Considerations on beam windows
Very large diameter (e.g. LHC TDE) means large pressure-induced stresses  tend to favour thick windows, which in turn means high (total) power deposition
Currently favoured with is 20 mm Be for the UHV/Ar window, graphite-based window could be an option for Ar/Ar interface
Windows required to separate the dumps from the UHV environment of FCCee

## Slide 18: Optimization of absorber shape
Current foreseen Pb mass flow is about 300 kg/s
Considering that only the central part is impacted by the beam, further optimisation would reduce the mass flow (hence costs & total activated mass)
Basic slope
S-slope

## Slide 19
Scattered photo electrons and soft photons from the surface of liquid Pb carries a signficant fraction of beam power
Any way out?
O(100 kW) leaking
20% 300 kg/s
80% 300 kg/s
a) Double injection
b) Double slope
Options under study to contain power while keeping mass flow ~300 kg/s

## Slide 20: Conclusions and perspectives
We just started an ambitious program towards the development of the FCCee machine
Beamstrahlung photons absorption is a challenging endeavour, quite new to CERN (and other similar institutions)
Work in progress for the optimization of such system
Liquid Pb is a serious candidate, and a technological development is being planned for the next 5-10 years, aimed at realizing a reduced scale test loop by 2029